## Slide 1: CoBF Signaling Details
Date: 2025-05-29
Authors:
Name | Affiliation | Address | Phone | Email
Sherief Helwa | Qualcomm Inc. |  |  | shelwa@qti.qualcomm.com
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
Duncan Ho |  |  |  | 
Sanket Kalamkar |  |  |  | 
Giovanni Chisci |  |  |  | 

## Slide 2: Introduction
Coordinated BeamForming (CoBF) is one of the features that were agreed on for the 11bn amendment.
In July 2024 meeting, a high-level motion passed defining the CSR and CoBF CAP schemes.
  Motion 29 (MAC):
    Define a multi-AP Coordinated Spatial Reuse at TxOP-level with power control
    Define multi-AP Coordinated Beamforming
    Other multi-AP coordination modes are TBD
Since CoBF relies on the concept of beamnulling, hence requires the availability of CSI at the APs w.r.t. OBSS STAs, CoBF operation is split into two main phases: sounding phase and transmission phase.
Since July 2024, some progress was made on both phases:
  Sounding Phase:
    Some sounding details were approved in D0.1 and D0.2 covering the basic frame sequence and high-level rules for how NDP-based sounding will be used.
    More progress was made in May 2025 covering more details and filling in some gaps. (Added to D0.3)
  Transmission Phase:
    Consensus achieved to have an initial control frame exchange phase between the 2 AP doing the CoBF data transmission.
    The initial control frame exchange phase consists of 3 frames and some of the contents of these frames were agreed on.
However, many MAC-related aspects stay open. Therefore, the goal of this contribution is to discuss CoBF from a MAC perspective and to close on some of the open items related to both the CoBF sounding and transmission phases.

## Slide 3: Sounding Sequence
The following are the sounding sequence variants being discussed which are initiated with an invite/response 2-way handshake and optionally include ICF/ICR frame exchanges to support eMLSR/DPS STAs.
Sequential sounding sequence:
Joint sounding sequence:

## Slide 4: Sounding Order
CoBF sounding is constituted mainly of two cross-BSS sounding portions and optionally two in-BSS sounding portions.
Cross-BSS sounding is essential for each AP to collect the CSI w.r.t. OBSS STAs and do the beam nulling essential for successful CoBF operation.
Optionally, each AP may exploit the chance of having the STAs ready for sounding and collect fresh in-BSS CSI.
If a sounding sequence included both in-BSS and cross-BSS sounding, then it is preferred to do the cross-BSS sounding first.
  This way, the sounding initiating AP doesn’t keep the sounding responding AP hanging while doing in-BSS sounding.
  Additionally, if any error takes place within the in-BSS sounding, it can be redone in a separate TXOP using legacy sounding without any involvement of the other AP.

## Slide 5: Single-TXOP Vs. Multi-TXOP Sounding
Single-TXOP sounding:
  It is more efficient to do the entire sounding sequence in a single TXOP.
  This cuts out some of the overhead such as the APs’ initial handshake as well as medium access delay.
Multi-TXOP sounding:
  The benefit of multi-TXOP sounding is to avoid long sounding sequences and TXOPs.
  Also accounts for the possibility of some clients of the responding AP being unavailable, so it may, in some cases, choose to delay its sounding sequence to a later time (another TXOP).
Generally, there are advantages for both approaches and one option could be better in some scenarios while the other may be better in other scenarios. Therefore, we propose to allow both sequences.

## Slide 6: Frame Details
Sounding Invite:
  The purpose of the Sounding Invite frame is to initiate the sounding sequence with a 2-way handshake to make sure the responding AP is available and ready to participate in the sounding process.
  Some additional information can be exchanged such as indicating whether an ICF/ICR frame exchange will be included in the frame sequence or not.
Sounding Response:
  The Sounding Response frame is part of the initial 2-way handshake.
  The responding AP may indicate in the Sounding Response frame whether it is accepting or rejecting the sounding invitation.
    In case of rejection, it may also indicate the reason for it.
ICF/ICR:
  This ICF/ICR frame exchange is optional and is only essential when eMLSR or DPS STAs are scheduled for sounding within the TXOP.
  This frame exchange makes sure those STAs transition to a state of readiness for further frame exchanges.
Frame choices:
  Since the Sounding Invite/Response is a pure AP-to-AP exchange, then the BSRP NTB (formerly GI3)/M-BA frames are seen to be the simplest and easiest to design for this purpose.
  Both frames will be set to be unicast frames with enough room to include the needed information.

## Slide 7: Transmission Phase
The transmission phase consists of an initial 3-way handshaking between the two APs participating in CoBF followed by the actual data transmission and BA info collection.
During the initial handshaking steps, the APs:
  Share information about their scheduled clients for the other AP to pick the correct CSI and perform signal nulling.
  Agree on all the needed parameters for joint CoBF transmission.
  Provide the needed means for time and frequency synchronization.
CoBF Invite: Sharing AP invites shared AP to the CoBF TXOP and shares scheduled STA(s) information.
CoBF Response: Shared AP accepts/rejects CoBF invitation and shares scheduled STA(s) information.
CoBF Trigger: Acts as a synchronization reference and provide needed parameters for joint Tx.
Similar to the sounding sequence, ICF/ICR exchanges are needed to support eMLSR/DPS STAs.
  When present, they are staggered across the two BSSs (shown next slide)
Finally, Ack info can be solicited using legacy schemes while also being staggered across the two BSSs.

## Slide 8: Extended Timeout Period
Staggered ICF/ICR frame exchanges and Ack info polling across the two BSSs create silent periods w.r.t. the STAs which may cause eMLSR/DPS STAs to switch to listen/LC modes.
  To prevent this behavior, an indication should be given to those STAs in the ICF to use an “Extended Timeout period” before they switch back.
  The duration of the Extended Timeout Period must be longer than the longest silent period in the sequence to ensure no switch back until the sequence is terminated.
  The Extended Timeout Period duration should be indicated in the ICF to tell the STA how long it should wait before initiating a switch back upon inactivity.
  With those proposed changes in the ICF, it will make sense to exclude RTS as a valid ICF for DPS STAs when scheduled in a CoBF sequence.

## Slide 9: CoBF Invite/Response Frames
Frame Choice
  The CoBF Invite/Response frame exchange is similar to the Sounding Invite/Response in terms of some functionalities.
    Both invite frames are used to extend an invitation to participate in a CoBF TXOP.
    Both invite frames should be unicast frames addressing the peer AP.
    Both response frames are used to either accept or reject that invitation.
    Both response frames should be unicast frames sent in non-TB PPDU formats.
    Both frame exchanges may be used to exchange some control information between the 2 APs that is needed for their CoBF operation within the shared TXOP such as the inclusion of ICF/ICR in the sequence.
  Therefore, similar to the Sounding Invite/Response, we propose using the BSRP NTB/M-BA frames for the CoBF Invite/Response.

## Slide 10: Ack Information Polling
In a single BSS operation, an AP may solicit the Ack information, i.e., BA, in different ways, e.g., implicitly or using explicit BAR or MU-BAR frames.
We propose using the same baseline schemes for acknowledgment information polling in the CoBF transmission sequence.
However, one major difference from baseline, is that this acknowledgement information polling steps must be done sequentially between the 2 APs as shown below.
  Note: The first MU-BAR frame for the sharing AP can be substituted with a Basic Trigger frame that is aggregated with the DL PPDU and solicits the BA frame as per baseline.

## Slide 11: Note on CoSR
Due to the high similarity in CoBF and CoSR operation, we propose using the same CoBF transmission frame sequence for CoSR.
  Both schemes involve simultaneous PPDU transmission by 2 APs to their STAs.
  Both need to support eMLSR and DPS STAs.
    CoBF is limited to UHR STAs anyway.
    Similarly, CoSR can be limited to UHR STAs as well.

## Slide 12: Summary
The CoBF Sounding and Transmission sequences are discussed and proposals for the following signaling, and operation details were provided:
  Frame sequence details in terms of the frame sequence structure, frame choices, and some frame contents.
  Sounding details related to cross-BSS and in-BSS sounding order as well as single-TXOP and multi-TXOP sounding.
  eMSLR and DPS operation modes support within the CoBF sequences and how an Extended Timeout Period indication is made to those STAs.
  Ack information polling schemes.
  CoBF similarity with CoSR and the opportunity to simply the schemes by using the same frame sequence.

## Slide 13: SP1
Do you agree to use the following CoBF transmission sequence to support STAs requiring ICF/ICR before data frame exchanges?
  The frame sequence consists of:
    A CoBF Invite/CoBF Response frame exchange between the sharing and shared APs.
    Follows ICF/ICR frame exchanges between the APs and their associated STAs happening sequentially across the two APs; sharing AP then shared AP.
      The presence of the ICF/ICR frame exchange from each AP is conditional on the CoBF PPDU being addressed to one or more STA.
      The presence of the ICF/ICR frame exchange from each AP is indicated in the CoBF Invite/Response frames.
      ICF1-ICR1 are exchanged between the sharing AP and its STAs
      ICF2-ICR2 are exchanged between the shared AP and its STAs
    Finally, a CoBF Trigger frame preceding the data PPDUs sent by the two APs simultaneously.
    Frame sequence for Ack information polling is TBD.
  Whether the CBF-invite and ICF1 can be merged and CBF-response and/or ICF2 can be merged as below is TBD.
  Supporting list: [24/412, 25/879]

## Slide 14: SP2
Do you agree to use the following sequence for acknowledgement information polling from STAs scheduled in a CoBF transmission sequence
  MU-BAR/BA frame exchanges are used by each AP separately, i.e., sequentially.
NOTE1: The first MU-BAR frame (transmitted by the sharing AP) can be replaced with a basic trigger that is aggregated with the DL PPDU as in baseline.
NOTE2: The frame sequence for eliciting simultaneous ACKs from clients of both sharing and shared APs if agreed in PHY is TBD.
  Supporting list: [24/412, 25/879]

## Slide 15: SP3
If an eMLSR non-AP MLD that receives an ICF addressed to one of its affiliated STAs during CoBF sequences and if the affiliated STA responds with an ICR, then the eMLSR non-AP MLD shall follow the eMLSR procedure defined in 35.3.17, except that the STA shall use an extended time-out period prior to switching back upon inactivity:
  The duration of the extended time-out period shall be sufficient to cover any inactivity period within the COBF sequence, e.g. (but not limited to), from the end of the ICR to the beginning of the data PPDU, or from the DL PPDU until the beginning of the MU-BAR frame from the shared AP for STAs associated with the shared AP
  The duration of the extended timeout period(s) is explicitly indicated to the STA in the ICF frame sent by its associated AP.
    Whether there is more than one extended timeout period is TBD
  The signaling and derivation of these timeout periods to the STA are TBD.
  Once the eMLSR STA(s) switch back to listen mode, they start using the default time-out period (aSIFSTime + aSlotTime + aRxPHYStartDelay) in future TXOPs unless otherwise indicated in the ICF.
  This is applicable to CoBF transmission sequence
Supporting list: [24/412, 25/879]

## Slide 16: SP4
For DPS non-AP STA(s) scheduled with CoBF in high capability mode, the same switch-back behavior as for eMLSR with extended time-out period is used
  The RTS frame shall not be used as an ICF for DPS in the CoBF Transmission sequence even when the DPS STA does not have any DPS padding required
NOTE: The RTS frame cannot be modified to include the extended timeout period usage and the extended timeout period duration indications.
Supporting list: [24/412, 25/879]

## Slide 17: SP5
Do you agree that an AP shall use the BSRP GI3 Trigger frame variant for the Sounding Invite frame
  The Sounding Response frame shall be M-BA
  TBD whether there’s another frame variant allowed for the Sounding Invite/Response frame
Supporting list: [24/412, 25/879]

## Slide 18: SP6
Do you agree that an AP shall use the BSRP GI3 Trigger frame variant for the CoBF Invite frame
  The CoBF Response frame shall be M-BA
  TBD whether there’s another frame variant allowed for the CoBF Invite/Response frame
Supporting list: [24/412, 25/879]

## Slide 19: SP7
Do you support that if a CoBF sounding sequence within a TxOP includes Cross-BSS and In-BSS sounding, then the Cross-BSS sounding portion shall come first?
  If In-BSS sounding fails, it can be redone using legacy sounding without any involvement of the other AP.
Supporting list: [24/412, 25/879]

## Slide 20: SP8
Do you agree that an AP MLD that receives an ICR from a STA affiliated with an EMLSR non-AP MLD during CBF data frame exchange does not attempt to transmit to the eMLSR non-AP MLD on another link during the extended time-out periods, per baseline behavior.
Supporting list: [24/412, 25/879]

## Slide 21: SP9
Do you support that any CoBF sounding sequence that includes Cross-BSS CSI collection shall be initiated by a two-way handshake between the two APs participating in the sequence
  The two-way handshake exchange consists of a Sounding Invite frame and a Sounding Response frame.
  The Sounding Invite/Response frame exchange is used to:
    Confirm the availability of both APs for CSI collection.
    TBD for indication whether each AP will include ICF/ICR exchanges with its client or not.
    Further information to be exchanged is TBD.
Supporting list: [24/412, 25/879]

## Slide 22: SP10
Do you support that Co-BF and Co-SR transmission TXOP shall follow the same frame exchange sequence framework?
  Co-SR does not need to support EHT eMLSR non-AP STA
Supporting list: [24/412, 25/879]