## Slide 1: Discussion on DCM of DRU – Follow up
Date: 2025-05-07
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu |  |  |  | 
Ming Gan |  |  |  | 
Shimi Shilo |  |  |  | 

## Slide 2: Background: DRU and Its Power Gain
11bn supports the distributed-tone RU (DRU) for TB PPDU transmissions. The following table shows the transmit power in the regular RU (RRU) case and the DRU case with different distribution bandwidths (DBWs).
How to calculate these power can be found in [1].
RU Size | RRU | DRU (M below indicates the number of tones in each 13 subcarriers (1 MHz)) |  |  | 
 |  | DBW = 20 MHz | DBW = 40 MHz | DBW = 60 MHz | DBW = 80 MHz
26 | 2.08 | 10.14 (M=2) | 13.15 (M=1) | N/A | N/A
52 | 5.09 | 11.39 (M=3) | 13.15 (M=2) | 16.16 (M=1) | 16.16 (M=1)
106 | 8.18 | 11.47 (M=6) | 14.48 (M=3) | 16.24 (M=2) | 16.24 (M=2)
242 | 11.77 | N/A | 14.39 (M=7) | 15.85 (M=5) | 16.82 (M=4)
484 | 14.78 | N/A | N/A | N/A | 17.40 (M=7)
996 | 17.91 | N/A | N/A | N/A | N/A
Table 1 Maximum Transmit Power of RU (dBm)

## Slide 3: Problem of DCM in DRU
In the RRU case, DCM could provide 3 dB gain because of the duplication. However, things become different in the DRU case. Take 106-tone RU using DCM in 20 MHz DBW as an example:
DCM itself achieves 3 dB gain.
Compared with a 52-tone DRU, each subcarrier loses around 3 dB gain.
Compared with a 52-tone DRU, the number of subcarriers are doubled.
Compared with a 52-tone DRU, the transmitted bits are almost the same with the same MCS.
The above means that DCM in DRU may provide worse performance compared with directly using a smaller RU
The DCM provides a similar performance but the subcarriers are doubled.
RU Size | RRU | DRU (DBW = 20 MHz)
52 | 5.09 dBm | 11.39 (M=3, 3 subcarriers per 1 MHz)
106 | 8.18 dBm | 11.47 (M=6, 6 subcarriers per 1 MHz)
Table 2 Maximum Transmit Power of RU

## Slide 4: Disallow UHR-MCS 15 in DRU Transmission
The main issue for the DRU DCM is:
With the increase of the RU size in the same DBW, the power for each subcarrier is reduced, which leads to no gain compared with using a smaller size RU.
To resolve it, we propose to enable DCM crossing two DBWs in [1], or, to disallow the DCM in a DRU transmission.
To simplify the procedure, suggest removing the DCM in the DRU case.

## Slide 5: Summary
The traditional DCM is usually useless in the DRU case. Suggest removing it in the DRU case, or finding some other robust methods for the DRU transmission.
To simplify the procedure, suggest removing the DCM in the DRU case.

## Slide 6
Do you support that UHR-MCS 15 is not allowed in the DRU transmission?
    Y
    N
    A
Straw Poll #1

## Slide 7
[1] Mengshi Hu, et al. Discussion on DCM of DRU, 802.11 DCN 2024/1456r0
References

## Slide 8: Appendix: DCM
Dual carrier modulation (DCM) has been introduced in HE and EHT to enable a more robust transmission of an RU or MRU.
For RU or MRU sizes smaller than or equal to 996 tones, the DCM signal contains an original part and the corresponding duplicated part.
For RU or MRU sizes larger than 996 tones, DCM is performed on the segment parser output for each 80 MHz frequency subblock.
Fig. 1 DCM in the case of RU or MRU sizes ≤ 996
Fig. 2 DCM in the case of RU or MRU sizes ＞ 996 (e.g. 160 MHz)
NOTE 1: is the original part, and is the duplicated part.
NOTE 2: The subscripts and indicate the lower and upper parts, respectively.