## Slide 1: Remaining Issue for NPCA
Date: 2025-05-02
Authors:

## Slide 2: Background
In [1], when an OBSS PPDU(/frame) is detected on primary channel, NPCA STA may switch to NPCA primary channel and exchange DL/UL frame on the NPCA primary channel during a time period for the OBSS activity
  Based on several switching conditions and the corresponding switching time & switching delay
  This will increase the TX opportunities and reduce the delay of latency traffic
  NPCA STA needs to finish transmitting frame on NPCA primary channel within a duration for the OBSS activity on the primary channel
Generally, NPCA STA need to return to primary channel from NPCA primary channel before the end of the OBSS activity on the primary channel

## Slide 3: Remaining Issue
According to several previous contributions, AP and non-AP STA may have different views on channel idle/busy
  AP may not receive OBSS frame while the non-AP STA receives the OBSS frame (or vice versa).
  Then the non-AP STA can switch to NPCA primary channel while AP is still on PCH
In this case, if AP transmits data frame to the non-AP STA on primary channel, the STA can not receive data frame
  Note that AP’s power is usually stronger than non-AP STA’s power. The non-AP STA may receive data frame if it’s on the primary channel although the OBSS NAV of the non-AP STA is non-zero value or there is OBSS interference
This will increase the AP’s CW by invoking exponential backoff and retry count unnecessarily. It will finally degrade the WLAN performance

## Slide 4: Early switching back operation of non-AP STA
When NPCA non-AP STA upon switching to NPCA primary channel can guarantee that AP is on the primary channel, there is no reason for the NPCA non-AP STA to remain still on NPCA primary channel
NPCA non-AP STA on NPCA primary channel switches back to primary channel when the NPCA non-AP STA receives, on NPCA primary channel from the AP, a PPDU occupying the primary channel

## Slide 5: Early switching back operation of AP
NPCA AP on NPCA primary channel switches back to primary channel when the NPCA AP receives PPDUs, from NPCA non-AP STAs on NPCA primary channel, occupying the primary channel
AP may perform this operation when the OBSS interference is weak

## Slide 6: Conclusion
It would be better for NPCA STA (AP) on NPCA primary channel to switch back to primary channel immediately when NPCA STA detects that a peer NPCA STA (AP or non-AP STA) is on primary channel
For example, NPCA STA can determine that the peer NPCA STA is on primary channel when the NPCA STA receives a PPDU occupying the primary channel from the peer NPCA STA

## Slide 7: References
[1] TGbn D0.2

## Slide 8: Straw Poll 1
Do you agree the following text?
  NPCA non-AP STA shall switch back from NPCA primary channel to primary channel immediately when it receives a PPDU occupying the primary channel from an NPCA AP that the NPCA non-AP STA is associated with

## Slide 9: Straw Poll 2
Do you agree the following text?
  NPCA AP shall switch back from NPCA primary channel to primary channel immediately when it receives a PPDU occupying the primary channel from all NPCA non-AP STAs that are associated with the NPCA AP and enables NPCA mode/operation