## Slide 1: EBCS UL Privacy Enhancement
Date: 2025-05-13
Authors:

## Slide 2: Abstract
This presentation is a proposal to add enhanced privacy to EBCS UL transmitter.
Although it is related to privacy, EBCS is independent from the existing TGbi draft.
I’m not sure whether TGbi is the correct group or not.

## Slide 3: CID 903
Comment
EBCS UL has potential risk of third party tracking.
Proposed Change
If possible, the commenter would like to make a proposal presentation in May meeting.

## Slide 4: EBCS UL
EBCS UL is used for data transmission from a non-AP STA to APs.
  Sensor
  RFID
  …
EBCS UL uses EBCS UL frame which is not encrypted.
AP
Non-AP
STA
AP
EBCS UL frame

## Slide 5: EBCS UL frame
Source MAC address is not important for EBCS UL.
  It can be randomly changed for each frame.
The following fields have potential risk of third-party tracking.
  Destination URI
  HLP Payload Container
  STA Certificate Container
  Frame Count

## Slide 6: Proposed Solution
AP distributes its own certificate by EBCS Info frame.
  EBCS Info frame transmission is less frequent than Beacon frame.
Non-AP STA verifies the AP’s certificate by pre-installed CA’s public key.
Non-AP STA encrypt the contents of EBCS UL frame by using the public key that is contained in the received AP certificate.
Non-AP STA transmits the encrypted EBCS UL frame with randomized MAC address.
  Source MAC address is not important for EBCS UL.
  Non-AP STA may change source MAC address for each EBCS UL frame.
AP decrypts EBCS UL frame by its own private key.
AP processes EBCS UL frame as in existing specification.
Note: This modification makes multiple AP reception unavailable.
AP
Non-AP
STA
AP’s certificate in EBCS Info frame
Verify AP’s certificate by CA’s public key
Encrypt contents of
EBCS UL frame by AP’s public key
Encrypted EBCS UL frame with randomized MAC address
Encrypt
Decrypt EBCS UL frame by AP’s private key
Process EBCS UL frame as in existing specification

## Slide 7: Straw poll
Do you prefer to add the EBCS UL enhanced privacy to TGbi draft?
Yes:
No:
Abstain: