## Slide 1: Field measurements of EDCA characteristics
Date: 2025-05-13
Authors:
May 2025
Notes: September 2012

## Slide 2: Abstract
Measurements of EDCA Access Category tags applied to packets from a variety of applications
Project reports from two students at University of Colorado - Boulder in WLAN class, Spring 2025
May 2025
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3
Overview
With the current focus on latency and reliability, we wish to assess whether applications are using current priority levels (Access Categories in EDCA)
  AC_VO (AC3) - Voice
  AC_VI (AC2) - Video
  AC_BE (AC1) - Best Effort
  AC_BK (AC0) - Background
If applications are not using appropriate AC tags, data packets may suffer increased latency and poor reliability
Two students (Ben & Jimmy) made measurements of various applications using Wireshark to identify AC tags
Thanks to Ben (benjamin.nowotny@colorado.edu ) and Jimmy (jimmy.nolan@colorado.edu ) for permission to present their results
May 2025
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 3

## Slide 4: Project #1: Ben Nowatny
Android phone running apps
Kali Linux on PC for packet capture and Wireshark analysis

## Slide 5: YouTube
YouTube video packets were all Best Effort
Background packets appear to be Android updates
Voice packets were ARP exchanges

## Slide 6: Google Phone
Majority of packets were AC3 (Voice) as expected
Best Effort packets appear to be management tasks

## Slide 7: Zoom Teleconference
Zoom teleconference with both audio and video
Surprisingly, essentially all traffic was Best Effort

## Slide 8: Application download from Play Store
Downloading a typical app from the Google Play Store
  Best Effort as expected

## Slide 9: Video Game update and asset download
PUBG: Battlegrounds: downloading new assets and setting up an update.
PUBG: Battlegrounds (referred to as PBUG Mobile) is a live multiplayer shooting game

## Slide 10: Network Based Video Game
Packet traffic for an online game of PUBG Mobile
  Includes gameplay data and voice
  All traffic appears to be Best Effort

## Slide 11: Project #2: Jimmy Nolan
Setup
Linux Mint PC with Alfa AWUS036ACS adapter for packet capture and Wireshark analysis
Monitor mode in channel 11 (using software from github)
Tested against two different laptops, iPhone 11 SE and Chromecast

## Slide 12: Remote Desktop over VPN

## Slide 13: Wi-Fi calling

## Slide 14: Discord (Voice) with YouTube

## Slide 15: Casting HBO from iPhone vis Chromecast

## Slide 16: QoS Null Function Packets when using Chromecast
Received a Wi-Fi voice call toward the end of the recording session

## Slide 17: AIFSN Analysis
Discord + YouTube

## Slide 18: Conclusion
Wi-Fi calling applications seem to be using AC3 (AC_VO) as expected
Zoom Teleconference used AC1 (AC_BE)
  Need to check Teams, Webex, GoToMeeting, Facetime, Facebook Messenger, WhatsApp
  Unclear where AC tags are or are not originating from: app? OS? AP? Driver?
Network based videogame used AC1 (AC_BE)
  Would have expected games needing low latency to use AC3 or AC2
  Need to test other games
Chromecast of video stream was AC1 (AC_BE)
Initial tests indicate Access Points seem to follow AIFSN rules
Suggestions for next semester?
Send email to jim.lansford@ieee.org or jim.lansford@colorado.edu