## Slide 1: Multiple TXOP Support
Date: 2025-04-30
Authors:

## Slide 2: Recap: AMP Information Exchange
The information exchange between one AMP reader and one AMP tag may not be able to be finished in one TXOP, e.g. when security, write information to a tag or additional information other than EPC is required in the information exchange.
Multiple neighbor AMP tags may have the same value of their device ID.
Multiple neighbor AMP readers may exist.
  When one reader’s read/write operation is not finished with tag 1, another neighbor reader may start the read/write operation with tag 2 that has the same device ID with tag 1.
Some AMP tags may not be able to maintain complex information between the TXOPs, e.g. only one bit can be maintained through the TXOPs in the backscatter tags.
Before an AMP reader finishes it information exchange with an AMP tag through one or multiple TXOPs, the AMP reader doesn’t start its information exchange with another AMP tag.

## Slide 3: Issue 1: Multiple AMP Readers Performing Frame Exchanges with Tags Having Same ID
Reader 1 Polling Tag
Tag1 with ID N
Responding with EPC
TXOP 1
Reader 2 Polling Tag
Tag 2with ID N
Responding with EPC
TXOP 2
TXOP 3
Reader 2 writing
info to Tag2
Tag 1/2 with ID N
Responding with EPC

## Slide 4: Tag Identification Flag for Multiple TXOPs
Each AMP tag has a flag called Tag Identification Flag (EPC Sent flag).
Each time a broadcast Trigger is received by an AMP tag with its Tag Identification Flag to 1, the tag sets its Tag Identification Flag to 0.
Ext End may be used by the reader to a tag for the tag to set its Tag Identification Flag to 0.
In the first TXOP performing the information exchange with an AMP TAG, the AMP reader acquire the tag’s ID.
  The tag sets its Tag Identification Flag to 1.
An AMP tag with Tag Identification Flag equal to 1 receives a unicast Trigger/Write addressed to it will send the response/Ack.
An AMP tag with Tag Identification Flag equal to 0 receives a unicast Trigger addressed to it will not send the response.
  This may happen since two tags have the same STA ID (CRC code).
An AMP reader will execute the following
  If the following are true
    the AMP reader detects a 11bp PPDU,
    the AMP reader is trying to continue the information exchanges with an AMP tag from which it acquires the EPC.
  Then, the AMP reader will stop the further frame exchanges with AMP tag.

## Slide 5: Information Exchange Example 1
Tag Identification Flag is not used when a single TXOP is enough for the information exchange.
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
(Data(EPC))
EPC
(Data(Query))
Data((EPC))
11bp PPDU
11 PPDU
11 PHY
Header
TXOP
Query
Receiving broadcast Trigger, Tag Identification Flag being set to 0 if it is equal to 1..
Tag Identification Flag being set to 1.

## Slide 6: Information Exchange Example 2
When multiple TXOPs are used for the information exchange, only one tag has its Tag Identification Flag equal to 1 after the first TXOP.
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
EPC
(Data(Query))
Data((EPC))
PPDU 1
11bp PPDU
11 PPDU
11 PHY
Header
Frame
(Authentication
response))
Unicast
Trigger
(Authentication)
11 PHY
Header
Authentication
CTS
Authentication)
Authentication response
(Data (Authentication) )
(Data (Authentication response))
Authentication
Response
(Unicast RAIID, delay of response,
Data(Authentication) )
(Data (Authentication response))
(Data(EPC))
Query
TXOP 1
TXOP 2
AP assumes no error if no response is received from the STA within delay of response.
Receiving broadcast Trigger, Tag Identification Flag
being set to 0 if it is equal to 1..
Tag Identification Flag being set to 1.

## Slide 7: Solution to Issue 1
Reader 1 Polling Tag
Tag1 with ID N
Responding with EPC
TXOP 1
Reader 2 Polling Tag
Tag 2with ID N
Responding with EPC
TXOP 2
TXOP 3
Reader 2 writing
info to Tag2
Tag 2 with ID N
Responding with EPC
Tag1 setting
Tag Identification Flag to 1
Tag1 setting
Tag Identification Flag to 0
Tag2 setting
Tag Identification Flag to 0

## Slide 8: Issue 2: Multiple AMP Readers Performing Frame Exchanges with Tags Having Same ID
Reader 1 Polling Tag
Tag1 with ID N
Responding with EPC
TXOP 1
Reader 2 Polling Tag
Tag 2with ID N
Responding with EPC
TXOP 2
TXOP 3
Reader 1 writing
info to Tag1
Tag 2 with ID N
Responding with EPC
Tag1 setting
Tag Identification Flag to 1
Tag1 setting
Tag Identification Flag to 0
Tag2 setting
Tag Identification Flag to 0

## Slide 9: Tag Identification Flag for Multiple TXOPs
Each AMP tag has a flag called Tag Identification Flag (EPC Sent flag).
Each time a broadcast Trigger is received by an AMP tag with its Tag Identification Flag to 1, the tag sets its Tag Identification Flag to 0.
Ext End may be used by the reader to a tag for the tag to set its Tag Identification Flag to 0.
In the first TXOP performing the information exchange with an AMP TAG, the AMP reader acquire the tag’s ID.
  The tag sets its Tag Identification Flag to 1.
An AMP tag with Tag Identification Flag equal to 1 receives a unicast Trigger/Write addressed to it will send the response/Ack.
An AMP tag with Tag Identification Flag equal to 0 receives a unicast Trigger addressed to it will not send the response.
  This may happen since two tags have the same STA ID (CRC code).
An AMP reader will execute the following
  If the following are true
    the AMP reader detects a 11bp PPDU,
    the AMP reader is trying to continue the information exchanges with an AMP tag from which it acquires the EPC.
  Then, the AMP reader will stop the further frame exchanges with AMP tag.

## Slide 10: Solution to Issue 2
Reader 1 Polling Tag
Tag1 with ID N
Responding with EPC
TXOP 1
Reader 2 Polling Tag
Tag 2with ID N
Responding with EPC
TXOP 2
TXOP 3
Reader 2 writing
info to Tag2
Tag 2 with ID N
Responding with EPC
Tag1 setting
Tag Identification Flag to 1
Tag1 setting
Tag Identification Flag to 0
Tag2 setting
Tag Identification Flag to 0
Reader1 canceling its following operation with Tag1

## Slide 11: Usage of Ext and Ext End
Ext and Ext End may be used further improve the inter-op.
  When Ext is received, Tag Identification Flag is set to 1.
  When Ext End is received, Tag Identification Flag is set to 0.

## Slide 12: AMP Reader ID for Multiple TXOPs
A frame transmitted by AMP reader carries the TA that identifies the AMP reader.
  This method is only applicable to backscatter tag.
Each time a broadcast Trigger is received by a tag in a TXOP with the TA equal to its recorded AMP reader ID, the tag resets the recorded reader’s ID.
If a tag sends its EPC solicited by the AMP reader, the tag records the reader’s ID.
If the tag receives the unicast trigger with TA equal to its recorded reader’s ID and the tag sends its tag ID and EPC in the previous TXOP, the tag sends the response solicited by the AMP reader.
If the tag receives the unicast trigger with TA being not equal to its recorded reader’s ID to which the tag sends its tag ID and EPC in the previous TXOP, the tag ignores the unicast Trigger.

## Slide 13: AMP Reader ID Collision
Observation:
  The neighbor AMP readers may have the same AMP reader ID.
Solution:
  If an AMP reader detects that another AMP reader uses the same AMP reader ID as its AMP reader ID, the AMP reader randomly selects a new AMP reader ID value under the condition that it has no on-going information exchanges with a tag.
  An AMP reader may announce its AMP reader ID through a broadcast public 802.11 management frame.

## Slide 14: Backup Slides

## Slide 15: Information Exchange Example 3
When multiple TXOPs are used for the information exchange, only one tag has its Tag Identification Flag equal to 1 after the first TXOP.
11bp PPDU
11 PPDU
Frame
(responding data))
Unicast
Trigger
(Read)
11 PHY
Header
Read
CTS
Read
Responding data
(Data (Authentication) )
(Data (Responding data))
Responding data
(Unicast RAIID,
Data(Read) )
(Data (Responding data))
TXOP 2
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
EPC
(Data(Query))
Data((EPC))
PPDU 1
11 PHY
Header
(Data(EPC))
Query
TXOP 1
Receiving broadcast Trigger, Tag Identification Flag
being set to 0 if it is equal to 1..
Tag Identification Flag being set to 1.

## Slide 16: Information Exchange Example 4
When multiple TXOPs are used for the information exchange, only one tag has its Tag Identification Flag equal to 1 after the first TXOP.
11bp PPDU
11 PPDU
Ack Frame
Unicast
Write
(Write)
11 PHY
Header
Read
CTS
Write
(Data (Write) )
Responding data
(Unicast RAIID,
Data(Read) )
(Data (Responding data))
TXOP 2
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
EPC
(Data(Query))
Data((EPC))
PPDU 1
11 PHY
Header
(Data(EPC))
Query
TXOP 1
Receiving broadcast Trigger, Tag Identification Flag
being set to 0 if it is equal to 1..
Tag Identification Flag being set to 1.