## Slide 1: Frame Format Discussion
Date: 2025-05-10
Authors:

## Slide 2: Recap: Frame Format Indication in [1]
The following are potential 11bp frame formats (at least for mono-static backscatter tag):
  Frame format 1: FC (frame control) field + frame body + FCS field where the frame body carries RFID message defined by RFID.
    MAC layer needs to understand the RFID command in frame body.
  Frame format 2: similar to WUR frame format.
    Frame header includes FC, TA, RA, frame body, FCS.
    The frame body is transparent to MAC.

## Slide 3: Frame Format Option 1
A 11bp frame includes the following fields
  Frame Header
    Frame Control field
      Responding Data rate (1 bit)
      Reserved (7 bits)
  Frame body.
    RFID message from reader to tag
      Broadcast Trigger, RFID Query, RFID Read, RFID Write, RFID Authentication.
    RFID message from tag to reader
      CRC code, EPC, information being read, RFID Authentication response, Ack to the information being written to the tag.
  FCS.
Frame Header
Frame Body
FCS
Response
Rate
Reserved

## Slide 4: Frame Format Option 2: Frame Consideration
The broadcast trigger frame initiates random access in its slot(s).
  The frame body includes the number of random slots, the threshold for accessing each slot, the slot length, the date rate of responding frame if the frame header doesn’t carry such information,
The unicast trigger frame frame with unicast RA ID solicits the UL frame from the indicated tag (STA).
  The frame body of a unicast frame carry the (updated) command (Query, Read, Authentication, Write) from the up layer.

## Slide 5: Frame Format Option 2: Frame Consideration
The response frame from the tag carries one of the following based on the Command in the soliciting unicast Trigger frame
  EPC.
  The information being read from the tag.
  Authentication response.
  The Ack to the information being written to the tag.
    One option is that no the up layer of the MAC layer is involved for sending the responding frame.
When all 11bp frame exchanges are initiated by the AMP reader (AP), the DL Ack frame for each UL frame solicited by the Trigger is not needed for the UL information transmission (information read, authentication, EPC acquiring).
  If the UL frame transmission fails, the AMP reader MAC will retransmit the Trigger frame.
  The new Trigger frame or the following Ack implies the correct reception of the UL frame.
When the AMP reader writes the information to the tag, the ack is needed.

## Slide 6: Frame Format Option 2: Frame Format Definition (1)
Frame Header
Frame Body
(Optional)
FCS
Frame
Type
Protection
Indication
Response
Rate
Reserved
RA/TA ID
(Optional)
A 11bp frame includes the following fields
  Frame Header
    Frame Control field
      Frame Type (3 bits),
        Option 2.1: Broadcast trigger, Unicast trigger, Response (Ack is special type of Response)
          Unicast Trigger carries one of Query, Read, authentication request, Write.
        Option 2.2: Broadcast trigger, Unicast trigger, Write, Response, Ack
        Option 2.2: Broadcast trigger, Authentication (Unicast trigger with delayed response), Unicast trigger without delayed response, Write, Response, Ack
      Protection Indication (1 bit),
        This may not be required if the response of Authentication is the only frame with the protection.
      Responding Data Rate (1 bit)
      Reserved (3 bit)
    RA ID of DL unicast frame
      The RA ID of UL unicast frame may be required.
Frame Control

## Slide 7: Frame Format Option 2: Frame Format Definition (2)
A 11bp frame includes the following fields (Cont’d)
  Frame body.
    Optional, e.g. the Ack frame doesn’t have frame body.
  FCS.
One variant to 11bp frame option 2 is that a TA ID field is carried in Frame Header after RA ID field if exists or after FC if RA ID doesn’t exist.

## Slide 8: Summary
The UL/DL 11bp frame format is discussed:
  Option 1: FC field + frame body + FCS field
    MAC layer needs to decode frame body.
  Option 2: frame header (FC + RA) field + frame body + FCS field
    TA may be needed in DL case.
    Frame body is transparent to MAC layer except the broadcast Trigger frame.
For backscatter use case,
  the Ack from the AMP reader to AMP tag is not needed.
  The RA and/or TA is not needed in some frames.
We prefer option 2.

## Slide 9: Reference
[1] https://mentor.ieee.org/802.11/dcn/24/11-24-1811-00-00bp-frame-format-discussion.pptx