## Slide 1: Proposed Changes to 802.11 Definitions Based on 802-2024
Date: 2025-05-13
Authors:

## Slide 2: Abstract
This contribution provides a summary of the definition changes made in IEEE Std 802-2024 and discusses possible impacts on IEEE Std 802.11-2024.

## Slide 3: 802-2024 Changes that may impact 802.11 (1/5)
Definitions modifications:
  Modified: Access domain – from:“… to communicate over a common physical medium.” to: “… to access a common communications channel to exchange information.
  Modified: Bridge
    From: “A functional unit that interconnects two or more IEEE 802® networks that use the same data link layer (DLL) protocols above the medium access control (MAC) sublayer, but can use different MAC protocols. Forwarding and filtering decisions are made on the basis of layer 2 information.”
    To: “In the general sense, a functional unit that interconnects two or more access domains. In the context of IEEE Std 802, this is narrowed to interconnecting two or more bridgeable IEEE 802® networks that use the same data link layer (DLL) protocols above the medium access control (MAC) sublayer, but can use different MAC protocols. Forwarding and filtering decisions are made on the basis of Layer 2 information.”
  Added: bridgeable network: A communication resource that provides the medium access control (MAC) service specified in IEEE Std 802.1AC, between two or more MAC service access points (MSAPs), supporting the MAC Internal Sublayer Service.

## Slide 4: 802-2024 Changes that may impact 802.11 (2/5 )
Definitions modifications:
  Deleted: “canonical format”
  Added: Extended Unique Identifier (EUI): A 48-bit or 64-bit identifier intended to be globally unique and subassigned, by the assignee of a block of such identifiers assigned by the IEEE Registration Authority, to a hardware device instance or other object that requires unique identification.
  Deleted: frame
  Modified: handover
    From: “The process by which a mobile node obtains facilities and preserves traffic flows when traffic is switched from one link to another. Different types of handover are specified based on the way facilities for supporting traffic flows are preserved.”
    To: “A process by which a mobile node obtains facilities and preserves traffic flows when traffic is switched from one link to another.”
  Deleted: “IEEE 802 network” and “interconnection”

## Slide 5: 802-2024 Changes that may impact 802.11 (3/5 )
Definitions modifications:
  Added: logical link control (LLC) entity: The instantiation of an active element embodying LLC-specific capabilities at a single station.
  Mark H: We might want to look our uses of “LLC sublayer” and check if they should be LLC entity. For example, if we say something like, “The MAC delivers the MSDU to the LLC sublayer” (I don’t know if we do say anything like that, but I think we do…?)
  Added: logical link control (LLC) protocol data unit (LPDU): An LLC protocol data unit carried in the data field of a frame as an medium access control (MAC) service data unit (MSDU).
  Mark H: Consider if any of our uses of MSDU would be better as LPDU?
  Added: medium access control (MAC) entity: The instantiation of an active element embodying MAC-specific capabilities at a single station.
  Changed: “medium access control (MAC) data frame: A data structure consisting of fields in accordance with a MAC protocol, for the communication of user data and control information in a network; one of the fields contains a sequence of octets of user data.” To: “medium access control (MAC) frame: A data structure consisting of fields in accordance with a MAC protocol, for the communication of user data and/or control information in a network.”

## Slide 6: 802-2024 Changes that may impact 802.11 (4/5 )
Definitions modifications:
  Added: medium access control (MAC) service data unit (MSDU): Data sent within a MAC frame by a MAC entity for delivery to one or more MAC entities.
  Added: Network Unique Identifier (NUI): An identifier that is unique within the IEEE 802® local area network (LAN).
  Deleted: noncanonical format
  Added: protocol data unit: A unit of information transmitted among peer instances of a layer or sublayer comprising protocol-specific control information and user data.
  Modified: repeater:
    From: “A device that interconnects segments of the physical medium by retransmitting a copy of the physical layer (PHY) frame.”
    To: “A device used to interconnect segments of the physical communications media, for example, to extend the range of a network when the physical specifications of the technology would otherwise be exceeded, while providing a one access domain for the attached stations.”
  Deleted: service data unit, single access domain, and station
  Mark H: Actually, station is _not_ deleted. It is: “An end station or bridge”. In 802.11, we probably think a bridge contains 2 (or more) stations. Is this a problem?

## Slide 7: 802-2024 Changes that may impact 802.11 (5/5)
Definitions modifications:
  Added: Structured Local Address Plan (SLAP): An optional standardized specification to differentiate local medium access control (MAC) addresses.

## Slide 8: Access Domain - Modified
Access domain is used in 4 location in 802.11REVme_D7.0
198.7 – no issue the definition is consistent with use and call out “of “IEEE Std 802TM access domain”
278.43 – no issue the definition is consistent with use and call out of “IEEE Std 802TM access domain”
276.51 – This text to be reviewed: “If multiple BSSs are configured with the same SSID, but the APs are not interconnected by a common DS, there is no guarantee of seamless mobility for STAs between those BSSs. However, such a deployment might have a common LLC sublayer interconnection, in which case communication with location transparency to the LLC sublayer (a single access domain) is generally still possible, but such communication could be disrupted at times when a mobile STA moves between BSSs.”
3304.31 – no issue the definition is consistent with use, but adding the additional description of “IEEE Std 802TM access domain” may improve clarity.

## Slide 9: Bridge - Modified
Bridge is used in 71 location in 802.11REVme_D7.0
The majority of uses are “802.1Q bridge” which is specific type of bridge, and the definition change is of no concern. There are also multiple references to the “bridge port” and “VLAN bridge”, which is a clearly defined entities, and are not impacted by the definition change. 802.11 defines “attached bridge” 217.47, so it is not impacted by the definition change.
373.58, 378.59, 1885.44, 2966.13, 6115.39, 6115.41 – the general term “bridge” is used – the new definition does not impact this use.
No issues.

## Slide 10: Bridgeable Network, Extended Unique Identifier (EUI), logical link control (LLC) entity, logical link control (LLC) protocol data unit (LPDU) - Added
These terms are not used in 802.11. So, unless the term needs to be added, there are no issues.
Mark H: Seems like we should consider the new LLC entity term, as a replacement for our “LLC sublayer”, at least in some contexts.
Mark H: We should check the use of bridgeable (in the Proxy ARP subclause). (In fact, in hindsight, we should check that entire paragraph (and perhaps others in the subclause), as I can’t make sense of it. This seems to have come from 11-22/510r1)
Mark H: Should be using (or considering, depending on context?) using “EUI-48 or EUI-64” (except we probably don’t need the EUI-64) instead of “universal MAC address”?
Mark H: We could also check the use of MSDU versus LPDU, to see if we would be more correct to say LPDU. For example, in 4.3.31.2

## Slide 11: The following deleted terms are defined in 802.11
Frame is defined in 802.11. So, no issues.
Station is defined in 802.11. So, no issues.
Interconnection - Deleted
Interconnection is not defined in 802.11, the term is used in “Open Systems Interconnection (OSI)” which is not an issue. It is also used in two locations in the general sense (276.50, 319.11), and the lack of a definition is acceptable. So, no issues.
The following deleted terms are not used in 802.11
Canonical format is not used in 802.11. So, no issues.
IEEE 802 network is not used in 802.11. So, no issues.
canonical format is not used in 802.11. So, no issues.
noncanonical format is not used in 802.11. So, no issues.
service data unit is not used in 802.11. So, no issues.
single access domain is used in 802.11 as a generic term, it doesn’t need to be defined, no issue

## Slide 12: Handover - Modified
The term “handover” is used extensively in 802.11 (165 uses), it is not defined in 802.11, and the change to the definition in 802-2024 does not impact the use of the term in 802.11. Therefore, no issues.

## Slide 13: medium access control (MAC) entity - added
The term “MAC entity” is used extensively in 802.11 (325 uses), it is not defined in 802.11, and the change to the definition in 802-2024, may have some impact on the use of the term in 802.11. Therefore, additional review may be warranted.

## Slide 14: medium access control (MAC) service data unit (MSDU) - added
  802-2024 definition:
  medium access control (MAC) service data unit (MSDU): Data sent within a MAC frame by a MAC entity for delivery to one or more MAC entities.
  802.11definition:
  medium access control (MAC) service data unit: [MSDU] Information that is delivered as a unit between MAC service access points (SAPs).
  Should we align these definitions? I see no reason to have two different definitions for MSDU in 802-2024 and 802.11.

## Slide 15: Network Unique Identifier (NUI) - added
The term “Network Unique Identifier (NUI)” is not used in 802.11. Therefore, there is no impact, unless it is desired to add this concept to 802.11.

## Slide 16: protocol data unit - added
  protocol data unit: A unit of information transmitted among peer instances of a layer or sublayer comprising protocol-specific control information and user data.
  The term protocol data unit is used extensively in 802.11 (187 times). It is typically used in conjunction with a type: MAC (MPDU), PHY (PPDU), EAPOL, management (MMPDU) …, These PDUs are well defined in 802.11 and this new definition is compatible with the 802.11 definitions, so no issues.

## Slide 17: repeater - Modified
  From: “A device that interconnects segments of the physical medium by retransmitting a copy of the physical layer (PHY) frame.”
  To: “A device used to interconnect segments of the physical communications media, for example, to extend the range of a network when the physical specifications of the technology would otherwise be exceeded, while providing a one access domain for the attached stations.”
  The term repeater is not used in 802.11, so there are no issues.

## Slide 18: Structured Local Address Plan (SLAP) - Added
  Added: Structured Local Address Plan (SLAP): An optional standardized specification to differentiate local medium access control (MAC) addresses.
  Structured Local Address Plan (SLAP) is defined as an acronym in 3.4 and issued in 802.11 (18 locations). There is no issue with the new definition in 802-2024 as it defines the concept used in 802.11. Therefore, no issue.

## Slide 19: References