## Slide 1: Dynamic Power Saving Operation for EMLSR STAs
Date: 2025-05-14
Authors:

## Slide 2: Abstract
TGbn agreed Dynamic Power Saving (DPS) method
  DPS mode can be changed with ICF and ICR exchange.
    Lower capability mode (LCM) and higher capability mode (HCM) can be enabled with ICF and ICR exchange.
EMLSR was adopted in 11be for single radio devices’ multi-link operation.
  EMLSR non-AP STAs can receive an ICF frame in one of EMLSR links.
  Once an EMLSR non-AP STA receives an ICF, it will switch to the link on which the ICF was received.
  After communication with the AP, the EMLSR non-AP STA switches back to EMLSR listening mode.
In order for EMLSR non-AP STAs in DPS LC mode to transition to HC mode, switching delays of both EMLSR and DPS need to be considered.
In this contribution, DPS operation for EMLSR non-AP STAs is discussed.

## Slide 3: ICF and switching delay for the DPS mode change of an EMLSR non-AP STAs
When an EMLSR non-AP STA receives an ICF, it needs to be switched to EMLSR mode to receive data frames from the AP.
When an EMLSR non-AP STA is in DPS LC mode, it needs to be switched to HC mode upon the reception of DPS ICF.
In order to work for both EMLSR and DPS, common ICF needs to be defined and switching delay for both EMLSR and DPS needs to be considered.
  The longer switching delay between DPS padding delay and EMLSR delay can be used.

## Slide 4: Summary
This submission discussed a DPS operation for EMLSR non-AP STAs.
In order for EMLSR non-AP STAs in DPS LC mode to transition to HC mode, switching delays of both EMLSR and DPS and common ICF design for both EMLSR and DPS mode change need to be considered.