## Slide 1: Comparison between FEC/no-FEC for UL of active TX AMP STA
Date: 2025-06-17
Authors:

## Slide 2: Abstract
We provide a comparison for supporting the decision whether to include forward error correcting code (FEC) in the uplink of the active TX AMP non-AP STA or to define only uncoded transmission.

## Slide 3: Preface
The advantages of error correcting codes were prominent and consistent in the last 50 years, where these codes are implemented in practically all digital communication devices
FEC combined with Manchester encoding was already considered for 802.11ba [1], even though the WUR receiver is a very simple low power receiver
The receiver of the UL (AMP-AP) is expected to have higher capabilities like mixer, filters, ADC, AGC, either outlet or battery powered, legacy 802.11 reception and transmissions, NVM memory etc. These make decoding FEC a very simple task

## Slide 4: Performance Assumptions
UL of active TX: agreed on 3 rates - 0.25,1,4Mbps
  It was not discussed which is the best approach to deliver these rates
It is assumed AMP-AP receiver is a capable receiver
  Filtering, Coherent detection with track over PN and Viterbi decoder can be used
Schematic receiver structure:
As can be noticed, uncoded has a 3dB inherit advantage in SNR due to lower BW that the receiver can use to reduce the noise (for all data rates)

## Slide 5: Performance of FEC + M-OOK vs uncoded M-OOK UL for Active TX AMP STA
We used the standard FEC defined in 802.11 (17.3.5.6), i.e. [133,171] rate=1/2, including 6 tail bits for trellis termination
Using the assumptions of [3], we simulated coherent reception
FEC gains @FER=0.1: SNR gain = 8.5dB Coding gain = 5.5dB
FEC strength gives almost x4 rate (x4 energy) for the same TX power
FEC gives almost x2 range improvement over Friis for 0.25Mbps
Coding
Gain = 5.5dB

## Slide 6: Performance Impact on System
In terms of actual deployment, FEC provides substantial advantages
In most cases, it will reduce inventory times nearly x4
5.5dB coverage
Improvement
X4 energy usage improvement

## Slide 7: Analysis of Complexity @ AMP-STA
The FEC+M-OOK transmitter with FEC Rate=1/2 needs x2 symbol clock compared to the uncoded M-OOK
  This can increase complexity in some active TX AMP STA implementations.
  However our analysis indicates a 6% increase of power consumption w.o. any complexity impact.
TX-EVM benefit of 8.5dB is expected for the FEC+M-OOK (11.5dBc w. FEC vs 20dBc w.o. FEC)
  TX-EVM should be defined, similar to 19.3.18.7.4 in 802.11-2020. This will allow a simpler implementation of active TX AMP STA w FEC.
    For example, TX power difference between ON/OFF, unlike WUR which uses high quality transmitter, OFF with 11.5dB drop instead of 20dB (30.3.12.4 in 80211-ba 2021) is very beneficialy for active tx AMP-STA.
Robustness
  For high SNR, FEC prevents a single errounous bit to hinder the packet.
Lower EIRP
  FEC allows active TX AMP-STAs to operate with lower EIRP compared to no FEC

## Slide 8: Impact on SYNC Field Length
An analysis for SYNC length for coherent reception with 1000ppm LO accuracy and a PN model - which is reasonable for low complexity devices was presented in [3] slides 8-10.
It was shown in [3] that it is sufficient, while getting the FEC gains, to use the following SYNC lengths, with low overheads (<8% for 200 bits payload) and reasonable AMP-AP complexity:
Even higher overheads are still acceptable
Payload= | 200 | bits |  |  |  | 
Rate [Mbps] | 0.125 | 0.125 | 1 | 1 | 4 | 4
Payload [us] | 1600 | 1600 | 200 | 200 | 50 | 50
AMP-STF [us] | 128 | 64 | 16 | 8 | 4 | 2
%overhead | 7.41% | 3.85% | 7.41% | 3.85% | 7.41% | 3.85%

## Slide 9: Impact on Spectrum
FEC with Rate=1/2 increases BW by x2
For R=0.25,1 Mbps using FEC with Rate=1/2, the resulting BW is well below OFDM channel BW (20MHz)
For R=4Mbps, using FEC Rate=1/2 results in 3dB BW of 16MHz
  Adding the 1000ppm LO accuracy of active TX, transmission is within the 22MHz DSSS channels bandwidth, almost within 20MHz OFDM channels.
  In case we would like to fully comply with the OFDM channels (avoid the 0.8-1MHz deviation), we can consider the use of FEC with Rate=2/3 only for 4Mbps (from 17.3.5.6 in 80211-2020). This will result in BW=12MHz, which fits well within 20MHz OFDM channels even after considering the 1000ppm LO accuracy.

## Slide 10: Summary
Uncoded M-OOK was compared to FEC+M-OOK
It seems performance improvments are substential and come with complexity and power benefits for the AMP-STA
Since 802.11 channels are commonly 20MHz/22MHz wide, adding FEC improves the utilization of this channel and reduces slack BW.

## Slide 11: References
[1] 11-17-0670-00-00ba-data-rates-and-coding, Qualcomm
[2] 11-24-1497-00-00bp Uplink Rates for Active Transmission, Wiliot
[3] 11-24-1799-00-00bp-analysis-of-free-running-oscillators-accuracy-for-active-transmission-amp-devices, Wiliot

## Slide 12: Strawpoll
Do you agree to add into section 4.4.3 of the SFD the following text:
“11bp defines forward error correcting code (FEC) for the data portion of UL active transmission in 2.4 GHz”
Y:
N:
A:

## Slide 13: Strawpoll
Do you agree to add into section 4.4.3 of the SFD the following text:
“11bp defines forward error correcting code (FEC) for the data portion of UL active transmission in 2.4 GHz based on the code as defined in 17.3.5.6 in 80211-2020”
Y:
N:
A: