## Slide 1
Name | Affiliations | Address | Phone | email
Hang Yang | Ruijie Networks Co., Ltd. |  |  | yanghang1@ruijie.com.cn
Ke Zhong | Ruijie Networks Co., Ltd. |  |  | zhongke@ruijie.com.cn
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Fachang Guo |  |  |  | 
Discussion on Downlink Data Transmission
Date: 2025-5-29
Authors:

## Slide 2: Background
The following text has already been included into TGbn SFD[1]:
• During a roaming transition, the current AP MLD shall be capable of signaling termination of downlink data transmission to the non-AP MLD before the transient TBD time period to receive buffered downlink data from current AP MLD period ends
•Signaling TBD
NOTE: AP sends the indication when there is no more pending DL data (all TIDs). TBD other conditions.
[Motion #350]

## Slide 3: Introduction
In TGBn SFD[1], the early termination indication of downlink data transmission sent by AP MLD and non-AP MLD has been approved.
In this contribution, we would like to discuss some details about signaling on early termination indication to minimize the impact on downlink data transmission.

## Slide 4: Discussion on Downlink Data Transmission
In the case that AP MLD provide an indication to non-AP MLD for downlink data transmission is early-terminated.
  The indication could be sent in the HT-Control field of the Control frame or Data frame.
  This will reduce the impact on downlink data transmission and minimize ST execution latency.
Signaling:
  AP MLD: BA Request + HTC field (with Early termination indication)
STA
AP 1
(Current AP)
ST execution request
ST execution response)
Buffer data transmission
BA request + HTC field
(Early termination indication)
BA
AP decide to terminate transmission
Data forward
Communicate with Target AP2
The reasons could include:
  All TIDs data has been cleared.
  Some certain TIDs data has been cleared.
  Other TBD conditions.

## Slide 5: Summary
In this contribution, we discussed the details on downlink data transmission after ST execution:
  To reduce the impact on downlink data transmission and minimize ST execution latency, the early termination indication could be sent in the HT-Control field of the Control frame or Data frame.
  Other roaming related indication may also be considered to be carried in the HT-Control field, so that AP MLD and non-AP MLD could exchange these indication during data transmission.

## Slide 6: Straw Poll 1
Do you agree that early termination indication of downlink data transmission could be sent in HT-Control field of the Data frame or Control frame?
  Details on HT-Control field design is TBD
  Other roaming indications sent in HT-Control field are TBD

## Slide 7: References
[1] IEEE 802.11-24/0209r15, Specification Framework for TGbn