## Slide 1: Discussion on NPCA switching delay
Name | Affiliations | Address | Phone | email
Longlong Hong | Ruijie Networks Co., Ltd |  |  | honglonglong@ruijie.com.cn
Hui Che |  |  |  | 
Ke Zhong |  |  |  | 
Mengying Lin |  |  |  | 
Fangchang Guo |  |  |  | 
Date: 2025-06-06
Authors:

## Slide 2: Introduction
[Motion 124] An NPCA STA shall indicate the following to its peer NPCA STA[1]
  NPCA switching delay
    time it needs to switch from the BSS Primary channel to the NPCA Primary channel
  NPCA switch back delay
    time it needs to switch from the NPCA Primary channel to the BSS Primary channel
  Delay values range between 0 and 256 us with a 4 us resolution
The NPCA switching delay and NPCA switch back delay have been discussed in multiple proposals[2-5].
OBSSs often use the same primary channel if the operating channels overlap
  During TWT SPs, OBSS interference may significantly degrade transmission efficiency within TWT.
This contribution discusses the design of NPCA switching delay and NPCA switch back delay for TWT transmission scenarios.

## Slide 3: Problem Statement
NPCA non-AP STAs have different NPCA switching/switch back delays
  Case 1: Short NPCA switching/switch back delay when the NPCA primary channel is within their operating bandwidth
  Case 2: Long NPCA switching/switch back delay when the NPCA primary channel is outside their operating bandwidth
For NPCA APs, balancing fairness and efficiency with different switching/switch back delays is challenging.
Configuring tailored delay parameters based on the switching/switch back delay requirements of STAs in TWT groups can effectively enhance transmission efficiency.
Primary channel unavailable
NPCA Operation
Long NPCA switching delay
NPCA Operation
Short NPCA switching delay

## Slide 4: Proposed solution
TWT-Based NPCA Parameter Application:
  AP and non-AP STAs use pre-negotiated NPCA parameters during TWT SPs.
    TWT NPCA switching delay, TWT NPCA switch back delay
For different TWT groups, such as
  TWT Group 1{short NPCA switching/switch back delay}
  TWT Group 2{long NPCA switching/switch back delay}
During a TWT SP, when OBSS interference is detected:
  NPCA AP and non-AP STAs shall perform NPCA operation with the TWT NPCA switching/switch back delay.
Primary
channel
Non-primary
channel
TWT SP
OBSS PPDU
NPCA Operation
OBSS PPDU
…
TWT NPCA switching delay
TWT NPCA switch back delay
…

## Slide 5: Summary
In this contribution, we discusses NPCA switching delay and NPCA switch back delay
  AP and non-AP STAs use pre-negotiated NPCA parameters during TWT SPs
  During TWT SP, AP and non-AP STAs
    switch to the non-primary channel with TWT NPCA switching delay when an OBSS interference is detected
    switch back to the primary channel with TWT NPCA switch back delay when the OBSS interference ceases

## Slide 6: Straw Poll
Do you agree that AP and non-AP STAs use pre-negotiated NPCA parameters during TWT SP?
      TWT NPCA switching delay, TWT NPCA switch back delay

## Slide 7: References
[1] Draft IEEE P802.11bn D0.2
[2] 11-24/1218r1, “NPCA – Next level discussions,” Gaurang Naik
[3] 11-24/1222r1, “NPCA (Secondary Channel Usage) Follow Up,” Liwen Chu
[4] 11-25/0493r0, “NPCA during scheduled periods,” Zhenpeng Shi
[5] 11-25/624r0, “Further considerations for NPCA operation,” Vishnu Ratnam