## Slide 1: Thoughts on SCS enhancement
Name | Affiliations | Address | Phone | email
Mengying Lin | Ruijie Networks Co., Ltd |  |  | linmengying1@ruijie.com.cn
Fachang Guo |  |  |  | 
Ke Zhong |  |  |  | 
Hang Yang |  |  |  | 
Longlong Hong |  |  |  | 
Date: 2025-06-13
Authors:

## Slide 2: Problem Statement
TGbn defines or reuses/updates existing mechanism for a UHR AP to report long term (periodic) unavailability.
11be introduced the SCS procedures with QoS Characteristics element to enable a client to request the AP to facilitate DL/UL traffic delivery based on min./max. service interval and min. data rate etc.
When APs are operating in periodic unavailability operation mode, it may fail to schedule established SCS stream within the negotiated Min./Max. Service Intervals, resulting in service interruptions for critical traffic streams.

## Slide 3: Existing Solutions and Frameworks
Option 1: APs are prohibited from operating in periodic unavailability operation mode;
Option 2: APs may send an unsolicited SCS Response frame to terminate a granted SCS stream;
  There are no explicit signaling methods for APs to make decisions to terminate the SCS stream which may cause interruptions to critical traffic streams.
  STAs are unaware of the reasons for the AP's termination of corresponding SCS stream, which may lead to frequent re-setup SCS procedures.
In this contribution, we provide additional thoughts on potential enhancements during an SCS agreement with AP periodic unavailability operation (PUO).

## Slide 4: Proposal: Enhancing SCS for AP PUO
In SCS agreements, STAs report the compatibility of the traffic streams with AP availability requirements. For example:
  Requiring the AP to maintain continuous availability;
  Allowing suggested parameter modifications (e.g., adjusting Min./Max. Service Intervals);
  Tolerating temporary SCS authorization suspension/resumption during AP unavailability periods.
During an SCS agreement , the AP may modify scheduling parameters or temporarily suspend established traffic streams for non-critical traffic.
  Upon receiving the adjustment notification, STAs shall comply with the AP's modifications and schedule uplink traffic streams according to the adjusted timing parameters.

## Slide 5: Conclusion
In this contribution, we have provided thoughts on addressing the interruption of critical traffic streams when APs are operating in periodic unavailability operation (PUO).
  Allow parameter adjustments (Min./Max. intervals) or temporary suspension of SCS streams.
  Mandate APs availability for high-priority streams.
  STAs must adapt uplink scheduling strategies based on the AP’s dynamic configurations.

## Slide 6: Straw Poll 1
Do you agree that AP may modify scheduling parameters or temporarily suspend established SCS streams for non-critical traffic when the AP's unavailable periods conflict with the service intervals of SCS traffic streams?

## Slide 7: References
[1] IEEE 802.11-24/0209r15, Specification Framework for TGbn
[2] Draft IEEE P802.11bn D0.2
[3] IEEE 802.11-24/1602r1, Power Save Enhancements in UHR