## Slide 1: MAPC PASN follow up

## Slide 2: Introduction
11bn group agreed to define MAPC PASN procedure to generate PTK for the protected version of MAPC negotiation request/response frame.
TGbn defines a procedure based on pre-association security negotiation (PASN) or uses PASN with necessary extensions to derive the key(s) needed for the protected version of individually addressed MAPC Negotiation Request frame and MAPC Negotiation Response frame exchanged between two APs as part of MAPC operation.
[Motion #428, [264] and [387-389]]
In this contribution, we propose to define a MAPC authentication group concept for the MAPC authentication.

## Slide 3: Authentication problem for the MAPC APs in different ESSs
When two MAPC APs are the members of the same ESS, the two APs understand the can authenticate each other via the same SSID.
The problem is that when two MAPC APs are the members of different ESSs, the two APs can’t recognize whether they can authenticate each other via a certain identifier.
  In general, the two MAPC APs affiliated with different ESSs are configured with different SSIDs

## Slide 4: Propose to define MAPC authentication identifier(AI)
The functionality of MAPC AI is quite similar to SSID.
  Any two MAPC APs recognize whether they can authenticate each other via MAPC AI during MAPC discovery procedure.
  The MAPC AP may advise a MAPC AI list in MAPC discovery request frame, and its (potential) peer AP may make the MAPC discovery response if at least one common MAPC AI is mapped.
  For MAPC PASN with SAE(or other password-base validation techniques), its peer AP may indicate the selected MAPC AI in the first MAPC PASN frame(similar to password identifier in baseline).

## Slide 5: The following figure depicts the usage of MAPC AI in MAPC framework
（1）Discovery Request(MAPC AI list)
AP(1)
AP(2)
（2）Discovery Response(MAPC AI list)
（3）1- MAPC PASN(MAPC AI)
（4）2-MAPC PASN
（5）3-MAPC PASN
Out of band configuration for credential information
（6）Protected version of MAPC Negotiation request
（7）Protected version of MAPC Negotiation response
Discovery phase
PASN phase
Negotiation phase

## Slide 6: Summary
Analysis the authentication problem for the MAPC APs especially in different ESS.
Propose to define MAPC AI (list) included in MAPC discovery phase.
  The MAPC AI may be included in the first MAPC PASN frame.

## Slide 7
THANK YOU 

## Slide 8: Reference
24/209r15 TGbn Specification Framework for TGbn
24/1693r1 The MAPC security framework