## Slide 1: Co-BF OBSS CSI Status Exchange Without New Sequence
Date: YYYY-MM-DD
Authors:

## Slide 2: Abstract
In 802.11bn Co-BF (Coordinated Beamforming) [1], it requires both the sharing AP and the shared AP to have the CSI of the OBSS links ( interference links). Current standard draft does not specify a mechanism for the two APs to exchange their CSI status or CSI information.
In this contribution, a mechanism that allows for exchanging of CSI status between the sharing AP and the shared AP without extra frame exchange is proposed.

## Slide 3: Introduction
For Co-BF, both APs need to know the OBSS CSI of the interference links.
OBSS CSI status information exchange is essential for Co-BF transmission.
  Otherwise, the other AP may keep proposing unsuitable STAs to participate in Co-BF transmission.
CSI status exchange with additional sequence is not favored due to increased complexity and overhead.
CSI status may change over time. Informing updated CSI status helps improve Co-BF transmission success rate.
We propose a simple mechanism to exchange the OBSS CSI status between two APs using existing Invite and Response frames.

## Slide 4: OBSS Status Exchange Without Additional Frame Exchange
A scheme to exchange CSI status using Invite/Response frames during Co-BF transmission
  In the Invite frame, the sharing AP
    Includes a list of candidate STAs for Co-BF transmission that are associated with the sharing AP.
    Updates its OBSS CSI status by including a list of STAs that are associated with the shared AP and have valid OBSS CSI at the sharing AP.
  After receiving the Invite frame, in the Response frame, the shared AP
    Has the full knowledge of the OBSS CSI status at the sharing AP
    Updates its OBSS CSI status by including a list of STAs that are associated with the sharing AP and have valid OBSS CSI at the shared AP.
    Rejects the invite if the shared AP does not have the OBSS CSI for all candidates proposed by the sharing AP
    If it accepts the invite
      Proposes a list of candidate STAs associated with the shared AP from the list of available OBSS CSI STAs provided by the sharing AP.
  After receiving the response frame, the sharing AP has the full OBSS CSI status at the shared AP.
    After the Invite/Response frame exchanges, both AP will have complete OBSS CSI status no matter if the shared AP rejects or accepts the invite.

## Slide 5: Example 1
Sharing AP (AP1) has STAs (1,2) associated with it.
Shared AP (AP2) has STAs (3,4) associated with it.
AP1 has OBSS CSI of 3, OBSS CSI of STA4 is not received.
AP2 has OBSS CSI of 1, OBSS CSI of STA2 is not received.
Invite frame (From AP1)
Response frame (From AP2)
Proposed Candidates | STAs of Peer AP with CSI
STA1 | STA3
Accept or Rejection | STAs of Peer AP with CSI | Proposed Candidates
Accept | STA1 | STA3
AP1 luckily proposes right candidates. It provides OBSS CSI status (STA3)
AP2 accepts the invite and informs AP1 about its OBSS CSI status (STA1) and based on the list from AP1, it proposes only STA3.

## Slide 6: Example 2
Sharing AP (AP1) has STAs (1,2) associated with it.
Shared AP (AP2) has STAs (3,4) associated with it.
AP1 has OBSS CSI of 3, OBSS CSI of 4 is not received.
AP2 has OBSS CSI of 1, OBSS CSI of 2 is not received.
Invite frame (From AP1)
Response frame (From AP2)
Proposed Candidates | STAs of Peer AP with CSI
STA1, STA2 | STA3
Accept or Rejection | STAs of Peer AP with CSI
Reject | STA1
Future Co-BF TX
Proposed Candidates | STAs of Peer AP with CSI
STA1 | STA3
Accept or Rejection | STAs of Peer AP with CSI | Proposed Candidates
Accept | STA1 | STA3
AP1 proposes both STA1/2 as candidates. It provides OBSS CSI status (STA3)
AP1 proposes right candidates based on OBSS CSI status from AP2 in last Invite/Response exchange

## Slide 7: Updated OBSS CSI Helps Co-BF Transmission
CoBF Transmission K
CoBF Transmission 1
Invite
AP11
Sounding
Response
AP11
Sounding
CoBF Transmission
Sync
Invite
Response
CoBF Transmission
Sync
CSI status may change between sounding and transmission and between transmissions.
Update OBSS CSI status at the beginning of transmission helps improve CoBF transmission success rate

## Slide 8: Benefits
CSI status in the Invite and Response frames during transmission is the most accurate and complete.
  Sounding stage CSI status exchange is not complete unless new frames are added.
  CSI status at sounding stage may not be accurate any more at transmissions stage
    Not necessarily transmission immediately follows sounding.
    Between sounding and transmission, the CSI may expire or be evacuated from memory
      Each AP has its own policy on memory management.
    It is natural for an AP to track only the CSI it stores.
  Since CSI is dynamic (could change between Co-BF transmission), it is reasonable to have the CSI updated in the Co-BF transmission Invite/Response frames.
No new frame exchanges needed
After the Invite and Response frame exchange, complete and accurate CSI information is available to both APs.
  No AP will persistently propose unsuitable candidates.

## Slide 9: How Will APs Use the CSI Information
An AP can choose to ignore it. Nothing changed. Only a few bits (or 44(22) bits) wasted. But why not use the information if it is available?
If shared AP schedules Co-BF before Invite (unlikely)
  Issue
    Not necessarily Invite frame comes right after sounding
    STAs’ status may change between sounding and Invite.
  If it can’t reschedule upon Invite frame, at least it can reject the Invite if CSI information from the sharing AP invalidates its planned schedule.
If shared AP schedules upon Invite frame, it can propose candidates based on CSI information from the sharing AP.
The two AP’s reactions to the CSI information are independent.
After first Invite/Response frame exchange, both AP get complete OBSS status information and will be able to propose suitable candidates for next Co-BF transmission.
Continued updating through Invite/Response frame keeps CSI status updated and improves Co-BF transmission success rate.

## Slide 10: Thoughts
The number of OBSS STAs in the list has a limit of 4 or 2.
  An AP has no motivation to store excessive number of CSIs of the OBSS STAs.
  The maximum number of STAs in Co-BF transmission from one AP is 2.
  Include both sequential and jointly sounded STAs.
Implementation suggestion
  Straightforward method is to use AIDs of OBSS STAs, then up to 44(22) bits in Invite and Response frame. Pros: self contained. Cons: more space is needed.
  To save space, we can use a 4-bit value to indicate the status. Each bit maps to one STA. A bit value of 1 indicates its OBSS CSI is available and not expired, 0 otherwise.
    The 4 bits map to the STAs from latest up to 2 NDPA frames from the other AP. If only k<4 STAs, the last 4-k bits are set to 0. If we have sounding session ID concept, the list of OBSS STAs are from the last active session ID
    For the k OBSS STAs, the are sorted in ascending order of AID value. First bit maps to OBSS STA with smallest AID value.

## Slide 11: References
[1] IEEE P802.11bn/D0.1