## Slide 1
June 2025
Channel configuration for NPCA
Date: 2025-06-18
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Introduction
In this contribution, we discuss updating channel configuration parameters through the NPCA Operation Information field to avoid potential ambiguity between NPCA STAs and improve bandwidth efficiency

## Slide 3: Potential ambiguity / BW efficiency (1/3)
The NPCA p-channel is designated channel within the BSS BW to enable NPCA operation and after switching to the NPCA p-channel, if NPCA STAs obtain TXOP on this channel, the BW including NPCA p-channel can serve as the primary segment
This primary segment can be defined based on where the NPCA p-channel is located
  When considering an OPBW 320 MHz, the primary segment during NPCA operation may vary depending on whether the NPCA p-channel is located within an S80 or S160
P80
P20
BSS channel configuration
NPCA channel configuration
S80
S160
P20
P80
P80
P20
BSS channel configuration
NPCA channel configuration
S80
S160
P20
P80
<NPCA p-channel within an S80>
<NPCA p-channel within an S160>

## Slide 4: Potential ambiguity / BW efficiency (2/3)
However, following a channel configuration based only on the primary segment including the NPCA p-channel may lead to ambiguity between NPCA STAs
  For example, NPCA AP and NPCA non-AP STAs may interpret the secondary segment differently
To prevent malfunction due to misaligned channel segments between NPCA STAs, explicitly sharing the full channel configuration can resolve these ambiguity issues
Moreover, it can offer advantages if the explicit configuration is designed in a bandwidth-efficient manner
  A simple method is to configure the full channel allocation across the BSS BW to enable the use of a larger BW during NPCA operation
    By enabling the user of larger BW, when the NPCA AP advertises the NPCA disabled subchannel bitmap which contains information about punctured subchannels, the number of candidate of subchannels available for puncturing may increase
    For example, when operating an NPCA BSS with a 320 MHz BW, there is an additional 160 MHz margin compared to operating it at 160 MHz, and by applying puncturing depending on the channel conditions, a wider NPCA BSS BW can be utilized.

## Slide 5: Potential ambiguity / BW efficiency (3/3)
Case 1 and Case 2 represent different interpretations of the secondary segment depending on whether the NPCA p-channel is in S80 or S160
  In both scenarios, interpreting the channel as Case 2 is more advantageous than Case 1 because it can utilize a larger BW
Therefore, it is necessary to explicitly share the channel configuration so that after the NPCA STA switches to the NPCA p-channel, the channel configuration operates according to Case 2
  One way to explicitly share the configuration is to reuse parameters such as CCFS0 and CCFS1
  These parameters can be included in the NPCA Operation Information field
Case 1
Case 2
P80
P20
BSS channel configuration
NPCA channel configuration
S80
S160
P20
P80
Unused
P80
S160
S80
S80
Case 2
Case 1
P80
P20
BSS channel configuration
NPCA channel configuration
S80
S160
P20
P80
S80
S160
P80
Unused
S80

## Slide 6: Offering channel configuration parameters (1/2)
Proposal : Including NPCA CCFS0/CCFS1 in the NPCA Operation Information field
NPCA CCFS0/CCFS1 subfield :
Subfield | Encoding
NPCA CCFS0 | For 80 MHz NPCA BSS BW, indicates the channel center frequency index of 80 MHz channel For 160 MHz NPCA BSS BW, indicates the channel center frequency index of the primary 80 MHz For 320 MHz NPCA BSS BW, indicates the channel center frequency index of the primary 160 MHz
NPCA CCFS1 | For 80 MHz NPCA BSS BW, this subfield is set to 0 For 160 MHz NPCA BSS BW, indicates the channel center frequency index of 160 For 320 MHz NPCA BSS BW, indicates the channel center frequency index of 320
NPCA CCFS0
(8 bits)
NPCA CCFS1
(8 bits)
NPCA Operation Information field format with added subfield NPCA CCFS0 and NPCA CCFS1

## Slide 7: Offering channel configuration parameters (2/2)
If the NPCA AP and non-AP STA use NPCA CCFS0/CCFS1 along with the NPCA p-channel and set these parameters to optimize BW efficiency, they can clarify the channel configuration and operate unambiguously while enhancing spectrum utilization
  For example, if the NPCA operation is intended to follow the channel configuration shown below (i.e., the desired configuration), this can be achieved via NPCA CCFS1/CCFS0
P80
P20
BSS channel configuration
NPCA channel configuration
S80
S160
P20
P80
S160
S80
NPCA
CCFS0
NPCA CCFS1
(desired)
P80
P20
BSS channel configuration
NPCA channel configuration
S80
S160
P20
P80
S160
S80

## Slide 8: Summary
In this presentation, by explicitly sharing channel configuration parameters, potential ambiguities in NPCA operation can be resolved
Furthermore, if the explicit channel configuration is determined in a bandwidth-efficient manner, it has been shown that NPCA operation can take place over a larger BW during the NPCA period