## Slide 1: Considerations on ELR PPDU Selection Rules
Date: June 20, 2025
Authors:
Name | Affiliations | Address | Phone | Email
Xuwen Zhao | TCL | Building G1, TCL International-E City, Shenzhen, Guangdong, China. |  | zhaoxuwen123@outlook.com
Pei Zhou | TCL |  |  | 
Zhanjin Bao |  |  |  | 

## Slide 2: Introduction
Wi-Fi 8 (802.11bn UHR) & ELR: IEEE 802.11bn aims to support Ultra-High Reliability (UHR) for next-gen Wi-Fi (Wi-Fi 8) in long-range and IoT scenarios. It introduces an Enhanced Long Range (ELR) PPDU format to extend coverage and improve reliability. [1]
Extended Range Benefit: The UHR ELR PPDU significantly improves link budget for distant, low-SNR links (analogous to 802.11ax’s Extended Range PPDU) to serve devices like outdoor cameras, video doorbells, smart appliances at the edge of coverage. This PHY format trades data rate for range by using robust modulation and repetition.
Gap in Draft: The current 802.11bn/D0.3 draft defines the ELR PPDU PHY format. Currently, a CR has proposed ELR operations based on ELR capabilities and indication information[2]. However, it lacks more detailed triggering conditions for selecting ELR PPDU, such as under which scenarios, service types, or device states ELR PPDU should be chosen. As well as, under which specific conditions, ELR PPDU should no longer be used.
Objective: Establish clear selection rules for ELR PPDU usage (when to enter/exit ELR mode, and how to negotiate it) to fully leverage its long-range reliability benefits while maintaining overall network efficiency and compatibility.

## Slide 3: Background (PPDU Selection in 802.11)
Legacy PPDU Selection: In 802.11n/ac/ax/be, PPDU format selection (HT, VHT, HE, EHT) is based on capabilities exchange and dynamic rate adaptation. APs/STAs generally pick the highest performance format both support, falling back to more robust modes as link conditions worsen. No explicit standard mechanism exists to signal “use a more robust PPDU” – devices rely on their own algorithms (e.g. lowering MCS, bandwidth, etc.). [3] [4]
802.11ax Extended Range Example: 802.11ax introduced an HE Extended Range SU PPDU (HE ER SU PPDU) for single-user long-range links. It was restricted to 20 MHz, one spatial stream, and the lowest MCS rates (0–2). This extended-range mode improved coverage but its use was implementation-defined – e.g. an AP could decide to send a far STA’s data with HE ER SU PPDU if needed, without a standardized handshake. [3]
    Throughput vs. Range Trade-off: Using the ELR PPDU greatly extends range and robustness (e.g. increased receiver sensitivity and repetition for low-SNR environments), but it substantially reduces data rate. It is ideal for scenarios prioritizing coverage/reliability (outdoor sensors, low-speed IoT telemetry, emergency data, etc.), whereas for strong links or high-throughput traffic, standard UHR PPDUs (non-ELR) are preferable. A mechanism is needed to switch to ELR only when beneficial.

## Slide 4: Problem Statement
No detailed triggering conditions for ELR PPDU selection: The 802.11bn draft lacks “detailed selection rule” for ELR – meaning vendors must decide on their own when to send a frame using UHR ELR PPDU. This can lead to inconsistent behavior: one device might use ELR in situations where another would not, causing interoperability and performance issues.
No Defined Exit Criteria: Similarly, there is no specified mechanism to exit ELR mode once in it. ELR PPDUs, while reliable, have very low throughput. If a link’s conditions improve or if high-throughput traffic (e.g. HD video, VR streaming) resumes, staying in ELR mode will unnecessarily throttle performance. Without a clear exit strategy, a device might remain in ELR mode longer than needed, degrading user experience when high data rates are required.
Reliability-Efficiency Trade-off: The lack of standardized ELR usage rules presents a trade-off problem. On one hand, not using ELR PPDU when needed means missing out on reliability gains for distant or critical devices. On the other hand, using ELR PPDU too liberally (or not switching back) hurts network efficiency. A balanced strategy is needed so that Wi-Fi 8 can meet its reliability targets (for far-range IoT, etc.) while maintaining throughput and spectrum efficiency for general traffic.

## Slide 5: Proposal #1: Autonomous Decision (Sender/Receiver Controlled)
  In this approach, the decision to use an ELR PPDU is made by one side independently (either the AP or the STA) based on network conditions. For example, an AP can proactively switch to an ELR PPDU for downlink when a given STA is at the cell edge or experiencing high retry rates, to improve delivery success.
0. ELR Capability Exchange
ELR mode is only used if both AP and STA support the UHR ELR PPDU format. If either side is not ELR-capable, the link will always use standard PPDUs.
1. Trigger Conditions
The autonomous decision is driven by configurable thresholds. The initiating device monitors trigger. When the trigger conditions are met, the device decides to enter ELR mode for subsequent frames.
2-5. Data Transfer in ELR Mode
Once activated, the link enters ELR mode – the sender transmits data frames using the UHR ELR PPDU format, and the receiver responds with acknowledgments (ACKs) also in ELR PPDU format. The sender can mark this STA’s state as “ELR in use” in its internal tables, so that even future downlink frames are automatically formatted as ELR PPDU.
6-10. Exit and Reversion
The device that initiated ELR mode continues to monitor link conditions. When it determines that ELR is no longer needed, it will exit ELR mode. The initiator can revert to normal PPDU for the next. After exit, subsequent transmissions use standard (non-ELR) PPDUs.

## Slide 6: Proposal #2 : Negotiated Decision (Sender-Receiver Coordination)
  In this approach, the sender and receiver jointly decide whether to use the ELR PPDU, through an exchange of negotiation frames. Unlike Proposal #1’s unilateral decisions, here a device proposes the ELR mode and the other device explicitly agrees or disagrees. ELR is enabled only if both sides concur that it’s necessary.
0. ELR Capability Exchange
1. ELR Mode Request
When the sender(e.g. the AP) judges that the ELR mode conditions are met, it sends an “ELR Mode Request” to the other side. This can be a new Action frame containing an ELR mode indication and optionally additional info like current link metrics or reason codes. For example, the AP might include the measured RSSI or number of retries for that STA, to justify why ELR is recommended.
2-5. Peer Decision and Response
Upon receiving the request, the receiver (e.g. the STA) evaluates it alongside its own view of the link. The receiver might check, for instance, its throughput needs or battery impact. If the receiver agrees that ELR mode is beneficial, it sends an “ELR Mode Response – Accept” back to the sender. This response frame confirms that it will enter ELR mode; it may be sent using an ELR PPDU itself (to immediately use the robust format for the acknowledgment). If the receiver disagrees, it can respond with a “Reject” or simply not enable ELR.
6-10. Entering ELR Mode
Once the sender receives an acceptance, both sender and receiver switch to ELR mode. The sender proceeds to transmit the pending data frame(s) using the UHR ELR PPDU format. The receiver, having agreed and likely been informed of the switch, is prepared to receive in ELR mode. It successfully decodes the ELR PPDU and then sends its ACK using ELR PPDU as well. At this point, both sides mark the link/state as “ELR mode active.”
6-10. Negotiating Exit (Mode Off)
Either device can initiate an ELR mode termination when conditions improve or high-throughput service is needed again. For example, the sender (e.g. the AP) might detect the channel is now better and send an “ELR Mode Terminate” (or the receiver could do likewise). The other side responds with an acknowledgment to confirm exiting ELR mode. After this handshake, both revert to normal non-ELR PPDU operation. This ensures a mutual understanding before returning to regular high-speed transmission. (If one side thinks it still needs ELR, it could deny the disable request, though in practice both should prefer returning to normal mode when conditions allow.)

## Slide 7: Summary
Addresses Draft Gap: This proposal fills an important gap in IEEE 802.11bn by defining when and how the MAC layer should utilize the ELR PPDU. By introducing selection rules, we ensure that all Wi-Fi 8 devices handle the Enhanced Long Range feature consistently, unlocking its benefits (extended range, higher reliability) for real-world deployments.
Two Complementary Methods: Providing two mechanisms – one autonomous and one negotiated – for initiating ELR mode.
  The autonomous approach allows immediate reaction to link degradation by whichever side (AP or STA) detects it.
  The negotiated approach adds a handshake to ensure both sides agree, preventing needless use of the low-rate mode. t.
Reliability with Efficiency: The aim is to improve reliability for distant or challenging links by leveraging the ELR PPDU when needed, but also to return to normal high-throughput operation as soon as conditions permit. In ELR mode, devices gain range and robustness (fewer drops for far-away IoT nodes, better coverage in outdoor environments), and once the link quality improves, they seamlessly switch back to wideband, multi-stream PPDUs to maximize data rates. This dynamic ensures overall network throughput is not sacrificed unnecessarily for reliability.

## Slide 8: Straw Poll #1
Do you agree to add the following text to the TGbn SFD:
Clear selection rules for ELR PPDU usage (when to enter/exit ELR mode, and how to negotiate it) shall be introduced to fully leverage its long-range reliability benefits while maintaining overall network efficiency and compatibility.
Y/N/A

## Slide 9: References
[1] Draft P802.11bn_D0.3
[2] 11-25-0915-02-00bn-pdt-cr-for-elr-mac
[3] Draft P802.11REVme_D7.0
[4] Draft P802.11be_D7.0