## Slide 1: DPS Suspending Operation
Date: 2025-04-23
Authors:

## Slide 2: Abstract
Dynamic power save (DPS) operation has be defined in the 802.11bn™/D0.2[1]. If a STA enables the DPS operation, the STA may change its capability when receiving an ICF frame. If the STA is a mobile AP, the STA may receive ICF frame and change capability frequently, reducing the power efficiency of the DPS operation.
In this contribution, we discuss the issue of frequent ICF frame.

## Slide 3: Discussion
Is there a scenario where the AP may receive ICF at high frequency:
  Yes. There are some examples as following
    In R-TWT/TWT SP, several STAs may initiate ICF/ICR exchanges for frame exchanges in HC mode.
    In another scenario, the AP determines that the UL buffer size is too large based on buffer report
    Predictable periodical UL traffic transmission from multi-STA
Can we reduce the ICF/ICR exchanges by disabling DPS operation
  NO. Changing DPS mode is a slow process that requires prior indication by the AP for a sufficient period of time[2].
Do we need a mechanism to reduce the ICF/ICR exchanges
  Yes. There are two aspects:
    Frequent ICF/ICR exchanges could reduce the power efficiency both in AP and STA side.
    The padding in ICF and mode switching could lead to larger latency

## Slide 4: Proposal: DPS Suspending Operation
An DPS (mobile) AP STA that has enabled DPS mode may announce a service period (SP) during which the DPS operation in AP STA side is suspending
  The AP STA shall operate in HC mode and non-AP STAs can initiate frame exchanges in HC mode without transmitting ICF during the SP
  The announced SP may span several TXOPs
AP
STA-1
STA-2
DPS Suspending Frame
UL Frame in HC mode
UL Frame in HC mode
DPS suspending duration ( HC mode)
TXOP
TXOP

## Slide 5: DPS Suspending Frame
DPS Suspending Frame could be a type of UHR action frame that may include:
  DPS Suspending Start Time field that indicates the TSF time (eg, Partial TSF Timer field) of the DPS operation suspending
  DPS Suspending Duration field that indicates the period of time (eg, in units of TU) during which the STA operates in HC mode
  Others are TBD
Category | UHR Action | DPS Suspending Info
… | DPS Suspending Start Time | DPS Suspending Duration | …
DPS Suspending Frame Format
Octets:
4
1

## Slide 6: Straw Poll 1
Do you support to add the following into the 11bn SFD?
  Define a mechanism to suspend LC (Lower Capability) mode in DPS operation
    Allowing an STA that has enabled DPS mode to announce a period of time during which the STA operates in HC mode (Higher Capability)
    Note: the detailed announcement design is TBD.

## Slide 7: References
[1] 802.11bn™/D0.2
[2] 11-25-0404r0 Parameter Update in DPS mode