## Slide 1: Discussion on NPCA switch back
Date: 2025-06-25
Authors:

## Slide 2: Abstract
NPCA operation has been introduced in UHR by which a STA can access the wireless medium when the primary 20 MHz channel is occupied.
NPCA STAs can achieve more opportunities for transmission and reduce the delay of their traffic by doing channel access on the NPCA primary channel.
It is obviously that NPCA STAs should not stay on the NPCA primary channel for a long time. Several contributions provide solutions for different procedures of NPCA operation. But no consensus has been reached on switch back rules or conditions for NPCA.

## Slide 3: EMLSR switch back
The switch back rules for EMLSR are very worthy of reference for switch back rules of NPCA.
It can be briefly summarized as :
  When the non-AP STA received the EMLSR ICF detected the end of the frame exchanges, the affiliated non-AP MLD shall initial switch back to listening operation and finish it after the EMLSR transition delay.
    1. It doesn’t detect an PPDU, or;
    2. It doesn’t detect an PPDU that it is interested in,
    during a timeout interval,
To achieve more gain from multiple links, an MLD should switch back to EMLSR listening operation on every EMLSR link after the end of frame exchange ASAP.
Notes: The non-AP MLD shall be switched back to the listening operation on the EMLSR link(s) after the
EMLSR transition delay time most recently indicated by the non-AP MLD if any of the following
conditions is met, and this is defined as the end of the frame exchanges:
•
The MAC of the non-AP STA affiliated with the non-AP MLD that received the initial Control
frame does not receive a PHY-RXSTART.indication primitive during a timeout interval of
aSIFSTime + aSlotTime + aRxPHYStartDelay, where aRxPHYStartDelay is equal to 20 µs,
starting at the end of the PPDU transmitted by the non-AP STA affiliated with the non-AP MLD
as a response to the most recently received frame from the AP affiliated with the AP MLD or
starting at the end of the reception of the PPDU containing a frame for the non-AP STA from the
AP affiliated with the AP MLD that does not require immediate acknowledgement.
•
The MAC of the non-AP STA affiliated with the non-AP MLD that received the initial Control
frame receives a PHY-RXSTART.indication primitive during a timeout interval of
aSIFSTime + aSlotTime + aRxPHYStartDelay starting at the end of the PPDU transmitted by
the non-AP STA affiliated with the non-AP MLD as a response to the most recently received
frame from the AP affiliated with the AP MLD or starting at the end of the reception of the
PPDU containing a frame for the non-AP STA from the AP affiliated with the AP MLD that does
not require immediate acknowledgement and this non-AP STA does not detect, within the PPDU
corresponding to the PHY-RXSTART.indication any of the following frames:
-
an individually addressed frame with the RA equal to the MAC address of the non-AP STA
affiliated with the non-AP MLD
-
a Trigger frame that has one of the User Info fields addressed to the non-AP STA affiliated
with the non-AP MLD
-
a CTS-to-self frame with the RA equal to the MAC address of the AP affiliated with the AP
MLD
-
a Multi-STA BlockAck frame that has one of the Per AID TID Info fields addressed to the
non-AP STA affiliated with the non-AP MLD
-
an NDP Announcement frame that has one of the STA Info fields addressed to the non-AP
STA affiliated with the non-AP MLD and a sounding NDP
•
The non-AP STA affiliated with the non-AP MLD that received the initial Control frame does
not respond to the most recently received frame from the AP affiliated with the AP MLD that
requires an immediate response after a SIFS.

## Slide 4: EMLSR vs NPCA
There are many differences between EMLSR and NPCA.
  EMLSR switching is triggered by EMLSR ICF on one of EMLSR links and NPCA switching is triggered by an inter-BSS transmission on the primary channel.
  After “switching”, the STA affiliated with the EMLSR MLD is a member of a TXOP but an NPCA non-AP STA shall access the wireless medium by using channel access procedure (include triggered by the AP) or wait for the DL transmission from the AP.
Which means
  Transmission may or may not happen on the NPCA PCH.
  Compared with EMLSR operation, Third-party STAs are more likely to interrupt NPCA operation after “switching”.
Therefore, NPCA operation cannot directly copy the switching back rules of EMLSR operation.

## Slide 5: Remaining Issues for NPCA switch back
The transmission initiated on the NPCA PCH still needs to run the channel access procedure, it can be blocked by other transmissions.
NPCA AP and NPCA non-AP STA may have different views on the channel. [1]
  Both of them may do NPCA switching independently while the other does not. The one switching to NPCA PCH may
    Try to transmit to the other with no ACK for it.
    Wait for the other transmitting to it.
Even some contributions have proposed solutions from the perspective of avoiding useless transmissions or switches [1-3] ,designing switch back rules that can recognize useless switches is beneficial.

## Slide 6: Switching back for NPCA
The end time of NPCA duration should be taken into consideration.
But it is unwise for a NPCA STA to stay on the NPCA PCH until the end of NPCA duration (the basic NAV expires on the primary channel).
  The TXOP on the primary channel might be truncated.
  There might be another OBSS transmission to refresh the NAVSync Timer.
NPCA switching back rules should take them into consideration.
  A simple solution: if the time left is less than a NPCA Transmission Threshold, the STA and AP switch back; otherwise, the STA and AP may keep retrying. [4]
  Another solution : immediately when NPCA STA detects that a peer NPCA STA (AP or non-AP STA) is on primary channel. [5]

## Slide 7: Switching back for NPCA
Both of solutions are attractive, based on them, we proposed that a NPCA STA that has switched to the NPCA PCH should initial switch back to the BSS primary channel
  When there are no frame exchanges it participates in and it recognizes the remainder time of NPCA duration is or will be less than the NPCA Transmission Threshold.
    There might be 2 options for a NPCA STA to determine that the remaining time is insufficient.
    These 2 options can be combined, meaning that the option whose conditions are met first will be applicable
  After frame exchange with the peer NPCA STA on the NPCA PCH (another time threshold may be needed) .
  There is no response to the NPCA ICF it transmitted.

## Slide 8: Option 1
Option 1. The time from the current time to the end of NPCA duration is less than the threshold.
  This still applies even when unknown interference signals are detected on the NPCA PCH.

## Slide 9: Option 2
Option 2. The time from the end of PPDU/TXOP to the end of NPCA duration is less than the threshold.
  In this option, the specific switch back time (point) is not clearly defined, as it depends on when the STA recognizes that the remaining time is insufficient.
  When it decode part of OBSS PPDUs on the NPCA PCH, it can initial switch back procedure .
  It should ensure finishing the NPCA switching back before the end of this OBSS PPDU/TXOP or before the end of NPCA duration.

## Slide 10: Conclusion
This contribution presents discussions on the NPCA switch back.
NPCA operation cannot directly copy the switching back rules of EMLSR operation.
It is benefit for a NPCA STA on the NPCA PCH to switch back to the primary channel early when there is less chance to access the medium on the NPCA PCH and do data transmission.
We proposed some NPCA switch back rules and an optional enhancement for the NPCA Transmission Threshold.

## Slide 11: References
[1] 11-23/2005r1, “Non-primary channel access (NPCA)”, Minyoung Park et al.
[2] 11-24/670r2, “Different view problems of NPCA”, Sanghyun Kim et al.
[3] 11-24/1093r3, “Special scenarios in Non-Primary Channel Access”, Sindhu Verma et al.
[4] 11-25/538r2, “cc50-cid-1780-discussion-on-npca-switch-back”, Chaoming Luo et al.
[5] 11-25/893r0, “Remaining Issue for NPCA”, Jeongki Kim et al.