## Slide 1: Considerations on UHR Critical Update
Date: 2025-07-04
Authors:

## Slide 2: Background – EHT critical update
BSS Parameters Change Count (BPCC) and Critical Update Flag (CUF) were introduced in EHT for AP MLD to indicate critical updates to non-AP MLD
  BPCC is per link and gets incremented when a critical update occurs
  CUF is set to 1 until and including the next DTIM Beacon if BPCC of any link changes
Non-AP STA can use BPCC and CUF in Beacon / Probe Response to learn if critical update has occurred
  Non-AP STA needs to retrieve critical update (e.g., by receiving Beacon / Probe Response, sending Probe Request) if BPCC has changed
  CUF can be used as an early indication of whether BPCC has changed

## Slide 3: Problem statement
Current spec does not specify whether a critical update is related to EHT/HE/VHT/… features
  In other words, critical update events are indifferent to the generation to which the update belongs
In UHR, many new features will be introduced and corresponding critical updates will be defined
  e.g., enablement / disablement / parameter update of NPCA, AP DPS, AP PUO, P-EDCA, DSO, …
  future generations will define even more new critical updates
  BPCC gets incremented and CUF is set to 1 if any of the above features gets an update
With these new critical updates being defined, legacy non-AP STAs will notice critical updates happening very frequently, but only find irrelevant update after retrieving them
Therefore, it is beneficial to be able to distinguish UHR (and post-UHR) critical updates from pre-UHR critical updates
  such that a STA can ignore irrelevant critical updates and save the efforts to retrieve those updates

## Slide 4: Problem statement
Desired properties of the design for distinguishing UHR (and post-UHR) critical updates from pre-UHR critical updates
  Reducing false positive: STAs retrieves update info only for critical updates relevant to them
  Forward compatibility: better to avoid a similar problem that will appear in the future, by distinguishing UHR critical updates from post-UHR critical updates
  Per-link indication: indication of critical update is per-link such that STAs only need to retrieve update info on updated link(s)
  Similar to existing EHT design: follow the design of EHT critical update with minimal changes
Example scenario to consider
  AP MLD has UHR critical update on link 1, and post-UHR critical update on link 2
  EHT STAs on both links are supposed to ignore the critical updates above
  UHR and post-UHR STAs on link 1 are supposed to retrieve update info of link 1
  Post-UHR STAs on link 2 are supposed to retrieve update info of link 2

## Slide 5: Proposal: new counters for UHR/post-UHR
To address the previously mentioned challenges, we propose to define new critical update counter(s) for UHR and post-UHR generations
  UHR/post-UHR STAs should be able to determine whether a relevant critical update has occurred on a link by checking newly defined counter(s)
Option 1) all UHR and post-UHR generations share a common counter per link (UHR BPCC)
  If a critical update relevant to UHR or post-UHR occurs, UHR BPCC gets incremented
  A device maintains UHR BPCC for each link
Option 2) each generation (Gen X) starting from UHR has its own counter per link (GenXBPCC)
  If a critical update relevant to Gen X occurs, GenXBPCC gets incremented
    X = 1, 2, 3, …, where Gen 1 corresponds to UHR
  A device maintains GenXBPCC up to its own generation
    e.g., UHR STA (Gen1 STA) maintains Gen1BPCC, Gen 2 STA maintains Gen1BPCC and Gen2BPCC, Gen 3 STA maintains Gen1BPCC, Gen2BPCC and Gen3BPCC, …

## Slide 6: Proposal: Gen Indicator per link (option 1)
We propose to include Gen Indicator with the counter to indicate the generation of critical update(s)
In option 1), Gen Indicator indicates generation X, and it is generation X’s update that causes UHR BPCC to increment
  Gen X corresponds to the earliest generation of critical on that link starting from UHR
    If critical updates belonging to multiple generations happen on one link, X corresponds to the earliest gen
  UHR BPCC (e.g., 8 bits) indicates the critical update counter starting from UHR on that link
  Gen Indicator (e.g., 3 bits) indicates the value of X on that link
    By checking Gen Indicator, STAs can identify the earliest generation of update on that link
    On different links, Gen Indicator can be set to different values (e.g., X on link 1, Y on link 2, Z on link 3, …)
  If no critical update on that link during the latest (DTIM) Beacon interval
    Gen Indicator keeps unchanged (same as the value in the last (DTIM) Beacon interval)

## Slide 7: Proposal: Gen Indicator per link (option 2)
We propose to include Gen Indicator with the counter to indicate the generation of critical update(s)
In option 2), Gen Indicator indicates generation X, and it is generation X’s counter (GenXBPCC) that is carried
  Gen X corresponds to the earliest generation of critical on that link since UHR
    If critical updates belonging to multiple generations happen on one link, X corresponds to the earliest gen
  GenXBPCC (e.g., 8 bits) indicates the critical update counter of Gen X carried for that link
    Only one counter per link is required to be carried at a time (in Beacon)
    Counters that does not correspond to Gen X are maintained locally but not carried this time
  Gen Indicator (e.g., 3 bits) indicates the value of X on that link
    By checking Gen Indicator, STAs can identify which counter is carried at the location of GenXBPCC
    On different links, Gen Indicator can be set to different values (e.g., X on link 1, Y on link 2, Z on link 3, …)
  If no critical update on that link during the latest (DTIM) Beacon interval
    Gen Indicator keeps unchanged (same as the value in the last (DTIM) Beacon interval)

## Slide 8: Proposal (cont’d): Gen Indicator per link
If a Gen Y (Y≥X) non-AP STA finds Gen Indicator = X and the new counter (UHR BPCC or GenXBPCC) has changed, the STA shall attempt to retrieve Gen X ~ Y critical updates for that link
  By receiving Beacon / Probe Response, or sending Probe Request
  Note that Gen X critical update is relevant to Gen X or later-gen STAs
  A UHR Critical Update Flag (e.g., 1 bit) can be defined, similar to CUF in 11be
    If the new counter for any link gets incremented, UHR CUF is set to 1 until the next DTIM Beacon
Location for carrying <new counter, Gen Indicator> in Beacon
  Common Info field of Basic ML element for reporting AP; RNR for reported AP(s)
  Newly defined element as a container can also be considered

## Slide 9: Examples (option 1)
1) Gen 1 (UHR) AP MLD has two links, only link 1 has critical update related to Gen 1
  UHR BPCC incremented and Gen Indicator = 1 for link 1
  UHR BPCC and Gen Indicator unchanged (from the update last time) for link 2
  UHR and post-UHR STAs on link 1 determine a Gen 1 critical update occurs and attempt to retrieve Gen 1 update
  STAs on link 2 find UHR BPCC unchanged, so no action is required
2) Gen 2 AP MLD has two links, and it has Gen 1 (UHR) critical update on link 1, and Gen 2 (e.g., Wi-Fi 9) critical update on link 2
  UHR BPCC incremented and Gen Indicator = 1 for link 1
  UHR BPCC incremented and Gen Indicator = 2 for link 2
  UHR/post-UHR STAs on link 1 determine a UHR critical update occurs and attempt to retrieve the Gen 1~2 update
  UHR STAs on link 2 find Gen Indicator = 2, so no action is required
  Gen 2 STAs on link 2 determine a Gen 2 critical update occurs and attempt to retrieve the Gen 2 update

## Slide 10: Examples (option 2)
1) Gen 1 (UHR) AP MLD has two links, only link 1 has critical update related to Gen 1
  Gen1BPCC incremented and carried in Beacon, and Gen Indicator = 1 for link 1
  GenXBPCC and Gen Indicator unchanged (from the update last time) for link 2
  UHR and post-UHR STAs on link 1 determine a Gen 1 critical update occurs and attempt to retrieve Gen 1 update
  STAs on link 2 find GenXBPCC unchanged or Gen Indicator is not relevant to them, so no action is required
2) Gen 2 AP MLD has two links, and it has Gen 1 (UHR) critical update on link 1, and Gen 2 (e.g., Wi-Fi 9) critical update on link 2
  Gen1BPCC incremented and carried in Beacon, and Gen Indicator = 1 for link 1
  Gen2BPCC incremented and carried in Beacon, and Gen Indicator = 2 for link 2
  UHR/post-UHR STAs on link 1 determine a UHR critical update occurs and attempt to retrieve the Gen 1~2 update
  UHR STAs on link 2 find Gen Indicator = 2, so no action is required
  Gen 2 STAs on link 2 determine a Gen 2 critical update occurs and attempt to retrieve the Gen 2 update

## Slide 11: Additional considerations
For option 2), all counters are present in the same frame if
  The frame is Probe Response frame
  The frame is (Re)Association / UHR Link Reconfiguration Response frame
  Note: since Probe Response and (Re)Association Response do not have bloating issue, all counters can be provided for complete information
Comparison between option 1) and 2)
  In both options, one pair of <new counter, Gen Indicator> per link is carried in Beacon
  Option 1) is simpler by using a common counter starting from UHR, whereas Option 2) provides more accurate information about each generation’s update
When a transmitted BSSID AP is reporting UHR/post-UHR critical update of a nontransmitted BSSID AP in its multiple BSSID set, a similar design can be adopted except for indication location
  <new counter, Gen Indicator> for nonTxBSSID AP will be carried in Nontransmitted BSSID Profile subelement
  <new counter, Gen Indicator> for other APs affiliated with the same AP MLD as nonTxBSSID AP will be carried in RNR

## Slide 12: References
[1] 24-1880r1: Solutions for beacon bloating, Reza Hedayat
[2] 24-1888r0: Light beacon consideration, Liwen Chu