## Slide 1: Discussion on CID 757
Date: 2025-07-09
Authors:

## Slide 2: Abstract
This submission addresses different options to resolve comment CID 757, that reads:
Comment | Proposed change
The STA is assigned to the default group if it does not express a group preference, but the STA has no way to discover the groups before (re)assoc, which is an issue especially for fast roaming. | Design a mechanism for the associated STA to learn about the neighboring APs and their groups to faciliate roaming

## Slide 3: Possible solutions
The objective is to provide information to STAs regarding epochs available in neighboring APs.
  Minimum information required is the Group ID and the Epoch Interval. The Group ID may be omitted if only default group is advertised (Group ID 0).
  Just one group or a list of groups?
Two mechanisms are already defined which may be used for this purpose
  Neighbor Report
  Reduced Neighbor Report

## Slide 4: Neighbor Report
We can modify the BSSID Information field by using one reserved bit to signal EDP information
We can create a new EDP Subelement containing EDP information, such as Group ID/Epoch Interval or a complete EDP element/list

## Slide 5: Reduced Neighbor Report
We can add information on the Group ID/Epoch Interval to the TBTT Information Set
We can use the TBTT Information field when TBTT Information Field Type subfield is equal to 0 or to 1

## Slide 6: TBTT Information field when TBTT Information Field Type subfield is equal to 0
Need to agree on what is the minimum info to be added to the RNR
Fit it in an already crowded 9-328 table
EDP

## Slide 7: TBTT Information field when TBTT Information Field Type subfield is equal to 1
TBTT Information Length subfield value | TBTT Information field contents
0-1 | Reserved
2 | The EBCS Info Frame Tx Countdown field as defined in 9.4.1.70 (EBCS Info Frame Tx Countdown field)
3 | MLD Parameters
4-7 | Reserved
8 | MLD Parameters and the EDP element.
9-255 | Reserved
Table 9-330—TBTT Information field contents when TBTT Information Field Type subfield equal to 1
 | EBCS Info Frame Tx Countdown field | MLD Parameters | EDP Parameters
Octets | 0 or 2 | 0 or 3 | 0 or 5 (GroupID and Epoch Interval)
Figure 9-734b—TBTT Information field format when the TBTT Information Field Type sub-field is equal to 1
These tables are a recap from .11-2024 and .11be, since there is no single table with everything
Much easier to add it to the case of TBTT Information Field Type subfield = 1
It is already been used by the MLD Parameters