## Slide 1: IMMW Channel Bandwidth and Throughput Discussions
Date: 2025-07-03
Authors:

## Slide 2: Introduction
The Integrated mmWave PAR [1] and other contributions [2] define ways use existing 802.11 physical layer
The mmWave band allows to have wider channels and then to produce a more predictable multigigabit throughput
In this presentation, we share some analysis and thoughts on the use of the mmWave band to better align it with future FTTx technologies.

## Slide 3: FTTx and WLAN Throughput evolution
Can we increase WLAN single user throughput?
Maximum capacity of new FTTH technologies exceed present day WLAN system throughput
There is a need to have a 2x2 MIMO WLAN with significant 10Gbps coverage

## Slide 4: MMW WLAN
Advantages
Extremely high capacity possible up to 60Gbps with 2x2 MIMO
Extremely low latency (ms range)
Lower impact of contention effects and interference for indoor systems

## Slide 5: MCS and channel bandwidth at 60GHz
Thoughts about the maximum useful MCS level
MCS | Modulation
0 | BPSK1/2
1 | QPSK1/2
2 | QPSK3/4
3 | 16-QAM1/2
4 | 16-QAM3/4
5 | 64-QAM2/3
6 | 64-QAM3/4
7 | 64-QAM5/6
8 | 256-QAM3/4
9 | 256-QAM5/6
10 | 1024-QAM3/4
11 | 1024-QAM5/6
Channel Bandwidth (MHz) | Maximum MCS at 50cm | Maximum MCS at 100cm
320 | 11 | 9
640 | 10 | 8
1280 | 9 | 7
2560 | 8 | 7
5120 | 7 | 4
Free space propagation at 60GHz

## Slide 6: 60GHz Channel bandwidth
Approaching FTTx Maximum Throughput
Channel bandwidth | 320MHz | 640MHz | 1280MHz | 2560MHz | 5120MHz
Data subcarriers | 117 | 236 | 475 | 953 | 1909
Subcarrier spacing | 2.5MHz | 2.5MHz | 2.5MHz | 2.5MHz | 2.5MHz
FFT | 128 | 256 | 512 | 1024 | 2048
Guard interval | 18ns | 18ns | 18ns | 18ns | 18ns
Maximum number of channels available in 60GHz (57.24 – 74.52) | 54 | 27 | 13 | 6 | 3
Estimated maximum capacity @ 2x2 MIMO, distance = 50cm. | 3.7Gbps | 7.5Gbps | 15.1Gbps | 30.3Gbps | 60.8Gbps

## Slide 7: MMW Throughput happens inside the room
Maximum capacity vs propagation
Conditions:
Free space propagation
Tx power: 10dBm
Antenna gain: 10dBi

## Slide 8: Room coverage estimation - 16m2
Effect of the channel bandwidth
Assumptions: House 150 m2, average 16 m2 rooms, 20dB wall attenuation.
2x2 MIMO for different channel bandwidths at 62GHz
For a single user performance objective of 10Gbps, to have 80% coverage we need 5120 MHz channel
320
640
1280

## Slide 9: Preliminary takeaways
mmW phy layer
60GHz bands could have several channel bandwidths from 320MHz to 5.12GHz.
IEEE802.11bq could eliminate possible gap between future FTTx systems and WLAN throughput
Single user 10Gbps throughput will require 5.12GHz channels to have significant room coverage

## Slide 10: SP
We propose that the IMMW PHY channel bandwidth is extended up to 5120MHz to align with FTTx capacity

## Slide 11: References
[1] P802.11bq_PAR, https://www.ieee802.org/11/PARs/P802.11bq_PAR.pdf
[2] 11-24-0853r1 -immw tone plan discussions
[3] Recommendation ITU-R P.2040-3 (08/2023) P Series: Radiowave propagation Effects of building materials and structures on radiowave propagation above about 100 MHz
[4] IEEE 802.11-2015/0625r2 IEEE 802.11 TGay Use Cases
[5] IEEE Std 802.11ay -2021 enhanced throughput for Operations in License-exempt Bands above 45GHz