## Slide 1: A Dynamic Coordinated Decision Mechanism for NPCA Switch-Back
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd |  |  | chehui@ruijie.com.cn
Fachang Guo | Ruijie Networks Co., Ltd |  |  | 
Longlong Hong | Ruijie Networks Co., Ltd |  |  | 
Yongning Ke | Ruijie Networks Co., Ltd |  |  | 
Hang Yang | Ruijie Networks Co., Ltd |  |  | 
Date: 2025-07-10
Authors:

## Slide 2: Abstract
Background of NPCA:
The existing 802.11bn Draft defines conditions for NPCA STAs to switch from the BSS Primary Channel (PCH) to the NPCA Primary Channel (NPCH) upon detecting OBSS interference, including bandwidth, minimum duration thresholds, buffer status, and TA info in OBSS PPDUs. However, the switch-back conditions from NPCH to PCH remain a critical issue for 802.11bn.
Related Motions in 802.11bn SFD:
Current discussions on switch-back focus on delay and parameter reset:
[Motion #124]: NPCA STAs must indicate switch delay (PCH→NPCH) and switch-back delay (NPCH→PCH), with delays ranging 0-252 μs (4 μs resolution).
[Motion #126]: TXOP initiation on NPCH follows EDCA rules but resets CW_NPCA[AC] and backoff counters when switching to NPCH.
Key Issues:
Asymmetric OBSS interference detection between APs and STAs leads to mismatched OBSS NAVs, causing invalid transmissions, decoding failures, and signaling storms in dense scenarios.
Proposal:
A dynamic coordinated decision mechanism where APs collect STAs’ OBSS NAVs via OBSS Info ICF/ICR frames, then decide a unified switch-back time, reducing inefficiencies and improving channel utilization.

## Slide 3: Asymmetric OBSS NAV Scenario in NPCA Switch-Back
APs and STAs initiate NPCA operations triggered by different OBSS TXOPs, and the OBSS NAVs they obtain may differ, meaning the times to switch back to the original primary channel may vary.
Mismatched Switch-Back Timing:
If a non-AP STA switches back to PCH earlier than the AP, it may initiate invalid transmissions on PCH.
If an AP switches back earlier than STAs, STAs on NPCH may do invalid transmissions and lose medium synchronization.
Post-Switch-Back Interference:
Non-AP STAs switching back to PCH based on AP’s OBSS end time may face unresolved OBSS interference, blocking uplink transmissions and causing downlink decoding failures.
Signaling Overhead in Dense Scenarios:
Frequent OBSS NAV exchanges between APs and numerous STAs trigger signaling storms, increasing AP decision delay and reducing throughput.
STA2 may initiate invalid transmissions on the PCH.
STA1 may initiate invalid transmissions on NPCH, causing medium loss.
After STA1 switches back to the PCH, it’s OBSS traffic still exists. STA1 cannot initiate uplink transmission on the PCH and may incorrectly decode downlink data.

## Slide 4: Limitations of Existing Solutions
Existing Method 1:
The AP can transmit Delivered Info in the NPCA ICF frame, including the remaining time the AP will stay on the NPCA primary channel (duration) or the end time of OBSS traffic observed by the AP (end time).
If a STA sends an NPCA ICF, it needs to request this information, and the AP shall include such information in the NPCA ICR frame.
Method 1 uses the OBSS NAV observed by the AP as the condition for returning to the PCH, without considering the OBSS NAV on the STA side. This may lead to issues where OBSS interference persists after the STA switches back to the BSS channel, resulting in downlink data decoding failures or uplink transmission blockages.
Existing Method 2:
Option 1: Restrict the TXOP holder in NPCA to the AP only.
Option 2: When the AP acts as a TXOP responder, use ICR to indicate the duration of its NPCA operation, and non-AP STAs end their TXOP based on the duration in the ICR.
Method 2 is restricted to AP-centric modes, limiting operational flexibility.

## Slide 5: Proposed Dynamic Coordinated Decision Mechanism
APs dynamically collect OBSS NAV information from associated STAs, synthesize a unified switch-back time, and broadcast it to all STAs. This aligns switch-back timing and reduces inefficiencies.
The AP and its associated STAs exchange OBSS NAV information through OBSS Info ICF and OBSS Info ICR frames. To reduce signaling overhead in high-density scenarios, the following methods can be adopted:
Dynamic sampling: The AP randomly selects or selects STAs for OBSS NAV interaction based on certain criteria (such as buffer status). OBSS NAV interaction can be performed via polling or OFDMA.
Threshold triggering: The AP notifies the threshold of the reported OBSS NAV, and STAs that meet the threshold conditions report the OBSS NAV by the Uplink OFDMA Random Access (UORA).
The AP comprehensively decides the time to switch back to the PCH based on its own OBSS NAV and the OBSS NAVs from the STAs, and broadcasts the decided switch-back time to each STA. Both the AP and STAs switch back to the PCH according to the broadcast switch-back time.

## Slide 6: Implementation Flow
Information Collection:
AP sends OBSS Info ICF, requesting STAs’ OBSS NAVs (with sampling/threshold rules).
Qualified STAs respond with OBSS Info ICR containing their OBSS NAVs.
Decision Making:
AP integrates its OBSS NAV and STAs’ reports to determine the earliest feasible switch-back time (ensuring minimal post-switch interference).
Execution:
AP broadcasts the unified switch-back time to all STAs.
AP and STAs switch back to PCH simultaneously at the designated time.

## Slide 7: Conclusion
Current NPCA switchback rules lack coordination for asymmetric OBSS NAV
Proposed mechanism:
OBSS Info ICF/ICR for distributed NAV collection
AP-driven coordinated switch-back time (CST) calculation for synchronized switchback
Sampling/threshold triggers to optimize signaling

## Slide 8: References
[1] 11-24-1596-01-00bn, “Consideration of MAP coordination on NPCA channel”, ZTE, 2024
[2] 11-25-0538-00-00bn, “Discussion on NPCA switch back”, OPPO, 2025
[3] 11-25-0893-00-00bn, “Remaining Issue for NPCA”, Ofinno, 2025
[4] 11-25-1089-00-00bn, “Discussion on NPCA switch back”, Spreadtrum, 2025