## Slide 1: ACK Message in Time-Slot Based Channel Access for Active AMP STAs
Date: 2025-07-11
Authors:

## Slide 2: Abstract
To enhance efficiency of time-slot based channel access for active TX AMP STAs, we propose to define Sync signals indicating the beginning of each slot so that they carry the binary information "Ack/Nack" for the transmission that occurred in the previous slot.

## Slide 3: Background
  Converging to a time-slot based access mechanism for Active AMP non-AP STAs to transmit UL traffic
  [1] proposes a slot SYNC signal to indicate the beginning of each slot
  [1] proposes NACK in the following TXOP AMP ReTx-Poll
  [2] compares the pros and cons of Acking each frame inside the slot or using Block Acks at the end of the last slot

## Slide 4: Challenges with proposed Acking Mechanisms
Mechanism | Pros | Cons
AMP ACK in slot | ACK is sent immediately AMP non-AP STA can enter sleep immediately after the ACK | ACK Overhead in each slot Less slots in each trigger session
Block ACK | Single ACK for all slots in the trigger session | STA non-AP STA needs to keep awake or wake up again at the end of the trigger session
NACK in the following trigger frame | No ACK overhead at all | Assumption the non-AP STA are awake at the next trigger session

## Slide 5: Motivation
ACK overhead:
  AMP data frames being very short, ACK frames represent a big overhead
ACK ASAP:
  AMP non-AP STA might not have enough power to listen until the end of the TXOP after transmitting
  AMP non-AP STA might not have enough power to wake up again at the next Trigger frame after a transmission

## Slide 6: Proposal
Merge slot SYNC [1] and ACK in a unique short PHY frame
Two possibilities:
  Define two different slot SYNC signals – one represents SYNC+ACK, the other one is SYNC+NACK (used if no frame was received or correctly decoded by the AMP AP in the previous slot)
    Rough Example To Illustrate the concept
      SYNC+ACK: 1100110011
      SYNC+NACK: 0110011001
  Extend a single slot SYNC message with a new field one bit long carrying the ACK information.
  Rough Example to illustrate the concept:
    SYNC+ACK: 11001100111
    SYNC+NACK: 11001100110

## Slide 7: Last Slot Ack
Last Slot could be ack-ed in the same way (slot Sync + ACK). As the AMP trigger contained the number of slots, AMP non-AP STA are aware this last sync signals the end of the trigger session
Alternatively, an AMP-ACK frame could be used for the last slot.

## Slide 8: Proposal Example
AMP Reader
AMP non-AP STA-1
AMP non-AP STA-2
AMP non-AP STA-3
AMP non-AP STA-4
CTS
To Self
AMP Trigger
Slot Sync+ACK
Slot Sync+NACK
UL Data
UL Data
UL Data
UL Data
Slot Sync+ACK
Slot Sync+NACK
Indicates 4 slots
Slot 0
Slot 1
Slot 2
Slot 3
AMP Trigger

## Slide 9: Advantages
The AMP non-AP STA that has transmitted a frame receives the ACK immediately after its transmission, enabling it to sleep again for a longer time
The ACK/NAK is not a complete frame (it does not need the MAC header) because it always refers to the previous slot making the overhead very limited.
In case of two different SYNC messages, the overhead is none.

## Slide 10: Summary
We examined pros and cons of current proposals to acknowledgment UL data from Active Tx non-AP STAs in the time-slot channel access trigger procedure
We proposed a new way to immediately acknowledge UL data frames:
  By defining two different slot-sync signals
  By adding a new symbol to a single slot-sync signal

## Slide 11: Straw Poll 1
Do you agree in defining a slot SYNC signal that indicates the beginning of a slot and carries acknowledgement information on the previous slot UL transmission?
  Yes
  No
  Abstain

## Slide 12: Straw Poll 2
Do you prefer defining?
  Two different sync messages (different patterns) for slot SYNC + ACK and slot SYNC + NACK
  One single sync message followed by a new symbol indicating acknowledgement or non-acknowledgement on the previous slot
  Abstain

## Slide 13: References
[1] https://mentor.ieee.org/802.11/dcn/25/11-25-0046-00-00bp-channel-access-for-active-tx-non-ap-amp-stas.pptx
[2] https://mentor.ieee.org/802.11/dcn/25/11-25-0859-00-00bp-amp-ack-frame.pptx