## Slide 1: Invite and Response Frame Design for Co-SR and Co-BF
Date: 2025-06-04
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Ross Jian Yu |  |  |  | 
Arik Klein |  |  |  | 

## Slide 2: Introduction
In previous discussions, it is proposed that Invite and Response frame exchange is needed before Co-SR and Co-BF transmission
This contribution discusses frame format design of the Invite and Response frames for Co-SR and Co-BF
Co-SR/Co-BF Invite Frame
Co-SR/Co-BF Response Frame
Co-SR/Co-BF Trigger Frame
Co-SR/Co-BF Data Transmission
Co-SR/Co-BF Data Transmission
Coordinating AP
Coordinated AP

## Slide 3: Recap – Co-BF contents in the Invite/Response frame
Category | Information
Control | ‘Co-BF Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Maximum Total Nss Allowed for shared AP
 | Number of Co-BF Users in sharing BSS
Per-User Info in Sharing BSS | STA ID
 | Nss
Category | Information
Control | ‘Co-BF Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier
 | Extra LTF Allowed
 | Number of CoBF Users in shared BSS
Per-User Info in Shared BSS | STA ID
 | MCS
 | Nss
 | 2xLDPC
The following PHY related contents of Co-BF Invite and Response frames have been agreed in Motion #327 and Motion #328

## Slide 4: Some other information needed (1)
ICF Required
  Indicates whether the AP needs to exchange ICF/ICR with its associated STAs before Co-BF/Co-SR transmission
  Needed in both Co-BF and Co-SR
  Needed in both Invite and Response frames
ICF/ICR duration
  Indicates the duration of the ICF/ICR exchange between the AP and its associated STAs before Co-BF/Co-SR transmission
  Needed in both Co-BF and Co-SR
  Needed in both Invite and Response frames
Suggested BW
  Indicates the suggested BW from the coordinated AP. Motivation: if the BW of the coordinated AP’s STA is smaller, then the coordinated transmission is still possible, if allowed by the coordinating AP
  Needed in both Co-BF and Co-SR
  Needed in the Response frame only
Flexible BW
  1 bit, indicates whether the coordinating AP allows a smaller BW suggested by the coordinated AP
  Needed in both Co-BF and Co-SR
  Needed in the Invite frame only

## Slide 5: Some other information needed (2)
Minimum acceptable TX power
  Indicates the minimum acceptable TX power to be used by the shared AP during Co-SR transmission.
  Needed in Co-SR
  Needed in the Response frame
ICR Length
  Indicates the length of the ICR frame if the ICF/ICR exchange between the AP and its associated STAs before Co-SR transmission
  Needed in Co-SR mode 1
  Needed in both Invite and Response frames
Number of LTF Symbols
  Indicate the number of LTF symbols intended to be transmitted to achieve symbol level alignment
  Needed in Co-SR
  Needed in both Invite and Response frames

## Slide 6: Summary of frame contents
Invite Frame |  | 
Information | Co-BF | Co-SR
‘Co-BF/Co-SR Invite’ | Y | 
Minimum Number of Data OFDM Symbols | Y | 
Maximum Number of Data OFDM Symbols | Y | 
PHY Version Identifier | Y | 
Bandwidth | Y | 
Punctured Channel Information | Y | 
GI+LTF Size | Y | 
Maximum Total Nss Allowed for shared AP | Y | N
Number of Co-BF Users in sharing BSS | Y | N
STA ID | Y | N
Nss | Y | N
ICF Required | Y | Y
ICF/ICR Duration | Y | Y
Flexible BW | Y | Y
ICR Length | N | Y
Number of LTF Symbols | N | Y
Response Frame |  | 
Information | Co-BF | Co-SR
‘Co-BF/Co-SR Acceptance’ | Y | 
Suggested Number of Data OFDM Symbols | Y | 
PHY Version Identifier | Y | 
Extra LTF Allowed | Y | N
Number of CoBF Users in shared BSS | Y | N
STA ID | Y | N
MCS | Y | N
Nss | Y | N
2xLDPC | Y | N
ICF Required | Y | Y
ICF/ICR Duration | Y | Y
Suggested BW | Y | Y
Minimum acceptable TX power | N | Y
ICR Length | N | Y
Number of LTF Symbols | N | Y

## Slide 7: Frame format - Invite Frame
The BSRP NTB frame is a good candidate as the Invite frame of Co-SR and Co-BF
Due to the large amount of parameters that are exchanged between the Coordinating AP and the Coordinated AP, more than one user info fields need to be used to carry the information needed for Co-SR/Co-BF Invite
Frame Control
Duration
RA
TA
Common Info
User Info
User Info
FCS
AID12
Feedback Type
Feedback Information
12
4
24
Set to 4~15
……
Bits:
Special User Info

## Slide 8: Frame format - Invite Frame
Regarding the format of the user info field, three options are under consideration
Option 1:
  All the user info fields have the same format: AID12 + Feedback Type + Feedback Information
Option 2:
  The first user info field has the format: AID12 + Feedback Type + Feedback Information,
  From the second user info field, the format is: Feedback Information
Frame Control
Duration
RA
TA
Common Info
User Info
User Info
FCS
AID12
Feedback Type
Feedback Information
12
4
24
Set to 4~15
……
Bits:
Special User Info
User Info
AID12
Feedback Type
Feedback Information
12
4
24
Feedback Information
40
Opt 1
Opt 2

## Slide 9: Frame format - Invite Frame
Regarding the format of the user info field, three options are under consideration
Option 3:
  All the user info fields have the same format: Feedback Information
  The Feedback Type field is carried in the Common Info field
  RA is set to the MAC address of the coordinated AP
Frame Control
Duration
RA
TA
Common Info
User Info
FCS
……
Special User Info
User Info
Feedback Information
40
Opt 3
Note-for all the options, some fields common to Co-SR and Co-BF can be moved to the Common Info/Special User Info fields

## Slide 10: Invite Frame Option 1 (Co-BF)
B0 B11 | B12 B15 | B16 B24 | B25 B33 | B34 B36 | B37 B39
AID12 | Feedback Type | Feedback Information |  |  | 
 |  | Minimum number of data OFDM symbols | Maximum number of data OFDM symbols | PHY Version Identifier | BW
B0 B11 | B12 B15 | B16 B31 | B32 | B33 B39
AID12 | Feedback Type | Feedback Information |  | 
 |  | Punctured Channel Information | ICF Required | ICF/ICR Duration*
1st user info field
2nd user info field
3rd user info field
B0 B11 | B12 B15 | B16 | B17 B18 | B19 B20 | B21 B22 | B23 B39
AID12 | Feedback Type | Feedback Information |  |  |  | 
 |  | Flexible BW | GI+LTF Size | Maximum Total Nss Allowed for shared AP | Number of Co-BF Users in sharing BSS | Reserved
* the need of this field depends on the choice of the frame exchange sequence

## Slide 11: Invite Frame Option 1 (Co-BF)
B0 B11 | B12 B15 | B16 B27 | B28 B29 | B30 B39
AID12 | Feedback Type | Feedback Information |  | 
 |  | STA ID | NSS | Reserved
If there are two or more users, then the 4th user info field is followed by the 5th user info field, (or, and the 6th user info field), each of them has the same format as the 4th user info field
4th user info field

## Slide 12: Invite Frame Option 2 (Co-BF)
1st user info field
2nd user info field
3rd user info field
B0 B10 | B11 B12 | B13 B23 | B24 B25 | B26 B36 | B37 B38 | B39
Feedback Information |  |  |  |  |  | 
STA ID 1 | NSS 1 | STA ID 2 | NSS 2 | STA ID 3 | NSS 3 | Reserved
B0 | B1 B7 | B8 | B9 B10 | B11 B26 | B27 B28 | B29 B30 | B31 B39
Feedback Information |  |  |  |  |  |  | 
ICF Required | ICF/ICR duration | Flexible BW | GI+LTF Size | Punctured Channel Information | Maximum Total Nss Allowed for shared AP | Number of Co-BF Users in sharing BSS | Reserved
B0 B11 | B12 B15 | B16 B24 | B25 B33 | B34 B36 | B37 B39
AID12 | Feedback Type | Feedback Information |  |  | 
 |  | Minimum number of data OFDM symbols | Maximum number of data OFDM symbols | PHY Version Identifier | BW

## Slide 13: Invite Frame Option 3 (Co-BF)
1st user info field
2nd user info field
3rd user info field
B0 | B1 B7 | B8 | B9 B10 | B11 B12 | B13 B14 | B15 B39
Feedback Information |  |  |  |  |  | 
ICF Required | ICF/ICR duration | Flexible BW | GI+LTF Size | Maximum Total Nss Allowed for shared AP | Number of Co-BF Users in sharing BSS | Reserved
B0 B8 | B19 B17 | B18 B20 | B21 B23 | B24 B39
Feedback Information |  |  |  | 
Minimum number of data OFDM symbols | Maximum number of data OFDM symbols | PHY Version Identifier | BW | Punctured Channel Information
B0 B10 | B11 B12 | B13 B23 | B24 B25 | B26 B36 | B37 B38 | B39
Feedback Information |  |  |  |  |  | 
STA ID 1 | NSS 1 | STA ID 2 | NSS 2 | STA ID 3 | NSS 3 | Reserved

## Slide 14: Invite Frame Option 1 (Co-SR)
B0 B11 | B12 B15 | B16 B24 | B25 B33 | B34 B36 | B37 B39
AID12 | Feedback Type | Feedback Information |  |  | 
 |  | Minimum number of data OFDM symbols | Maximum number of data OFDM symbols | PHY Version Identifier | BW
B0 B11 | B12 B15 | B16 B31 | B32 | B33 B39
AID12 | Feedback Type | Feedback Information |  | 
 |  | Punctured Channel Information | ICF Required | ICF/ICR Duration
1st user info field
2nd user info field
3rd user info field
B0 B11 | B12 B15 | B16 | B17 B18 | B19 B24 | B25 B27 | B28 B39
AID12 | Feedback Type | Feedback Information |  |  |  | 
 |  | Flexible BW | GI+LTF Size | ICR Length | Number of LTF Symbols | Reserved

## Slide 15: Invite Frame Option 2 (Co-SR)
2nd user info field
B0 B11 | B12 B15 | B16 B24 | B25 B33 | B34 B36 | B37 B39
AID12 | Feedback Type | Feedback Information |  |  | 
 |  | Minimum number of data OFDM symbols | Maximum number of data OFDM symbols | PHY Version Identifier | BW
1st user info field
B0 | B1 B7 | B8 | B9 B10 | B11 B26 | B27 B32 | B33 B35 | B36 B39
Feedback Information |  |  |  |  |  |  | 
ICF Required | ICF/ICR duration | Flexible BW | GI+LTF Size | Punctured Channel Information | ICR Length | Number of LTF Symbols | Reserved

## Slide 16: Invite Frame Option 3 (Co-SR)
2nd user info field
1st user info field
B0 | B1 | B2 B3 | B4 B19 | B20 B39
Feedback Information |  |  |  | 
ICF Required | Flexible BW | GI+LTF Size | Punctured Channel Information | Reserved
B0 B8 | B9 B17 | B18 B20 | B21 B23 | B24 B29 | B30 B32 | B33 B39
Feedback Information |  |  |  |  |  | 
Minimum number of data OFDM symbols | Maximum number of data OFDM symbols | PHY Version Identifier | BW | ICR Length | Number of LTF Symbols | ICF/ICR duration

## Slide 17: Frame format - Response Frame
The Multi-STA Block Ack frame is a good candidate as the Response frame of Co-SR and Co-BF
  One Per AID TID Information field is carried in the BA Information field
  A Status Code field can be put in the Block Ack Starting Sequence Control field
  Different values of the Feedback Type field are used to differentiate Co-BF and Co-SR
  The contents of the Response frame can be put in the Feedback field
Frame Control
Duration
RA
TA
BA Control
BA Information
FCS
Per AID TID Information
AID TID Info
Block Ack Starting Sequence Control
Feedback
AID11
ACK Type
TID
Set to 0
Set to 13
Frag. Number
Status Code
Feedback Type
4
8
4
Set to 4~15
0, 4, 8, 16, 32, 64, or 128

## Slide 18: Response Frame (Co-BF)
Contents in the Feedback field
Feedback
PHY Common Info
Per-User Info
……
Per-User Info
PHY Common Info |  |  |  |  |  |  | 
B0 B8 | B9 B11 | B12 | B13 | B14 B20 | B21 B22 | B23 B25 | B26 B31
Suggested Number of Data OFDM Symbols | PHY Version Identifier | Extra LTF Allowed | ICF required | ICF/ICR duration | Number of Co-BF Users in shared BSS | Suggested BW | Reserved
Per-User Info |  |  |  | 
B0 B11 | B12 B15 | B16 B17 | B18 | B19 B23
STA ID | MCS | NSS | 2xLDPC | Reserved

## Slide 19: Response Frame (Co-SR)
Contents in the Feedback field
Feedback |  |  |  |  |  |  |  | 
B0 B8 | B9 B11 | B12 B17 | B18 | B19 B25 | B26 B28 | B29 B34 | B35 B37 | B38 B39
Suggested Number of Data OFDM Symbols | PHY Version Identifier | Minimum acceptable TX power | ICF required | ICF/ICR duration | Suggested BW | ICR Length | Number of LTF Symbols | Reserved

## Slide 20: Summary
We propose the contents and frame formats of Co-BF/Co-SR Invite and Response frames

## Slide 21: SP
Which option do you prefer as the frame format for the Co-BF/Co-SR Invite frame as listed in slide 8~9?