## Slide 1: Thoughts on PPDU-based NPCA
Date: 2025-09-08
Authors:

## Slide 2: Introduction
In NPCA PDT [1] and 11bn D1.0 [2], two types of NPCA are defined
  PPDU-based NPCA (PHYLEN NPCA)
  TXOP-based NPCA (MOPLEN NPCA)
Both types of NPCA can be triggered by
  OBSS Control frame exchange
  OBSS HE/EHT/UHR PPDU
If NPCA is triggered by OBSS Control frame exchange, switch time is at the third PPDU following ICF + ICR
  In PPDU-based NPCA, NPCA duration is based on length of the third PPDU
  In TXOP-based NPCA, NPCA duration is based on Duration indicated in ICF
In this contribution, we discuss inefficiency of PPDU-based NPCA triggered by OBSS Control frame exchange and possible options for optimization

## Slide 3: Motivation
If PPDU-based NPCA is triggered by OBSS control frame exchange, NPCA gain may be limited
  If pre-HE OBSS PPDUs follow ICF+ICR, NPCA can only be performed during the first data PPDU
  The following pre-HE data PPDUs in OBSS TXOP will not trigger NPCA under existing rules
  After switching back to primary channel (PCH), AP and STA have to wait until OBSS TXOP end before contending the channel again
RTS
CTS
VHT PPDU
BA
VHT PPDU
BA
OBSS TXOP duration
DL PPDU
P20
NPCA
P20
ICF
ICR
BA

## Slide 4: Motivation (cont’d)
AP and STA could perform PPDU-based NPCA during the pre-HE OBSS PPDUs after switching back to PCH
  Under the condition that OBSS TXOP is not early terminated (CF-End is not detected on PCH)
  The same NPCA Minimum Duration Threshold can be used
  New rules can be introduced for switching to NPCA primary channel (NPCH)
RTS
CTS
VHT PPDU
BA
VHT PPDU
BA
OBSS TXOP duration
DL PPDU
P20
NPCA
P20
ICF
ICR
BA
possible for another round of PPDU-based NPCA

## Slide 5: PPDU-based NPCA in OBSS TXOP – option 1
In an OBSS TXOP protected by OBSS ICF + ICR, PPDU-based NPCA can be triggered by a pre-HE PPDU under the following conditions:
  Basic NAV set by OBSS ICF is nonzero and has not been reset
  PPDU end time is earlier than the expiration time of basic NAV timer
  Length and bandwidth of the PPDU satisfy NPCA requirements
Additional considerations
  No need for checking BSS color or RA/TA field of the PPDU
  Switch time can be 3 OFDM symbols after reception of L-SIG field of the PPDU (NPCA NHT switch time)
  If OBSS TXOP is early terminated, AP/STA will be able to detect CF-End on PCH, since AP/STA needs to switch back to PCH by the end of PPDU triggering NPCA
  For robustness, this rule can be applied only after the STA has been triggered PPDU-based NPCA and switches back to PCH in this OBSS TXOP

## Slide 6: Example of option 1
RTS
CTS
VHT PPDU
BA
VHT PPDU
BA
OBSS TXOP duration
DL PPDU
P20
NPCA
P20
ICF
ICR
BA
DL PPDU
ICF
ICR
BA
(pre-HE) PPDU triggers NPCA when basic NAV is nonzero

## Slide 7: PPDU-based NPCA in OBSS TXOP – option 2
In an OBSS TXOP protected by OBSS ICF + ICR, PPDU-based NPCA can be triggered by a sequence of OBSS BA + a following PPDU, under the following conditions:
  OBSS BA and the PPDU is separated by SIFS time
  Basic NAV set by OBSS ICF is nonzero and has not been reset
  PPDU end time is earlier than the expiration time of basic NAV timer
  Length and bandwidth of the PPDU satisfy NPCA requirements
OBSS BA checking + SIFS separation ensures that the PPDU is from the same OBSS as the BA
Additional considerations
  Switch time can be 3 OFDM symbols after reception of L-SIG field of the PPDU (NPCA NHT switch time)
  If OBSS TXOP is early terminated, AP/STA will be able to detect CF-End on PCH, since AP/STA needs to switch back to PCH by the end of PPDU triggering NPCA

## Slide 8: Example of option 2
RTS
CTS
VHT PPDU
BA
VHT PPDU
BA
OBSS TXOP duration
DL PPDU
P20
NPCA
P20
ICF
ICR
BA
DL PPDU
ICF
ICR
BA
OBSS BA + following PPDU triggers NPCA

## Slide 9: Conclusion
In this contribution, we have discussed possible inefficiency of PPDU-based NPCA triggered by OBSS Control frame exchange
Two options are proposed to improve the gain of PPDU-based NPCA within an OBSS TXOP
  option 1) NPCA can be triggered by a pre-HE PPDU while basic NAV is nonzero
  option 2) NPCA can be triggered by OBSS BA + a following PPDU separated by SIFS
In both options, channel utilization can be improved by allowing more time for NPCA during OBSS TXOP

## Slide 10: References
[1] 11-25-0936-15-00bn-pdt-cr-mac-npca-cc50, Matthew Fischer
[2] Draft P802.11bn_D1.0

## Slide 11: SP
Do you support to add the following text to the 11bn SFD?
  After the NPCA operation induced by a sequence of ICF, ICR, and a third PPDU is completed, subsequent PPDUs received within the valid OBSS TXOP can trigger NPCA operation under the following conditions:
    Basic NAV is nonzero
    The end time of the PPDU is earlier than the expiration time of basic NAV timer
    The bandwidth of the PPDU does not overlap with the NPCA primary channel
    The remaining duration of the PPDU is larger than NPCA Minimum Duration Threshold