## Slide 1: NPCA considering OBSS ICF type
Date: 2025-07-18
Authors:

## Slide 2: Introduction
In NPCA PDT [1], two types of NPCA are defined
  PPDU-based NPCA (PHYLEN NPCA) – NPCA duration is based on PPDU length
  TXOP-based NPCA (MOPLEN NPCA) – NPCA duration is based on TXOP length
Both types of NPCA can be triggered by
  OBSS Control frame exchange
  OBSS HE/EHT/UHR PPDU
OBSS Control frame exchange can be
  RTS / MU-RTS + CTS
  BSRP + QoS Null
  BSRP NTB + M-BA
In this contribution, we discuss NPCA rules to consider if specific OBSS ICF/ICR is detected

## Slide 3: NPCA considering DUO ICF
If ICF by OBSS AP solicits unavailability info from an OBSS STA, OBSS AP may early terminate the TXOP before STA unavailability start time
If TXOP-based NPCA is triggered, AP/STA will stay on NPCH until TXOP end indicated in ICF, thus cannot detect CF-End sent by OBSS and may lose medium sync on PCH
OBSS ICF can be BSRP or BSRP NTB in this case
  If ICF is BSRP NTB, OBSS AP is more likely to shorten TXOP since the TXOP is for single-user communication
  Currently, BSRP NTB is a valid ICF sent by AP only when STA enables DUO/LLI

## Slide 4: NPCA considering DUO ICF
Proposal: PPDU-based NPCA should be used if OBSS ICF solicits unavailability info
  For simplicity, the rule can be: if NPCA is triggered by OBSS BSRP NTB + M-BA, then PPDU-based NPCA should be used
  Alternatively, AP only enables PPDU-based NPCA if it finds OBSS has enabled DUO
For further optimization, indication can be added to BSRP for making better NPCA decision, e.g.,
  Response type – if response type indicates unavailability info, then PPDU-based NPCA is used
  Whether TXOP duration is subject to change – if subject to change, then PPDU-based NPCA is used

## Slide 5: NPCA considering Co-BF/Co-SR
In Co-BF/Co-SR transmission phase, it has not been decided how to set Duration field in ICF
If coordinating AP sets a long NAV using ICF, STAs of coordinated AP may perform TXOP-based NPCA based on coordinating AP’s ICF/ICR
  These STAs will waste power and cannot participate in Co-BF/Co-SR transmission

## Slide 6: NPCA considering Co-BF/Co-SR
Proposal: define rules to prevent STAs of coordinated AP from performing TXOP-based NPCA based on coordinating AP’s ICF/ICR
  Opt 1) AP only enables PPDU-based NPCA if it has established Co-BF/Co-SR with another AP
  Opt 2) STA uses PPDU-based NPCA if it has enabled Co-BF/Co-SR
  Opt 3) STA uses PPDU-based NPCA if it determines OBSS ICF is for Co-BF/Co-SR
Additional rule: a Co-BF/Co-SR PPDU can trigger NPCA only if neither of two BSS colors in U-SIG field matches STA’s BSS color
  The second BSS color needs to be checked such that STAs of coordinated AP will not miss the Co-BF/Co-SR PPDU from the coordinated AP
  If Co-BF/Co-SR sequence doesn’t involve STA’s BSS, NPCA can be triggered by Co-BF/Co-SR PPDU

## Slide 7: Conclusion
In this contribution, we have discussed NPCA rules for specific scenarios
  PPDU-based NPCA should be used if OBSS ICF solicits unavailability info
  PPDU-based NPCA should be used if OBSS ICF is in a TXOP for Co-BF/Co-SR transmission

## Slide 8: References
[1] 11-25-0936-08-00bn-pdt-cr-mac-npca-cc50, Matthew Fischer