## Slide 1: Dynamic Decision Mechanism for NPCA Switch-Back in OBSS TXOP Early Termination
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd |  |  | chehui@ruijie.com.cn
Fachang Guo | Ruijie Networks Co., Ltd |  |  | 
LongLong Hong | Ruijie Networks Co., Ltd |  |  | 
Hang Yang | Ruijie Networks Co., Ltd |  |  | 
Yuqing Zheng | Ruijie Networks Co., Ltd |  |  | 
Date: 2025-07-16
Authors:

## Slide 2: Abstract
Background:
NPCA mechanisms (802.11bn) define switch conditions to NPCA channel but lack robust solutions for switch-back during dynamic OBSS TXOP changes.
Problem:
Existing methods (MAP coordination) fail when:
OBSS TXOP ends early, causing inaccurate switch-back timing;
AP/STA face different OBSS interference sources.
Proposal:
AP MLD uses multi-link to dynamically decide switch-back timing, reducing invalid TXOPs.

## Slide 3: NPCA Background & Gaps
Current NPCA Framework (802.11bn):
Switch to NPCA:
Triggered by OBSS interference (bandwidth, duration, TA info).
Switch-Back Rules:
Motion #124: Defines NPCA switch/swich-back delays (0–252 μs, 4 μs resolution).
Motion #126: Resets CW_NPCA[AC] and BO_NPCA when switching to NPCA channel.
Identified Gaps:
OBSS TXOP Early Termination:
AP/STA on NPCA channel miss PCH OBSS TXOP end → non-NPCA nodes initiate invalid TXOPs.
Diverse OBSS Interference:
AP and STA may switch due to different OBSS sources → existing coordination method fails.

## Slide 4: Proposed Dynamic Decision Mechanism
Core Idea:
AP MLD uses multi-link to detect OBSS TXOP early termination and optimize switch-back timing.
Key Components:
Detection:
Non-NPCA nodes (e.g., non-AP MLD on PCH) monitor OBSS TXOP status.
Notification:
OBSS early termination event + BSS Color sent via idle link (e.g., Link 2).
Decision:
AP MLD verifies BSS Color match → triggers switch-back command to NPCA nodes.

## Slide 5: Example Scenario
Network Setup:
AP MLD1 (Links: L1, L2), non-AP MLD1 (L1, L2), non-AP MLD2 (L1, L2). AP MLD2, AP MLD3.
OBSS interference (from AP MLD2) on PCH triggers non-AP MLD1-L1 to switch to NPCA.
OBSS interference (from AP MLD3) on PCH triggers AP MLD1-L1 to switch to NPCA.
Non-AP MLD2-L1 remains on the PCH and does not switch to the NPCA channel.
Mechanism Workflow:
OBSS TXOP (from AP MLD2) ends early → non-AP MLD2-L1 detects it on PCH.
non-AP MLD2 sends the OBSS TXOP Early Termination notification (including BSS Color) to AP MLD1 via L2.
AP MLD1 matches BSS Color → commands non-AP MLD1-L1 to switch back via NPCA channel.
Outcome:
Prevents invalid TXOPs by synchronizing switch-back.

## Slide 6: Benefits & Implementation Notes
Advantages:
Efficiency:
Reduces invalid TXOPs.
Scalability:
Works without AP cooperation.
Robustness:
Handles diverse OBSS scenarios.
Implementation Considerations:
BSS Color Matching:
Ensures only relevant OBSS events trigger actions.
Notification Channel:
Use reserved/link 2 to avoid congestion.
Fallback:
If no non-NPCA node exists, revert to traditional methods.

## Slide 7: Summary
Problem Addressed:
Dynamic OBSS TXOP changes and heterogeneous interference break existing NPCA switch-back mechanisms.
Solution:
Multi-link notification + BSS Color verification → dynamic switch-back decisions.
Impact:
Improves channel utilization, reduces collisions, and extends NPCA applicability to non-cooperative OBSS environments.

## Slide 8: References
[1]11-24-1852-00-00bn, “some-details-on-npca-operation”, Ofinno, 2025.