## Slide 1
July 2025
Further Considerations on P-EDCA
Date: 2025-07-17
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Introduction
The P-EDCA contention shall start immediately after the end of the transmitted DS-CTS frame and shall follow the random backoff procedure defined in 10.23.2.4 (Obtaining an EDCA TXOP) except that :
  Only EDCAF[AC_VO] shall be allowed to contend during the P-EDCA contention; Operation of the other EDCAFs is suspended
However, how to suspend to other EDCAFs is yet to be defined
In addition, one of the purposes of transmitting a DS-CTS before P-EDCA contention can be considered to be the provision of medium protection during the P-EDCA contention duration
In this contribution, we discuss how to allow only EDCAF[AC_VO] to contend during the P-EDCA by suspending other EDCAFs, and how to provide conservative channel protection after transmitting the DS-CTS

## Slide 3: EDCAF to contend P-EDCA (1/3)
P-EDCA is an enhancement of the EDCA mechanism to support pending AC_VO LL traffic
  For example, if the UHR STA has pending LL traffic and satisfies the conditions to perform P-EDCA, it can participate in P-EDCA contention
  In the context of P-EDCA, which is intended to support AC_VO LL traffic, it is reasonable that only EDCAF[AC_VO] shall be allowed to contend
  However, if the suspension of all EDCAFs except EDCAF[AC_VO] cannot be ensured, the following issue may occur
    Since internal resolution of contending EDCAFs within a STA does not always reflect intended prioritization
      For example, EDCAF[AC_VI] may unintentionally obtain the TXOP
    This may violate the main purpose of P-EDCA, and the pending AC_VO LL traffic may be lost (i.e., expired)
Therefore, it is essential to enforce a mechanism that strictly suspends all EDCAFs except EDCAF[AC_VO]
[Internal contention]
AIFS[2]
DS-CTS
RTS
AC_VI traffic
CTS
…
…
BA
AC_VI
AC_V0
RTS
BUSY

## Slide 4: EDCAF to contend P-EDCA (2/3)
The following described the related TXNAV timer from IEEE802.11 REVme7.0
  “The TXNAV timer is a single timer, shared by the EDCAFs within a STA, that is initialized with the duration from the Duration/ID field in the frame most recently successfully transmitted by the TXOP holder, except for PS-Poll frames”
  “All other channel access functions at the STA shall treat the medium as busy until the expiration of the TXNAV timer”
We already define the rule in P-EDCA :
  A P-EDCA STA that initiates a TXOP during a P-EDCA contention shall transmit an RTS frame as initial frame in the TXOP
Therefore, if the concept of the TXNAV timer can be reused or extended before the TXOP holder is clearly identified, all EDCAFs can be suspended except for EDCAF[AC_VO]

## Slide 5: EDCAF to contend P-EDCA (3/3)
Proposal : Extend the concept of the TXNAV timer by adding the following rule
  After transmitting the DS-CTS, the TXNAV timer shall be applied to all EDCAFs except the EDCAF for AC_VO, for the duration indicated in the Duration/ID field of the DS-CTS (e.g., until the end of 97 µs)
  By applying this, the TXNAV timer operates internally at the P-EDCA STA that transmitted the DS-CTS, causing all ACs except AC_VO to refrain from attempting channel access
AIFS[2]
DS-CTS
RTS
AC_VO traffic
CTS
…
…
BA
P-EDCA contention duration
(97 µs)
= TXNAV Timer
[Internal contention]
AC_VI
AC_V0
RTS

## Slide 6: Medium protection for P-EDCA contention
Due to the DS-CTS, the UHR STA that transmits the DS-CTS can contend only with other P-EDCA STAs
  This means that when OBSS STAs overhear DS-CTS, they shall not attempt channel access during the 97 µs duration
When a P-EDCA STA initiates a TXOP by transmitting an RTS frame, the data rate of the RTS frame can be defined as follows:
  “If a control frame is carried in non-HT PPDU, the transmitting STA shall transmit the frame using one of the rates in the BSSBasicRateSet parameter or a rate from the mandatory rate set of the attached PHY if the BSSBasicRateSet is empty”
However, if the RTS is transmitted at a higher data rate compared to 6 Mb/s, it may not provide conservative medium protection, which refers to ensuring the maximum possible coverage and decodability of the control frame
  In such a case, OBSS STAs that could receive the DS-CTS may not be able to receive/decode the RTS, and thus may attempt to access the channel after the 97 µs duration, causing interference to the TXOP obtained by the P-EDCA STA
Proposal: Use a data rate equal to or lower than 6 Mb/s for transmitting the RTS to maintain consistent medium protection and prevent interference after a P-EDCA STA obtains a TXOP

## Slide 7: Summary
In this presentation, we discuss how to allow only EDCAF[AC_VO] to contend in P-EDCA by reusing the concept of the TXNAV timer
Moreover, regarding medium protection, we discuss the data rate of the RTS transmitted after the DS-CTS as the initial frame in the TXOP

## Slide 8: Reference
[1] IEEE802.11 REVme7.0
[2] Draft P802.11bn_D0.3