## Slide 1
July 2025
Further Considerations on P-EDCA
Date: 2025-07-17
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Introduction
The P-EDCA contention shall start immediately after the end of the transmitted DS-CTS frame and shall follow the random backoff procedure defined in 10.23.2.4 (Obtaining an EDCA TXOP) except that:
  Only EDCAF[AC_VO] shall be allowed to contend during the P-EDCA contention
  Operation of the other EDCAFs is suspended
The text may benefit from clarifying how the suspension of the other EDCAFs is realized
Furthermore, one of the purposes of transmitting a DS-CTS prior to the P-EDCA contention is to provide medium protection, enabling P-EDCA STAs to content for the channel during the P-EDCA contention period
In this contribution, we discuss how to ensure that only EDCAF[AC_VO] contends during the P-EDCA contention by suspending the other EDCAFs, and how to provide conservative channel protection following DS-CTS transmission

## Slide 3: EDCAF to contend P-EDCA (1/3)
P-EDCA is an enhancement of the EDCA mechanism to support pending AC_VO traffic
  If a UHR STA has pending AC_VO traffic and meets the conditions for P-EDCA, it participates P-EDCA contention
  Given that P-EDCA is intended to support AC_VO traffic, it is reasonable that only EDCAF[AC_VO] be allowed to contend during the P-EDCA contention
  However, if suspension of all EDCAFs other than EDCAF[AC_VO] cannot be ensured, the following issue may arise
    Internal resolution among contending EDCAFs within a STA does not always reflect the intended prioritization
      For example, EDCAF[AC_VI] may unintentionally obtain the TXOP
    This would undermine the main purpose of P-EDCA, and pending AC_VO traffic may be lost (i.e., expired)
Accordingly, a mechanism that suspends all EDCAFs except EDCAF[AC_VO] may be needed to ensure the intended behavior during the P-EDCA contention
[Internal contention]
BUSY
AC_VI traffic
CTS
…
…
BA
DS-CTS
BUSY
…
AC_VO
AC_VI
RTS
BUSY
BUSY
BUSY

## Slide 4: EDCAF to contend P-EDCA (2/3)
The following described the related TXNAV timer from IEEE802.11 REVme7.0
  “The TXNAV timer is a single timer, shared by the EDCAFs within a STA, that is initialized with the duration from the Duration/ID field in the frame most recently successfully transmitted by the TXOP holder, except for PS-Poll frames”
  “All other channel access functions at the STA shall treat the medium as busy until the expiration of the TXNAV timer”
The P-EDCA text specifies the following:
  A P-EDCA STA that initiates a TXOP during a P-EDCA contention shall transmit an RTS frame as the initial frame in the TXOP
  This implies that the TXOP holder is defined upon the transmission of the RTS frame
Therefore, exploring reuse or extension of the TXNAV timer before the TXOP holder is determined may help suspend all EDCAFs other than EDCAF[AC_VO]

## Slide 5: EDCAF to contend P-EDCA (3/3)
Proposal : Extend the concept of the TXNAV timer by adding the following rule
  “The TXNAV timer is a single timer, shared by the EDCAFs within a STA, that is initialized with the duration from the Duration/ID field in the frame most recently successfully transmitted by the TXOP holder, except for PS-Poll frames”. In addition, the TXNAV timer shall also be initialized with the duration from the Duration/ID field in a transmitted defer signal (e.g., DS-CTS) for P-EDCA contention.
  With this rule, after transmitting DS-CTS, the TXNAV timer applies to all EDCAFs other than EDCAF[AC_VO] for the DS-CTS Duration/ID interval
    As a result, only EDCAF[AC_VO] attempts channel access during the P-EDCA contention
[Internal contention]
BUSY
AC_VO traffic
CTS
…
…
BA
DS-CTS
BUSY
…
AC_VO
AC_VI
RTS
BUSY
BUSY
P-EDCA contention duration (97 µs)
= TXNAV Timer
…
BUSY

## Slide 6: Medium protection for P-EDCA contention
After transmitting the DS-CTS, the UHR STA contends only with other P-EDCA STAs that have also transmitted a DS-CTS
  STAs that overhear the DS-CTS shall not attempt channel access for the 97 µs duration
When a P-EDCA STA initiates a TXOP by transmitting an RTS frame in a non-HT PPDU, the data rate of the RTS frame can be defined as follows:
  “If a control frame is carried in non-HT PPDU, the transmitting STA shall transmit the frame using one of the rates in the BSSBasicRateSet parameter or a rate from the mandatory rate set of the attached PHY if the BSSBasicRateSet is empty”
However, if the RTS is transmitted at a data rate higher than 6 Mb/s, it may fail to provide conservative medium protection, which refers to ensuring the maximum possible coverage and decodability of the control frame
  In such a case, OBSS STAs that overheard the DS-CTS may be unable to receive or decode the RTS/CTS, and may therefore attempt to access the channel after the 97 µs duration, causing interference to the TXOP obtained by the P-EDCA STA
Proposal: Transmit the RTS at a data rate no greater than that of the DS-CTS to maintain consistent medium protection and to prevent interference after a P-EDCA STA obtains a TXOP

## Slide 7: Summary
In this presentation, we outline an approach that aims to enable only EDCAF[AC_VO] to contend during P-EDCA by reusing the TXNAV timer concept
Moreover, we also discuss medium-protection aspects, focusing on the RTS data rate used after the DS-CTS as the initial frame of the TXOP

## Slide 8: Straw Poll #1
Do you agree to consider defining a mechanism for the P-EDCA STA to suspend all EDCAFs except EDCAF[AC_VO]?
  One option is to enhance the TXNAV timer

## Slide 9: Straw Poll #2
Do you agree to require that a P-EDCA STA transmit RTS at a data rate no greater than that used for the DS-CTS?

## Slide 10: Reference
[1] IEEE802.11 REVme7.0
[2] Draft P802.11bn_D1.0