## Slide 1: Co-BF Sync-reference and Sync-follower Determination
Date: 2025-07-22
Authors:

## Slide 2: Introduction: Sync-Reference and Sync-Follower
Concept of a Sync-reference and a Sync-follower is introduced in UHR [1]
They are defined as follows [1]:
  Sync-reference AP: The AP acting as a frequency reference during sounding stage and beyond
    Does not need to remember CFO re-corrections
  Sync-follower AP: The AP that aligns its frequency with respect to the Sync-reference AP during sounding stage and beyond
    Remembers pre-corrections
Decision/determination of which AP gets to be the Sync-reference is still TBD

## Slide 3: Background: Illustration when sounding process happens first in reference AP’s BSS [1]
Sounding is happening first in reference AP’s BSS
NDPA
Reference
AP1
Follower
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
AP2 Calculates CFO and applies to NDP
AP1 Calculates CFO and applies to NDP
Uses most recent
pre-correction

## Slide 4: Background: Illustration when sounding process happens first in follower AP’s BSS [1]
Sounding is happening first in follower AP’s BSS
Reference
AP1
Follower
AP2
STA1
associated
with AP1
STA2
associated
with AP2
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
NDPA
NDP
CSI
BFRP
BF
RP
NDPA
NDP
CSI
Uses most recent
pre-correction
AP1 Calculates CFO and applies to NDP
AP2 Calculates CFO and applies to NDP

## Slide 5: Problem
For a given pair of APs, how the Sync-reference and Sync-follower roles are determined is undecided
  As per current discussion, they are decided arbitrarily without considering any preference/criteria
For a pair AP1-AP2 participating in Co-BF:
  Both may be willing to be followers
  Neither may be willing to be a follower
  Only one may be willing to be a follower
An AP may strongly prefer to not be a follower (e.g., due to more complexity)
Preference of each AP may change over time based on some conditions (e.g., based on traffic)
As discussed in [2]:
  APs’ sync reference/follower roles need to be negotiated or determined before Co-BF sounding starts to avoid competition. This can be discussed as a MAC topic together with information exchanges when a Co-BF group is formed
Co-BF
Negotiation
Co-BF
Sounding
Co-BF
Data
AP 1
AP 2
(Sync-reference)
(Sync-follower)
Decided beforehand
w/o any consideration

## Slide 6: Solution 1
The Sync-reference and Sync-follower roles may be determined during MAPC agreement negotiation (establish/update) for Co-BF
  Considering the preference of each AP
  May agree to determine roles in subsequent stages based on a TBD criteria after Co-BF negotiation
Co-BF
Negotiation
Co-BF
Sounding
Co-BF
Data
AP 1
AP 2

## Slide 7: Solution 2
The Sync-reference and Sync-follower roles may be determined/switched during each sounding session
  Decided based on a criteria (e.g., initiating AP may decide)
Co-BF
Negotiation
Co-BF
Sounding
Co-BF
Data
AP 1
AP 2
Co-BF
Invite
Co-BF
Response
NDPA

## Slide 8: Solution 3
The Sync-reference and Sync-follower roles may be determined/switched outside of the MAPC negotiation/sounding/data transmission phase
  Either AP may initiate switch role request after roles have been decided
  Procedure for dynamic switching of roles may reuse Co-BF negotiation procedure or a separate frame exchange between APs
  Switching indication may happen at any stage above
Co-BF
Negotiation
Co-BF
Sounding
Co-BF
Data
AP 1
AP 2
FRAME
AP 1 indicates switching of
Reference-Follower roles

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/25/11-25-0083-01-00bn-cfo-correction-and-related-simplifications-for-cobf.pptx
[2] https://mentor.ieee.org/802.11/dcn/25/11-25-0103-00-00bn-simplified-carrier-synchronization-for-cobf-transmissions.pptx