## Slide 1: CW And BO Discussion In P-EDCA
Date: 2025-07-24
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Kaidong Wang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
P-EDCA is introduced in TGbn to reduce the access delay distribution tail for AC_VO traffic;
A P-EDCA STA may start a P-EDCA contention when QSRC[AC_VO] is equal or greater than P-EDCA QSRC threshold and PSRC[AC_VO] is not greater than P-EDCA PSRC threshold;
In P-EDCA contention, the EDCAF[AC_VO] shall initialize AIFSN, CWmin and CWmax with values of P-EDCA AIFSN, P-EDCA CWmin and P-EDCA CWmax respectively. CW[AC_VO] shall be initialized to P-EDCA CWmin, and set the backoff counter to an integer value randomly selection from 0 to CW[AC_VO];
A P-EDCA STA shall not attempt to start P-EDCA if one of below conditions matches
  that successfully delivered one or more pending MPDU through P-EDCA contion, or
  PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt transmission attempts
The EDCAF[AC_VO] shall update the AIFSN, CWmin, and CWmax with the values in dot11EDCATable;
For now, how to set the CW[AC_VO] and backoff counter is not defined yet.

## Slide 3: Option 1
If successfully transmitted an MPDU of AC_VO through P-EDCA contention, or PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt transmission attempts then CW[AC_VO] shall be initialized to CWmin[AC_VO], and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].
Cons of Option1: it is not good to set CW to CWmin after one or more consecutive failure transmission which may cause high collisions.

## Slide 4: Option 2
  If successfully transmitted an MPDU of AC_VO through P-EDCA contention, then CW[AC_VO] shall be initialized to CWmin[AC_VO], and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].
  If PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt transmission attempts, then CW[AC_VO] shall be initialized to the 2^n*CWmin[AC_VO]+1 where n = dot11PEDCAConsecutiveAttempt, and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].

## Slide 5: Option 3
  If successfully transmitted an MPDU of AC_VO through P-EDCA contention, then CW[AC_VO] shall be initialized to CWmin[AC_VO], and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].
  If PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt transmission attempts, then CW[AC_VO] shall be initialized to the 2^n*P-EDCA CWmin+1 where n = dot11PEDCAConsecutiveAttempt, and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].

## Slide 6: Option 4
  If successfully transmitted an MPDU of AC_VO through P-EDCA contention, then CW[AC_VO] shall be initialized to CWmin[AC_VO], and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].
  If PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt transmission attempts, then CW[AC_VO] shall be initialized to the 2*CW[AC_VO]+1, and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].

## Slide 7: Summary
When a P-EDCA STA switches from P-EDCA contention to EDCA contention, how to set CW[AC_VO] and backoff counter is not defined yet;
Several options are provided, and prefer to have different CW[AC_VO] setting due to successfully transmission or consecutive failures in P-EDCA contention;
  i.e. prefer one option from Opt 2 - Opt 4
 | CW[AC_VO] |  | Backoff counter
 | Successful | PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt | 
Opt 1 | CWmin[AC_VO] | CWmin[AC_VO] | Randomly selected from [0, CW[AC_VO]]
Opt 2 |  | 2^n*CWmin[AC_VO]+1 | 
Opt 3 |  | 2^n*P-EDCA CWmin[AC_VO]+1 | 
Opt 4 |  | 2*CW[AC_VO]+1 | 
Note: n = dot11PEDCAConsecutiveAttempt |  |  | 

## Slide 8: SP 1
Do you agree to add following CW[AC_VO] and backoff counter setting rules for a P-EDCA STA?
    If successfully transmitted an MPDU of AC_VO through P-EDCA contention, then CW[AC_VO] shall be initialized to CWmin[AC_VO], and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].
    If PSRC[AC_VO] reaches dot11PEDCAConsecutiveAttempt transmission attempts, then CW[AC_VO] shall be initialized to the <the option that the group could reach consensus>, and the EDCAF[AC_VO] shall set the backoff counter to an integer value chosen randomly with a uniform distribution taking values in the range 0 to CW[AC_VO].