## Slide 1: A New Procedure for DPS Mobile AP
Date: 2025-07-24
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Kaidong Wang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
A DPS assisting STA shall solicit the transition of the peer DPS STA from lower capability (LC) mode to higher capability (HC) mode by sending an ICF;
If a DPS assisting STA is also a DPS STA, it needs to make it clear when the DPS assisting STA switch from LC mode to HC mode;
  DPS assisting STA is a mobile AP, and the DPS STA is a non-AP STA, or
  DPS assisting STA is a non-AP STA, and the DPS STA is a mobile AP
Below is a procedure when the DSP assisting STA is also a DPS STA;
  The DPS assisting STA switches from LC mode to HC mode;
  The DPS assisting STA performs channel contention, and backoff counter reaches 0;
  The DPS assisting STA sends ICF to DPS STA with padding;
  The DPS STA receives ICF and switch from LC to HC mode during padding period of ICF frame;
  The DPS STA response ICR to ICF frame.

## Slide 3: Drawbacks
The DPS assisting STA cost more power
  It keeps in HC mode since the end time of its own switch delay period;
  If the channel changes to busy after channel delay, the DPS assisting STA may perform one of below based on implementation
    keeps in HC mode => waste power
    Switches back to LC mode, and then switch to HC mode again when the channel becomes idle => waste power and cause delay
  During the transition period of DPS STA, the DPS assisting STA needs to send padding information in HC mode
We need an improved procedure to save power as well as reduce the transmission delay.

## Slide 4: Proposed New Procedure
DPS assisting STA performs backoff and send out ICF in LC mode;
DPS STA responses ICR in LC mode;
DPS assisting STA and DPS STA switch from LC mode to HC mode after ICR frame;
DPS assisting STA performs backoff in HC mode;
  Usually only 20MHz is supported in LC mode, a backoff in HC mode can obtain a wider TXOP bandwidth
  If there is no transmission for time period larger than PIFS, the TXOP holder shall initiate a backoff in order to continues transmission in the TXOP
DPS assisting STA communicate with DPS STA in HC mode;
Switch back rules for DPS assisting STA and DPS STA keeps unchanged.

## Slide 5: Benefits of Proposed New Procedure
It is “safer” for DPS assisting STA to switch to HC mode after ICF/ICR exchange in LC mode;
  Avoid the medium becomes busy during the backoff period in HC mode in current procedure
DPS assisting STA switches during the switch delay period of DPS STA, no extra time cost;
DPS assisting STA doesn’t need to transmit padding information during the switch delay period of DPS STA, thus more power efficient.

## Slide 6: Summary
There are several drawbacks for current DPS procedure when DPS assisting STA is also a DPS STA;
  DPS assisting STA needs to stay a longer time in HC mode, which will cost more power
  If channel busy happens during the backoff period, DPS assisting STA needs to stay on HC mode to waiting for channel becomes idle again or switch back and forth between HC and LC modes.
A more power efficient procedure is proposed in which the DPS assisting STA will obtain a TXOP in LC mode before it switch to HC mode.

## Slide 7: SP 1
Do you agree that when a DPS assisting STA is a DPS STA, the DPS assisting STA is allowed to obtained a TXOP in LC mode before it switch to HC mode?

## Slide 8: SP 2
Do you agree that when a DPS assisting STA is a DPS STA, the following procedure is allowed?
  The DPS assisting STA obtains a TXOP in LC mode through ICF/ICR frame exchange with DPS STA;
  The DPS assisting STA and DPS STA switch from LC mode to HC mode after ICR frame;
  The DPS assisting STA performs a backoff in HC mode before transmitting to DPS STA.
The figure is only for reference, it is not a part of SP2.