## Slide 1: NPCA TIMER and NPCA Switch Back
Date: 2025-07-24
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Kaidong Wang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
There is below statement about NPCA TIMER description in doc 11-25/0936r8:
It is supposed that the NPCA_TIMER will be used for NPCA switch back, but the document doesn’t specify it;
We will discuss what’s the reasonable way to set the NPCA_TIMER, and when AP and NPCA non-AP STAs switch back to primary channel.
a) Each time that the STA switches to the NPCA primary channel, the STA shall
  i) If condition 1) from 37.10.2 (NPCA mode starting conditions) is met, set NPCA_CFRAME_TXOP_REM_DUR to 0.
  ii) Set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the largest of the switch back delays of the STA and its peers.

## Slide 3: Current Setting 1
Problem: the NPCA non-AP STAs can not identify which NPCA non-AP STA with the largest switch back delay, and thus can not correctly set their NPCA_TIMER.
a) Each time that the STA switches to the NPCA primary channel, the STA shall
  i) If condition 1) from 37.10.2 (NPCA mode starting conditions) is met, set NPCA_CFRAME_TXOP_REM_DUR to 0.
  ii) Set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the largest of the switch back delays of the STA and its peers.

## Slide 4: Current Setting 2
Problem:
  AP needs to maintain its own NPCA_TIMER and each NPCA non-AP STA’s NPCA_TIMER, it largely increase the scheduling complexity;
  Each NPCA non-AP STA needs to maintain its own NPCA_TIMER and AP’s NPCA_TIMER, it increase the scheduling complexity.
a) Each time that the STA switches to the NPCA primary channel, the STA shall
  i) If condition 1) from 37.10.2 (NPCA mode starting conditions) is met, set NPCA_CFRAME_TXOP_REM_DUR to 0.
  ii) Set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the switch back delays of the STA.

## Slide 5: Proposed Opt 1
AP announces a BSS switch back delay which is the largest switch back delay of the AP and all the enabled associated NPCA non-AP STAs;
AP and all associated NPCA non-AP STA will switch back to primary channel when NPCA_TIMER count down to 0;
AP may update the BSS switch back delay when a non-AP STA with switch back delay > BSS switch back delay enables NPCA.
a) Each time that the STA switches to the NPCA primary channel, the STA shall
  i) If condition 1) from 37.10.2 (NPCA mode starting conditions) is met, set NPCA_CFRAME_TXOP_REM_DUR to 0.
  ii) Set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the BSS switch back that announced by associated AP.

## Slide 6: Proposed Opt 2
AP announces a BSS switch back delay;
AP and all associated NPCA non-AP STA will switch back to primary channel when NPCA_TIMER count down to 0;
A non-AP STA with switch back delay > BSS switch back delay shall disable NPCA.
a) Each time that the STA switches to the NPCA primary channel, the STA shall
  i) If condition 1) from 37.10.2 (NPCA mode starting conditions) is met, set NPCA_CFRAME_TXOP_REM_DUR to 0.
  ii) Set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the BSS switch back that announced by associated AP.

## Slide 7: Proposed Opt 3
a) Each time that the STA switches to the NPCA primary channel, the STA shall
  i) If condition 1) from 37.10.2 (NPCA mode starting conditions) is met, set NPCA_CFRAME_TXOP_REM_DUR to 0.
  ii) Set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the largest of the BSS switch back delay and the switch back delay of the STA.
AP announces a BSS switch back delay;
AP and all associated NPCA non-AP STA will switch back to primary channel when its own NPCA_TIMER count down to 0;
AP shall not schedule a NPCA non-AP STA after the STA’s NPCA_TIMER count down to 0;
AP may update the BSS switch back delay to make it is the largest switch back delay of the AP and all the enabled associated NPCA non-AP STAs.

## Slide 8: Proposed Opt 3
Benefits of Opt 3:
Each NPCA non-AP STA only maintain its own NPCA_TIMER, because non-AP STA will always switch back earlier to at the same time as AP;
AP may announce and update BSS Switch back delay to make it always the the largest switch back delay of the AP and all the enabled associated NPCA non-AP STAs, so AP always only need to maintain its single NPCA_TIMER, or
AP can choose not update BSS Switch back delay, and additionally maintain NPCA_TIMER of few NPCA non-AP STAs with larger switch back delay than BSS switch back delay.

## Slide 9: Summary
Current settings of NPCA_TIMER have some issues
  can not be implemented for current setting 1: (NPCA_TIMER = REM_DUR - the largest of the switch back delays of the STA and its peers)
  very complex for the schedule for current setting 2: (NPCA_TIMER = REM_DUR - the switch back delay of the STA)
Propose to use opt 3 to set NPCA_TIME, due to below benefits
  NPCA non-AP STA only need to maintain single NPCA_TIMER
  AP can only need to maintain single NPCA_TIMER, (may need to update BSS switch back delay), or
  AP only additional maintain a few NPCA non-AP STAs’ NPCA_TIMER (instead of maintain all NPCA non-AP STAs’ NPCA_TIMER) without BSS switch back delay update

## Slide 10: SP 1
Do you agree to add below s?
  Each time that the STA switches to the NPCA primary channel, the STA shall set NPCA_TIMER to the largest non-zero value of the variables NPCA_PPDU_REM_DUR, NPCA_PHY_TXOP_REM_DUR and NPCA_CFRAME_TXOP_REM_DUR, minus the largest of the BSS switch back delay and the switch back delay of the STA.