## Slide 1: Information Exchange for CoSR Transmissions
Date: 2025-06-12
Authors:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm Technologies Inc. |  |  | svverman@qti.qualcomm.com
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Alice Chen |  |  |  | 

## Slide 2: Introduction
Two types of Coordinated Spatial Reuse (CoSR) is allowed in 11bn
  Type 1: The two transmissions have common preamble only till L-SIG
    E.g., UHR+EHT, EHT+UHR, EHT+EHT
  Type 2: The two transmissions have a common preamble till U-SIG
    UHR+UHR
In these slides we show how information exchange should work for CoSR
  Invite Frame from the sharing AP
  Response Frame from shared AP
  Sync Frame from the sharing AP

## Slide 3: High Level Direction -I
Sharing AP can advertise the following things in the invite frame
  PHY Version of the PPDU it intends to transmit
  Maximum transmit power limit of the shared AP
    This tells the shared AP which STAs are possible candidates for CoSR transmission in its BSS
    This may be better sent as a “Tx power limit per 20MHz” especially if shared AP is allowed some flexibility regarding the BW in the reuse transmission
  BW, punctured channel information of the PPDU it intends to transmit
    These are some basic parameters that shared AP must consider
  Min and Max number of data OFDM symbols
    May allow min and max to be the same number as well
    Similar mechanism as CoBF
  Number of LTF symbols and GI+LTF combination
    Helps to align the symbol boundaries in both the LTF and data section, to ease length calculations
  Transmit power it intends to use in the actual DL PPDU
    Helps the shared AP pick a good STA for its transmission, and MCS for its transmissions etc
      Maybe sent as a per-20MHz Tx power indication
      Appendix shows a more detailed list of advantages of this approach

## Slide 4: High Level Direction -II
Based on this, shared AP provides the following information in the response frame
  PHY version of the PPDU it intends to transmit
  Transmit power it intends to use
    Less than or equal to the max limit prescribed by the sharing AP in the invite frame
    May be best signaled in a power per 20MHz basis
    Maybe beneficial for sharing AP to revise its MCS
  BW, punctured channel information of the PPDU it intends to transmit
    If we want to allow CoSR transmissions from shared AP in a subset of non-punctured channels
  Requested length from shared AP (only a request and may not be honored by the sharing AP)
    Number of data OFDM symbols
    Should be higher than the one in the invite
Sync Frame contents depend on the response frame, i.e., if it is type 1 or type 2 CoSR
  The sync frame may have additional PHY parameters for the common U-SIG if it is type 2 CoSR
  Less PHY parameters needed if it is type 1 CoSR
  Final L-SIG length is carried here

## Slide 5: High Level View: Information Exchange
Below is a summary of the information flow we propose
Invite
Tx power limit for shared AP
Tx power of sharing AP
Response
TX power of shared AP
PHY Version of its transmission
Sync
Final L-SIG length
Any additional PHY parameters needed for common U-SIG
PHY Version of its transmission
Min and max OFDM symbols
BW, punctured channel info
GI+LTF combination of its transmission
Requested number of symbols
BW, punctured channel info
Shared AP
Sharing AP

## Slide 6: BW and punctured channel info
For type 1 CoSR, we can allow the responding AP to use a subset of the occupied BW of the initiating AP
  No impact to the initiating AP; only less interference
For type 2 CoSR
  Responding AP must use the same BW and puncturing info as declared by the initiating AP in the invite
    Common U-SIG requires this

## Slide 7: Parameters which we recommend fixing
EHT-SIG MCS and UHR-SIG MCS for a CoSR transmission can be fixed in the spec
  E.g., to MCS0
  More reliable reception in presence of interference
Number of EHT-SIG/UHR-SIG symbols
  No padding with extra SIG symbols
  2 symbols at MCS0 for SU case

## Slide 8: Design of Length Indication
Invite frame signals
  Min and Max number of data OFDM symbols
    Allow min and max to be the same number as well
      Alternate design: we can mandate those two to be the same
  Number of LTF symbols and GI+LTF combination
Response frame signals
  Suggested number of data OFDM symbols
Sync frame signals
  Final L-SIG length
  Number of LTF symbols and GI+LTF combination
    Same as invite frame

## Slide 9: Invite Frame Contents
Below, we show the contents of the Invite Frame for CoSR
Category | 
Control | ‘CoSR Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier (sharing AP)
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Number of LTF symbols
 | Tx Power Limit of Shared AP
 | Tx Power of Sharing AP

## Slide 10: Response Frame Contents
Below we show the contents of the response frame from the shared AP
Category | 
Control | ‘CoSR Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier (shared AP)
 | Bandwidth (shared AP)
 | Punctured Channel Information (shared AP)
 | Transmit power of shared AP’s PPDU
Suggested number of Data OFDM symbols should be greater than the max number in invite
BW and punctured channel information
  Allowed to be different from the invite for type 1 CoSR
  Required to be the same as the invite for type 2 CoSR (UHR+UHR)
Transmit power of shared AP’s PPDU shall be less than or equal to the limit prescribed in invite

## Slide 11: Summary
In these slides we showed a design for the information exchange needed for CoSR transmissions
  Detailed design of the fields of invite and response frames was also shown

## Slide 12: SP1
Do you support to add the following to the TGbn SFD?
  The CoSR transmissions from the two APs will use an aligned OFDM symbol boundary during the entire PPDUs (both LTF field and data field) and the same number of EHT-SIG or UHR-SIG field symbols
    No change to the existing extra-LTF rules shall be done

## Slide 13: SP2
Do you support to add the following to the TGbn SFD?
  The invite frame for CoSR will carry the following
    GI+LTF combination
    Number of LTF symbols

## Slide 14: SP3
Do you support to add the following to the TGbn SFD?
  The invite frame for CoSR will carry the following
    Tx power limit of the shared AP (as a dBm/20MHz number)
    Intended Tx power of the sharing AP (as a dBm/20MHz number)
    BW and punctured channel info of the sharing AP’s transmission

## Slide 15: SP4
Do you support to add the following to the TGbn SFD?
  The CoSR length indication will be done as follows:
    Invite frame signals
      Min and Max number of data OFDM symbols
    Response frame signals
      Suggested number of data OFDM symbols
    Sync frame signals
      L-SIG length
    The same 9 bit encoding as COBF shall be used for the following 3 fields
      Min and Max number of data OFDM symbols in invite
      Suggested number of data OFDM symbols in response
        Value 511 (‘111111111’) indicates “No suggestion”

## Slide 16: SP5
Do you support to add the following to the TGbn SFD?
  The response frame for CoSR will carry the following
    Requested length of transmission in number of data OFDM symbols
      If a request is being made, should be higher than the max number in the invite
    BW, punctured channel information of the shared AP’s PPDU
      For type 2 CoSR: Shared AP must use the same BW and puncturing info as declared by the sharing AP in the invite
      For type 1 CoSR: The shared AP is allowed to use a subset of the occupied BW of the sharing AP
    Tx power that the shared AP has chosen to use (as a dBm/20MHz number)
      Less than or equal to the max limit prescribed by the sharing AP in the invite frame

## Slide 17: SP6
Do you support to add the following to the TGbn SFD?
  For CoSR transmissions the UHR or EHT SIG MCS shall be fixed to MCS0 and the number of UHR or EHT SIG symbols shall be fixed to 2

## Slide 18: appendix
Benefits of putting the Tx power information in the invite

## Slide 19: Benefits of having Tx powers in the invite and response frames
Let’s assume AP1 is the sharing AP and AP2 is the shared AP
Benefit Area | Tx powers exchanged in invite and response | Tx powers in sync
Accurate user selection at AP2 and maximizing the number of potential CoSR candidates in AP2’s BSS |  Possible as both AP2’s max allowed power and AP1’s Tx power (and hence its interference level) is known |  AP2 must assume a conservative power level for itself based on minimum acceptable Tx power. Moreover, AP2 does not know interference caused by AP1 in this design to make accurate user selection.
Early determination of MCS for AP2 and packet length determination |  Possible after invite as both AP2’s power and interference from AP1 is known |  AP2 doesn’t know its power level or interference level from AP1 till the invite
MCS refinement possible for AP1 based on response |  Response has AP2’s chosen Tx Power |  Not possible as no power number in response

## Slide 20: Benefits of our scheme (contn’d)
Moreover, Tx powers being sent earlier is better from debugging, sniffing and testing stand-point
  Clear declaration of what is being used by both APs early on in the frame exchange
In general, earlier dissemination of Tx Powers has only positives
  No disadvantage from sending this information early-on
    When we have earlier frames available, no reason to not utilize them and exchange this information as early as possible
  Keeps things more aligned with CoBF
    The length field negotiation in invite/response hinges upon AP2 being able to determine its MCS accurately after invite

## Slide 21: Sync Frame
Below we show the contents of the sync frame from the sharing AP
  Contents may be different for type 1 and type 2 CoSR
 | Type 2 CoSR | Type 1 CoSR
Control | ‘CoSR Sync’ | ‘CoSR Sync’
PHY Common Info | L-SIG Length | L-SIG Length
 | PHY Version Identifier | PHY Version Identifier (sharing AP)
 | Bandwidth | Bandwidth (sharing AP)
 | Punctured Channel Information | Punctured Channel Information (sharing AP)
 | BSS Color 1, BSS Color 2 | BSS Color 1, BSS Color 2
 | TXOP | TXOP
 | Number of UHR-SIG Symbols | Number of UHR-SIG Symbols
 | GI+LTF Size | GI+LTF Size
 | Number Of UHR-LTF Symbols | Number Of UHR-LTF Symbols
 | Number of Users | Number of Users
PHY version identifier, BW, punctured channel info, GI+LTF, Num of UHR-LTF syms, are same as in the invite
Blue fields may be removed as well without much impact
Number of UHR-SIG symbols and Number of users likely to take fixed values