## Slide 1: Negotiation on LTF Number for Co-SR
Date: 2025-07-17
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Jason Yuchen Guo |  |  |  | 
Genadiy Tsodik |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
The following consensus has been reached regarding co-SR:
  11bn defines the following modes for co-SR transmission:
    Mode 1: trigger + same L-SIG contents, could be different U-SIG contents.
      For UHR+EHT, or EHT+UHR or EHT+EHT co-SR transmission.
      Provided no changes to non-UHR EHT non-AP STAs are needed.
    Mode 2: Tigger + same L-SIG contents + same U-SIG contents
      For UHR+UHR co-SR transmission.
    For all modes, the two PPDUs will start and end at the same time.
    UHR PPDU for co-SR transmission will be used for either mode 1 or mode 2 when UHR transmission exists.
      There exists an indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for co-SR transmission.
  [Motion #252, [264] and [282]]

## Slide 3: Symbol level alignment for Co-SR PPDUs
For all Co-SR modes, the two PPDUs will start and end at the same time. To enable this requirement, the following are proposed considering easy implementation:
  Two Co-SR transmissions will use an aligned OFDM symbol boundary during the entire PPDU (both LTF field and data field) and the same number of EHT-SIG or UHR-SIG field symbols
    No change to the current extra-LTF rules
    Number of LTF symbols and GI+LTF may need to be signaled in the invite frame
  Fix the UHR or EHT-SIG field MCS to MCS0 and the number of UHR or EHT-SIG symbols to 2, for Co-SR transmissions.
  For Co-BF and Co-SR all modes transmissions, PE setting applies:
    fixed TPE (nominal_packet_padding =20us and a factor =4)

## Slide 4: Symbol level alignment for Co-SR PPDUs
The following fields are aligned:
  L-STF, L-LTF, L-SIG, RL-SIG, U-SIG and EHT/UHR-STF: fixed length for UHR MU PPDU
  EHT/UHR-SIG and PE: fixed length (8us and 20us)
For 2x EHT/UHR-LTF, the symbol level alignment can be achieved by the same number of LTF symbols, and the same number of Data symbols.
For 4x EHT/UHR-LTF, the symbol level alignment can be achieved by the same number of the sum of number of LTF symbols and number of Data symbols.
LTF
LTF
Data
Data
LTF
Data
Data
Data
LTF
Data
Data
LTF
Data
Data
Data
Data
LTF
LTF

## Slide 5: Symbol level alignment for Co-SR PPDUs
Opt1: When Co-SR Invite frame indicates 2x LTF, then in the Co-SR Response frame, the maximum supported number of LTF symbols is indicated.
  Can optionally indicate the intended/max supported number of LTF symbols in Co-SR Invite frame.
  NOTE -- NSS info is not needed for Co-SR PPDUs.
Then in the Co-SR TF/sync frame, AP1 can indicate the GI + LTF size and the number of LTF symbols based on the max LTF symbols supported by AP 1 (known by AP1), and the max LTF symbols supported by AP2.
All feedbacks in Co-SR response can be suggestions and give more opportunities for AP 2 to participate in the Co-SR.

## Slide 6: Symbol level alignment for Co-SR PPDUs
Opt2: When Co-SR Invite frame indicates 2x LTF and indicates the intended number of LTF symbols in Co-SR Invite frame, then in the Co-SR Response frame, AP2 could suggest to use 4x LTF instead, if the number of UHR-LTF is not supported by AP2 .
  Could also provide a reject reason for the rejection.
There is no need for this mechanism for 4x LTF case in the Co-SR Invite frame.

## Slide 7: Symbol level alignment for Co-SR PPDUs
Opt3: When Co-SR Invite frame indicates 2x LTF and indicates the intended number of LTF symbols in Co-SR Invite frame, then in the Co-SR Response frame, AP2 could reject the invitation if the number of UHR-LTF is not supported by AP2 .
  Could also provide a reject reason for the rejection.
There is no need for this mechanism for 4x LTF case in the Co-SR Invite frame.

## Slide 8: 4x LTF + 0.8us GI Supported
The following GI + LTF Size combinations are supported. One of the mode is optional.
Two possible ways to handle this:
  Opt 1: in the Co-SR response, AP2 shall indicates if 4x + 0.8 us GI is allowed or not. AP1 could choose 4x + 3.2us GI instead if 4x + 0.8 us GI is not supported by AP2.
  Opt 2: reject the invitation. Not supporting 4x + 0.8 us GI could be one of the reject reason.
  Opt 3: disallow 4x + 0.8 us GI in Co-SR transmission
Prefer Opt 1, 4x + 0.8 us GI could be used more often considering the easy of alignment and the reduced overhead of GI.
GI+LTF Size | M/O
2x EHT/UHR-LTF + 0.8us GI | M
2x EHT/UHR-LTF + 1.6us GI | M
4x EHT/UHR-LTF + 0.8us GI | O
4x EHT/UHR-LTF + 3.2us GI | M

## Slide 9: Summary
In this contribution, we discuss how to enable symbol level alignment through the negotiation of LTF number for Co-SR transmissions. 4x LTF + 0.8us GI Supported is also discussed.

## Slide 10: Straw Poll #1
Do you agree to add the following into 11bn SFD?
  When Co-SR Invite frame indicates 2x LTF type and indicates the intended number of LTF symbols in Co-SR Invite frame, then in the Co-SR Response frame, AP2 could reject the invitation due to the number of LTF limitation.
    The existence of a rejection reason in the CO-SR Response frame is TBD and if a rejection reason field is adopted in TGbn, the presence of a specific rejection reason for LTF limitation is also TBD

## Slide 11: Straw Poll #2
Do you agree to add the following into 11bn SFD?
  When Co-SR Invite frame indicates 2x LTF, then in the Co-SR Response frame, the maximum supported number of LTF symbols is indicated by the coordinated AP.

## Slide 12: Straw Poll #3
Do you agree to add the following into 11bn SFD?
  When Co-SR Invite frame indicates 2x LTF and indicates the intended number of LTF symbols in Co-SR Invite frame, then in the Co-SR Response frame, AP2 could suggest to use 4x LTF instead.

## Slide 13: Straw Poll #4
Do you agree to add the following into 11bn SFD?
  In the Co-SR response, the shared AP could indicate if 4x + 0.8 us GI is allowed or not.

## Slide 14
11-24-0209-16-00bn-specification-framework-for-tgbn, Ross Jian Yu (Huawei)
References

## Slide 15: Appendix - Co-BF frames
Category | Information
Control | ‘Co-BF Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Maximum Total Nss Allowed for shared AP
 | Number of Co-BF Users in sharing BSS
Per-User Info in Sharing BSS | STA ID
 | Nss
Category | Information
Control | ‘Co-BF Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier
 | Extra LTF Allowed
 | Number of CoBF Users in shared BSS
Per-User Info in Shared BSS | STA ID
 | MCS
 | Nss
 | 2xLDPC
Category | Information
Control | ‘Co-BF Sync’
PHY Common Info | Length
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | BSS Color 1, BSS Color 2
 | TXOP
 | Number of UHR-SIG Symbols
 | GI+LTF Size
 | Number Of UHR-LTF Symbols
 | Number of Co-BF Users
Per-User Info in Both BSS | STA ID
 | BSS Color Indication
 | MCS
 | Spatial Configuration
 | 2xLDPC