## Slide 1: Tx Power Control Clarifications for Co-SR
Date: 2025-07-15
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Jason Yuchen Guo |  |  |  | 
Genadiy Tsodik |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
The following consensus has been reached regarding co-SR information exchange:
  In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent Co-SR transmissions:
    The transmit power limit of the shared AP
      The shared AP Tx power limitation indicated by the sharing AP should not be lower than the minimum TX power indicated by the shared AP in its request.
    The transmit power of the sharing AP
  [Motion #429, [264] and [283, 390, 391]]
  In this proposal, we further elaborate how target station is selected based on current passed motion.

## Slide 3: How does the current power control signaling work
Step 1: AP2 indicates its minimum acceptable TX power during MAPC agreement setup
  Note-the value of this minimum acceptable TX power is chosen based on the range of STAs (inner STAs of AP2’s BSS) that AP2 is going to serve during Co-SR transmission
Step 2: AP1 determines the TX power limit of AP2 and its own TX power based on:
  Its target STA – STA1
  The target MCS/NSS for STA1, e.g. based on the traffic of STA1 and the pathloss between STA1 and AP2/AP1
  And indicate them to AP2 in the Co-SR Trigger frame
Co-SR Setup Request
Invite
Response
Co-SR Setup Response
Co-SR Trigger
Data PPDU
Data PPDU
Minimum acceptable TX power
TX power limit of AP2
TX power of AP1

## Slide 4: How does the current power control signaling work
Step 3: before receiving the Co-SR Trigger, AP2 already has its target STA in mind (based on the minimum power and max Tx Power of AP1); TX parameters (MCS/Nss) can also be estimated based on that.
After receiving the Co-SR Trigger, AP2 knows its real TX power limit, and can further determine its final MCS/Nss if needed.
Moreover, the current method supports the case with multiple Co-SR Triggers in a TXOP
Invite
Response
Co-SR Trigger
Data PPDU
Data PPDU
TX power limit of AP2
TX power of AP1
ACK
Co-SR Trigger
Data PPDU
Data PPDU
TX power limit of AP2
TX power of AP1
ACK
If error happens in the previous transmission, AP1 can indicate a different TX power limit for AP2 to increase robustness
Or, if target STA of AP1 changes, AP1 can indicate a different Tx Power limit for AP2

## Slide 5: Summary
In this contribution, we elaborate how target station is selected based on current passed IEEE motion.

## Slide 6
11-24-0209-16-00bn-specification-framework-for-tgbn, Ross Jian Yu (Huawei)
References