## Slide 1: Padding requirement for cross-BSS Trigger frame
Date: 2025-07-15
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Jason Yuchen Guo |  |  |  | 
Genadiy Tsodik |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
For a TB PPDU transmission, a user needs a plenty of MAC padding to respond TB PPDU (MinTrigProcTime: 0/8/16 us).

## Slide 3: Padding requirement for cross-BSS Trigger frame
For cross BSS sounding, the BFRP TF is sent assume the other AP will parse the TF itself, prepare the TRIGvector, and then receive the BF report. The other AP also needs a MAC padding requirement for these reception and processing.

## Slide 4: Padding requirement for cross-BSS Trigger frame
The time required by the other AP can be:
  pre-negotiated during MAPC setup period
  or set to a fixed value (e.g., 16us, preferred for simplicity).

## Slide 5: Summary
In this contribution, we discuss the padding requirement for cross-BSS Trigger frame during sounding procedure.

## Slide 6: Straw Poll #1
Do you agree to add the following into 11bn SFD?
  When an AP transmits BFRP trigger frame during a cross BSS sounding or joint sounding, the AP shall ensure the MAC padding duration is larger than a predefined value (e.g., 16us).

## Slide 7
11-24-0209-16-00bn-specification-framework-for-tgbn, Ross Jian Yu (Huawei)
11-24-1542-05-00bn-sounding-schemes-for-coordinated-beamforming, Sameer Vermani (Qualcomm)
References