## Slide 1: CSI Process in a Joint Sounding
Date: 2025-07-19
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei | Ottawa, ON Canada |  | junghoon.suh@huawei.com
Mahmoud Hasabelnaby |  |  |  | 
Yan Xin |  |  |  | 
Osama AboulMagd |  |  |  | 
Abdalla Hussein |  |  |  | 

## Slide 2: Background
During a Joint Sounding, each STA associated with either Sharing or Shared AP needs to compute the CSI information based on the received NDPs sent from both the BSS and the OBSS APs
The CSI information is computed based on the estimated channel between the STA and the Sharing AP + the Shared AP
  The amplitude of the estimated channel with the OBSS AP can be likely to be much smaller than those with the BSS AP
    The angle quantization of the Givens-Rotation based CSI matrix may experience the Near-Far effect and may result in near-zero quantized angle (Psi) due to the large amplitude difference which may ends up sending the Quantization-noise only CSI feedback

## Slide 3: Actual Baseband Processor
Simple representation of a baseband processor above shows how the data can be passed between each function block, and the NU, ND and NP are the datapath size (unit: bits) between the function blocks
All the data are being represented in a fixed-point resolution beyond the ADC function block
For the estimated channels, the normalization with an amplitude of the estimated channel (real and imaginary components are separately done) is necessary to be represented in NP bits
AGC
ADC
FFT
GI Removal and
Channel Estimation
U
D
H
Maximum of the amplitude of U, MU
Maximum of the amplitude of D, MD
Maximum of the amplitude of H, MH, where H is the channel parameter
NU
ND
NP
Round( )
Round( )
)

## Slide 4: Recommended Process in the Channel Estimation function block
The N_SS in the Common field of EHT-SIG of NDP in the CoBF Joint Sounding is supposed to be 8, and the second 4 streams correspond to the streams of OBSS AP
The size of MIMO channel matrix estimated at each STA is NRX X 8, and the second four columns (5th to 8th columns of channel matrix) of the estimated MIMO channel matrix correspond to the channel between the OBSS AP and the STA
Within the Baseband processor, we may need to apply a different normalization to the MIMO channel matrix portion corresponding to the channel with OBSS AP, from the channel with In-BSS AP

## Slide 5: Recommended Process in the Baseband
AGC
ADC
FFT
U
D
Maximum of the amplitude of U, MU
Maximum of the amplitude of D, MD
Maximum of the amplitude of Hi, MHi, where Hi is the channel estimation output with In-BSS AP
NU
ND
NP
Round( )
Round( )
)
CSI
Quantization
Maximum of the amplitude of Ho, MHo, where Ho is the channel estimation output with OBSS AP
NP
H
)
GI Removal, Channel Estimation and Smoothing
Hi
Ho
SVD is applied
to

## Slide 6: Joint Sounding Indication for STA
The figure above shows the STA Info field format of the EHT NDPA.
Option 1: We propose to set B20 (or any Reserved subfield such as B29 to B31) above to “Joint Sounding” so that the receiving STA may know the following NDPs are transmitted from two coordinating APs
  That is, the UHR STA needs to check the Joint Sounding for the CoBF using B20, and B20 set to 0 may indicate the following NDP to be a Single AP Sounding regardless of Cross-BSS or In-BSS Sounding
  B20 set to 1 may indicate the following NDP coming from two separate APs in a Joint Sounding
Option 2: Repurpose one of the bit from Nc Index such as B24 to indicate the Joint Sounding, since the Nc parameter cannot be bigger than 8, and three bits may be enough for Nc parameter and the remaining one bit can be repurposed to indicate the Joint Sounding
Option 3: Each STA can choose to parse the 1st STA Info field and the 2nd STA Info field upon seeing the AID11 2047 from the 1st STA Info field, and the “Number of Spatial Streams” subfield in the 2nd STA Info field may imply the Joint/Sequential Sounding
(2047)
1st STA Info field
2nd STA Info field

## Slide 7: Ind. Normalization vs. Joint Normalization
4 TX per each AP
2 RX per each STA
Full Nulling based Precoder [1] based on Joint Sounding
  Joint Normalization for In-BSS and OBSS Channel portions VS. Individual Normalization for In-BSS and OBSS Channel portions (Our Proposal)
  SVD is applied to the 2X8 Big Channel
  Perfect quantization assumed
20 MHz/BCC/MCS 7
X dB : 10 and 20 dB lower in OBSS link than In-BSS link
AP 1
STA 0
AP 2
STA 2
0 dB
-X dB
-X dB
0 dB
Precoder computed based on 2 STS but only a single stream is transmitted to each STA
  2 Streams based 4 LTFs per AP
  Random data is transmitted for the 1st stream
  Zero-energy constellation of data is transmitted for the 2nd stream

## Slide 9
In a Sequential Sounding, the Estimated Channel is normalized before the CSI Quantization, individually for the In-BSS Channel or the Cross-BSS Channel
The same amplitude of Channels are quantized regardless of In-BSS or OBSS Channel in a Sequential Sounding  Supposed not to impact on the Nulling based Beamforming Performance

## Slide 10: DL MU-MIMO
Each STA prepares the CSI report based on its own estimated and normalized channel parameters
Precoder is computed based on the CSI report from each STA regardless of the distance from the AP or how it normalized
In AP side, there has been no need to know the ratio of the amplitude of the estimated channel from each STA for any MU-MIMO precoder computation
Precoder element is normalized again with the Frobenius norm of the Precoder matrix
AP
STA0
STA1
STA2
H0
H1
H2
is reconstructed based on
CSI Feedback for

## Slide 11: Summary
We proposed to separately process the fixed-point normalization in the Baseband processor for the channel matrix with In-BSS AP and for the channel matrix with OBSS AP
  The Near-Far effect in the CSI Quantization is minimized
Each STA needs to know the Joint Sounding, so it separates the In-BSS or OBSS portion of Channel matrix before the fixed-point normalization

## Slide 12: Reference
[1] I. Jung, et. al., “24/1204r0 Coordinated Beamforming for 11bn”

## Slide 13: SP 1
Do you agree to have an option of individually processing the fixed-point normalization to the Estimated Channel in In-BSS portion and OBSS portion in case of Joint Sounding?

## Slide 14: SP 2
Do you support to let each STA know the Joint Sounding in the UHR NDPA?
  How to indicate the Joint Sounding is TBD