## Slide 1: Misc. PHY Topics
Date: 2025-07-21
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 
Karim Toussi | Broadcom |  |  | 
Dignus-Jan Moelker | Broadcom |  |  | 

## Slide 2: Topic 1 – Nltf in DL OFDMA+MU-MIMO
Currently in D0.3 (page 290):
  In order to improve the MIMO channel estimation for the reception of non-OFDMA UHR MU PPDU or UHR sounding NDP, the number of UHR-LTFs may be larger than the initial number of UHR-LTFs determined by the total number of spatial streams. If additional UHR-LTFs are used, then the total number of UHR-LTFs (which is signaled separately from Nss) shall be no more than twice the initial number of UHR-LTFs determined by the number of spatial streams as shown in Table 38-39 (Initial number of UHRLTFs required for different number of spatial streams), and chosen from the set {2 4 8}. Supporting additional UHR-LTFs is optional for the receiver.
It makes sense to us to expand this limitation of using the set {2,4,8} to any MU PPDU carrying MU-MIMO in one of the RU (partial BW MU-MIMO)

## Slide 3: Topic 2 – COSR padding
Currently in D0.3 (page 312):
  For a UHR MU PPDU with the Co-BF or Co-SR transmission, the nominal packet padding value shall be equal to 20 μs, and the pre-FEC padding factor α shall be equal to 4. This leads to a fixed value equal to 20 μs.
However Co-SR is not limited to UHR (can use EHT). It makes sense to extend this to Co-SR in general to unify the design
Currently in the SFD:
  Use fixed values for the following fields in the Co-BF transmission
    UHR-SIG MCS is fixed to MCS0
    Spatial Reuse is fixed to ‘PSR_AND_NON_SRG_OBSS_PD_PROHIBITED’
    LDPC Extra Symbol Segment is fixed to 1
    PE Disambiguity is fixed to 1
  [Motion #433, [264] and [393, 326, 322, 323]]
It makes sense to extend “LDPC Extra Symbol Segment is fixed to 1” to Co-SR to align with Co-BF design

## Slide 4: SP#1
Do you agree to include the following into the 11bn SFD: The number of LTF is limited to the set {2,4,8} for any MU PPDU carrying MU-MIMO in at least one RU or MRU

## Slide 5: SP#2
Do you agree to include the following into the 11bn SFD:
  “LDPC Extra Symbol Segment is fixed to 1” for all CoSR modes transmissions that use LDPC

## Slide 6: SP#3
Do you agree to modify the text in D0.3 as follows (changes highlighted in yellow):
  For a UHR MU PPDU with the Co-BF or any mode of Co-SR transmission, the nominal packet padding value shall be equal to 20 μs, and the pre-FEC padding factor α shall be equal to 4. This leads to a fixed value equal to 20 μs.