## Slide 1: COSR Information Exchange
Date: 2025-07-28
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Kaiying Lu |  |  |  | 
Eric Pc |  |  |  | 
Hsin-chun Huang |  |  |  | 
Julia Feng |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
  The basic frame exchange for COSR was discussed in [1], and in this contribtuion we will discuss the information carried within those frames.

## Slide 3: Recap: Frame exchange for COBF/COSR
It is desirable to have a common framework for both COBF and COSR.
  To simply the standard design.
Prefer to exchange necessary info for performing COBF/COSR.
  To simply the carried info
Prefer to confirm and carry self-contained info for COBF/COSR PPDU transmission.
  To simply the implementation.
Sharing AP STA
AP1
Shared AP STA
AP2
COBF/COSR PPDU
  Exchange necessary Info for performing CoBF/CoSR PPDU transmission.
Invite
  Confirmed COBF/COSR transmission and provided the confirmed info (self-contain).
non-AP STA2
non-AP STA1
Response
Sync
COBF/COSR PPDU
  Detailed frame exchange will be determined in MAC

## Slide 4: Information exchange in Invite/Response
Prefer to have similar structure as COBF and resue defined subfields as much as possible.
  Additional subfield from passed motions are highlighted in blue.
Subfield | Invite | Response
MAP control | COSR Invite | COSR Acceptance
Minimum Number of Data OFDM Symbols | Yes | 
Maximum Number of Data OFDM Symbols | Can be the same as the minimum data sym or Reserved | 
Suggested Number of Data OFDM Symbols |  | Sam rule as COBF
PHY version | Sharing AP PHY version | Shared AP PHY version
Bandwidth | Yes | Yes (Shared AP)
Punctured Channel Information | Yes | Yes (Shared AP)
GI+LTF Size | Yes | 
Number Of LTF Symbols | Yes | 
Sharing AP TX power | Yes | 
Shared AP TX power limit | Yes | 
Shared AP TX power |  | Can only lower than the TX power limit
  Additional information may be carried in Invite/Response depends on MAC discussions.

## Slide 5: Packet length information
It is preferred to reused these subfields defined in COBF to indicate the packet length in COSR transmission. Since Sharing AP can determine its NSS and MCS of the COSR PPDU, we can indicate the exact value in the COSR Invite.
  Maximum/Minimum Number of Data OFDM Symbols can be the same.
Shared AP can indicate the” Suggested Number of Data OFDM Symbols”, which can only be higher than the value indicated in the COSR Invite.
  The request may not be accepted by the sharing AP (same as in COBF).
Number of LTF symbols and GI+LTF Size are also indicated in the COSR Invite for PPDU length alignment.

## Slide 6: Power control subfields
  To better help APs to select its STAs and the corresponding MCS:
  In the COSR Invite, the sharing AP indicate its TX power and the shared AP TX power limit.
  In the COSR Response, the shared AP indicates its desired TX power, which can only be lower than the TX power limit in the COSR Invite.
  All the power related subfield can be indicated in units of dBm/20MHz. (same method in the current Common Info field in a Trigger frame)

## Slide 7: References
[1] COSR Misc, 25/869r2