## Slide 1: Discussions on Cross-BSS Sounding
Date: 2025-05-15
Authors:

## Slide 2: Abstract
In this contribution, we discuss two topics related to CoBF sounding
  Options for how the cross-BSS sounding can be performed
  Indication of cross-BSS sounding failure in CoBF sounding

## Slide 3: Background
CoBF is a new feature in 11bn [1]
Both in-BSS sounding and cross-BSS sounding are essential for the successful operation of CoBF
CoBF is performed in two phases:
  Sounding phase
  Data transmission phase
CoBF Sounding can be performed either sequentially or jointly
The sequential CoBF sounding is also performed in two subphases
  in-BSS sounding subphase
  cross-BSS sounding subphase

## Slide 4: CoBF Sounding
In sequential CoBF sounding, in-BSS sounding and cross-BSS sounding are independent and may be performed disjointly.
  We propose to perform the two sounding phases independently
Cross-BSS sounding is more prone to failure and may need special treatment
  The indication of the cross-BSS sounding failure is crucial to efficient CoBF operation

## Slide 5: Cross-BSS Sounding in One TXOP
There may be several options for how cross-BSS sounding can be performed
  Option 1: Both cross-BSS sounding for AP1 and AP2 are performed in the same TXOP
    Pros: Efficient, no need to repeat the invite/response exchange for each cross-BSS
    Cons: Not flexible, ties both cross-BSS sounding sequences

## Slide 6: Cross-BSS Sounding in Two TXOPs
  Option 2: Each cross-BSS sounding is performed in a separate TXOP
    Pros: Flexible, each AP performs its cross-BSS separately at its convenience
    Cons: Not efficient, need to repeat the invite/response exchange for each cross-BSS

## Slide 7: Indication of Cross-BSS Sounding Failure
There may be 3 different options for the indication of cross-BSS failure
  Option A: During cross-BSS sounding
    Use NDPA to indicate the failure of the preceding cross-BSS sounding
  Option B: After cross-BSS sounding [2]
    Use another explicit frame exchange after the cross-BSS sounding
  Option C: In the data transmission phase [3]
    Use a rejection reason in the CoBF Response
We propose Option A as another method for the indication of cross-BSS sounding failure
  cross-BSS sounding failure can be early indicated in the sounding phase without the need to define any more frame exchanges

## Slide 8: Indication of Cross-BSS Failure in NDPA (1/2)
One or more bit(s) in the second STA Info field can be used to indicate that the preceding cross-BSS CSI was not received successfully.
  By receiving this indication, AP1 learns the CSI feedback status of cross-BSS1
  AP1 will receive the CSI in cross-BSS2 and can determine whether it is received successfully or not

## Slide 9: Indication of Cross-BSS Failure in NDPA (2/2)
If AP1 is the TXOP holder in the data transmission phase, no need for further indications
If AP2 is the TXOP holder in the data transmission phase, AP1 may reject with a reason indicating the failure of receiving cross-BSS2

## Slide 10: Comparison of Mechanisms to Indicate Cross-BSS Sounding Failure
Options | Pros | Cons
Option A NDPA Indication | No need to define another frame exchange Efficient, less overhead Early indication of the failure in the sounding phase. | If the sounding responder is the TXOP holder, we may need another indication of the failure.
Option B Explicit Indication | Explicit May allow for the repetition of the sounding process before data transmission | Adds more overhead to the sounding process
Option C Data Transmission Indication | No need to define another frame exchange Efficient, less overhead | Last-minute indication, performed in the data transmission phase No chance to repeat the channel sounding at this point

## Slide 11: Conclusions and Way Forward
Cross-BSS Sounding can be performed disjointly from in-BSS sounding
It may be better to perform the cross-BSS sounding for both APs in the same TXOP
A simple indication in the NDPA may be used for early indication of cross-BSS sounding failure.
Indication of the cross-BSS sounding failure as one of the reasons for rejection in the data transmission phase is another viable solution
  When combined with indication of failure in NDPA, it will allow for the efficient and early indication of cross-BSS sounding failure.

## Slide 12: References
[1] IEEE P802.11bn™/D0.2: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, March 2025
[2] Information Exchange between CBF APs (Intel)
[3] Further Considerations on Co-BF Sounding (Huawei)