## Slide 1: DBE Operation with NPCA
Authors:

## Slide 2: Introduction
TGbn is defining DBE (Dynamic Bandwidth Expansion) feature:
  Dynamic bandwidth expansion (DBE) is a mode of operation that allows a UHR AP to dynamically enable operation with an expanded bandwidth that is greater than the BSS bandwidth and up to the AP’s maximum supported bandwidth for DBE, for UHR non-AP STAs that support DBE mode.”
When AP is operating in DBE mode with expanded BW (DBE BW), AP’s primary channel remains unchanged. If AP supports NPCA (Non primary channel access), then NPCA operation can be performed over the expanded DBE BW after DBE mode is enabled.
Here we propose behavior for DBE operation with NPCA.

## Slide 3: Recap - DBE High-level Operation
DBE enables an AP to dynamically expand its operating BW for DBE supporting STAs.
DBE BW change is announced in Beacon, Probe Resp etc. using UHR critical update advance notification mechanism before bandwidth expansion takes effect.
  During DBE mode, AP and DBE supporting STAs operate with min of AP’s DBE BW + DBE BW supported by STAs
  Any subsequent DBE BW change (e.g. 160->320 MHz) or reset to BSS BW is announced in Beacon using the same critical update advance notification mechanism

## Slide 4: DBE operation with NPCA (1)
When DBE mode is enabled, an AP is operating over expanded DBE BW (e.g. to 160/320 MHz), then AP can enable NPCA operation over the wider DBE BW (if desired), which may enable NPCA over a cleaner primary channel

## Slide 5: DBE Operation with NPCA (2)
When DBE mode is enabled, some STAs will be operating over DBE BW and some STAs may be operating over BSS BW (non-DBE supporting STAs)
Based on the DBE support/enablement and NPCA support/enablement from STAs, AP may decide to enable NPCA over the DBE BW, after DBE mode is enabled
  E.g. enable NPCA over DBE BW if most STAs support/enable DBE mode + NPCA
Two cases are possible:
  Case 1: NPCA was disabled before DBE mode is enabled.
  Case 2: NPCA was enabled before DBE mode is enabled.
  In these cases, after DBE mode is enabled, AP can support NPCA over the DBE BW by enabling NPCA over DBE BW (case 1) or by updating NPCA PCH and other parameters (case 2)

## Slide 6: DBE Operation with NPCA (3)
AP signals only one NPCA PCH when DBE mode is enabled (as in 11bn D1.0)
  Allow NPCA PCH to be within the DBE BW or within the BSS BW  need to relax current NPCA rules of NPCA PCH to be always in the secondary subband
  If more STAs operating over DBE BW, then makes sense for NPCA PCH to be within DBE BW. Only DBE STAs can perform NPCA.
  If more STAs operating over BSS BW, then makes sense for NPCA PCH to be within BSS BW. Both non-DBE and DBE STAs can use NPCA.
  Having only one NPCA PCH is preferred to avoid AP and STAs switching to different NPCA PCH
To support NPCA over DBE BW, following aspects need to be addressed:
  Indicating capability support for NPCA over DBE BW
  Enablement of NPCA over the DBE BW by the APand STA)
  Allow NPCA PCH to be outside of BSS BW
    Define rules such that non-DBE supporting STAs stop using NPCA when NPCA PCH is outside the BSS BW.

## Slide 7: DBE Operation with NPCA (4)
Capability signaling for NPCA over the DBE BW
  Extend NPCA Supported field to indicate NPCA is supported over BSS BW or DBE BW
    If a STA/AP supports DBE and supports NPCA, it supports NPCA over both BSS BW and DBE BW.
    If a STA/AP does not support DBE, the NPCA Supported indicates NPCA support over the BSS BW
NPCA Enablement signaling over the DBE BW from AP
  Extend existing ‘NPCA Enabled’ bit in UHR Operation to also indicate NPCA is enabled over DBE BW when DBE is enabled
    If NPCA PCH is within the BSS BW, then NPCA is enabled for both BSS BW and DBE BW, Both non-DBE supporting STAs and DBE supporting STAs can perform NPCA.
    If NPCA PCH falls outside the BSS BW, then NPCA is only enabled for DBE BW. Non-DBE supporting STAs do not perform NPCA in this case.

## Slide 8: DBE Operation with NPCA (5)
NPCA critical update for NPCA enable/update over DBE BW
  To enable NPCA over DBE BW, AP needs to send a critical update for NPCA that indicates:
    NPCA PCH within the DBE BW (or in BSS BW)
    NPCA Disabled Subchannel Bitmap parameter for the DBE BW
  Even if NPCA was already enabled for BSS BW, AP would need to send NPCA critical update to update NPCA PCH and/or NPCA Disabled Subchannel Bitmap
  NPCA critical update shall have a Countdown Timer value such that NPCA critical update takes effect at the same TBTT or a later TBTT as the related DBE mode enable/update critical update
    Typically, NPCA should be enabled/updated at the same TBTT as DBE mode

## Slide 9: DBE Operation with NPCA (6)
STA side enable/disable of NPCA over the DBE BW
  STA needs to enable/disable NPCA over DBE BW with the AP (using generic OM and parameter updates mechanism) to be able to perform NPCA over the DBE BW
  It is important for AP to know which STAs can perform NPCA over the DBE BW, to decide if NPCA should be enabled over the DBE BW
  Propose that for STAs that support both NPCA and DBE, NPCA enablement from STA enables NPCA for both BSS BW and DBE BW.
    Same NPCA switching delay parameters apply for NPCA over the DBE BW.
    If STA does not support DBE, then naturally NPCA enablement only enables NPCA for the BSS BW
    To avoid gold rush of NPCA enablement over the DBE BW when DBE mode is enabled by the AP, DBE supporting STAs should enable DBE and NPCA even before DBE mode is enabled

## Slide 10: Summary
We propose that AP defines only one NPCA PCH when NPCA is enabled over DBE BW
  Allow NPCA PCH to be within the DBE BW or within the BSS BW  need to relax current NPCA rules of NPCA PCH to be always in the secondary subband.
  If NPCA PCH is within BSS BW, both DBE and non-DBE STAs can perform NPCA.
  If NPCA PCH is outside the BSS BW and in the DBE BW, only DBE STAs can perform NPCA. Non-DBE STAs do not perform NPCA in this case.
To support NPCA over the DBE BW, we define following aspects:
  Indicating capability support for NPCA over DBE BW – leverage existing NPCA Supported field
  NPCA enablement signaling for NPCA over the DBE BW from the AP – existing NPCA Enabled in UHR Operation also indicates NPCA enabled over DBE when DBE mode is enabled
  NPCA critical update for NPCA enable/update over the DBE BW – AP needs ti an NPCA CU to indicate NPCA parameters for DBE BW (NPCA PCH, NPCA Disabled Subchannel for DBE BW).
  STA side enable/disable of NPCA over the DBE BW – for DBE supporting STAs NPCA enablement enables NPCA for both BSS BW and DBE BW

## Slide 11: Straw Polls (1)
SP1:
Do you support to extend the NPCA Supported field to indicate that NPCA is supported over the BSS BW or the DBE BW?
  If a STA/AP supports DBE and supports NPCA, it supports NPCA over both the BSS BW and the DBE BW.
  If a STA/AP does not support DBE, then NPCA Supported field indicates NPCA support over the BSS BW only.
SP2:
Do you support to extend the existing NPCA Enabled field in UHR Operation to also indicate NPCA enablement over DBE BW when DBE mode is enabled?
  If NPCA PCH is within the BSS BW, then NPCA is enabled for both the BSS BW and the DBE BW when DBE mode is enabled. Both DBE and non-DBE STAs can perform NPCA.
  If NPCA PCH falls outside the BSS BW and in the DBE BW, then NPCA is only enabled for the DBE BW. Non-DBE STAs shall not perform NPCA in this case.

## Slide 12: Straw Polls (2)
SP3:
Do you support that when DBE mode is enabled or DBE BW is changed, to enable NPCA over the DBE BW AP may send a critical update for NPCA that indicates?
  NPCA PCH within the DBE BW or BSS BW + NPCA Disabled Subchannel Bitmap parameter for the DBE BW
  NPCA critical update shall take effect at the same TBTT or a later TBTT as the related DBE mode enable/update critical update
SP4:
Do you support that for a STA that support both NPCA and DBE, NPCA enablement from STA enables NPCA for both the BSS BW and the DBE BW (supported by the STA)?
  Same NPCA switching delay parameters apply for NPCA over the DBE BW.
  To avoid gold rush of NPCA enablement over the DBE BW when DBE mode is enabled by the AP, DBE supporting STAs should enable NPCA (and DBE) even before DBE mode is enabled.

## Slide 13: References
[1] Draft P802.11bn Draft 1.0
[2] 11-24/0088 “Maximizing channel bandwidth in dense AP deployments”
[3] 11-24-0815 “Dynamic Bandwidth Selection Signaling Details”
[4] 11-24/0209 “Specification Framework for TGbn”