## Slide 1: Enhancement of Co-BF Procedure
Date: 2025-07-24
Authors:

## Slide 2: Introduction
TGbn has defined Coordinated beamforming (Co-BF) as one of specific multi-AP coordination schemes [1-2].
TGBn has agreed to include invite, response and sync/trigger frames for information exchange between participating APs, i.e., coordinating AP and coordinated AP, for use of Co-BF procedure (Co-BF transmission sequence) [3-11].
In this contribution, we propose methods to improve the COBF procedure.

## Slide 3: Recap: Information Exchange of Co-BF Procedure
The coordinating AP (AP1) may send the invite frame indicating parameters of PHY common info. and per-User info in AP1’s BSS intended being used for the Co-BF transmission.
  E.g., Min/max numbers of data OFDM symbols, BW, punctured channel pattern., GI+LTF size, max. total Nss allowed for AP2, num. of CoBF users in BSS2, and Per-User info in AP1’s BSS: STA ID and Nss
The coordinated AP (AP2) may send the response frame indicating suggested parameters of PHY common info. and per-User info in AP2’s BSS.
  E.g., Suggested num. of data OFDM symbols, extra LTF allowed, num. of CoBF users in AP2’s BSS, and Per-user info in AP2’s BSS: STA ID, MCS, Nss and 2xLDPC.
AP1 may send the sync/trigger frame indicating the parameters determined to be used for the Co-BF transmission.
  E.g., PPDU length, BW, punctured channel pattern, BSS colors, TXOP, num. of UHR-SIG symbols, GI+LTF size, num. of UHR-LTF symbols, num of Co-BF users, and
  Per-user info in both BSS: STA ID, BSS colors of AP1 or AP2, MCS, spatial configuration, and 2xLDPC.

## Slide 4: COBF Transmission with Large Amount Data
AP1 and AP2 may respectively have large amount data buffered to be send to their associated STAs. AP1 and AP2 may use 1st COBF invite/response frames of 1st COBF transmission during TXOP1 to exchange parameters for their buffered data.
AP1 may indicate parameters with less resource in the COBF trigger frame, so that AP1 and AP2 cannot send all buffered data (e.g., to STA1 and STA2 respectively) during the 1st COBF transmission.
Example 1: AP1 determines a PPDU length in the 1st COBF trigger frame that is smaller than the equivalent PPDU length corresponding to the suggested number of OFDM symbols (and number of spatial streams) by AP2 in response frame.
Example 2: AP2 may have additional data buffered for STA3 indicated in the 1st COBF invite frame; but AP1 determines the 1st COBF transmission only including STA1 and STA2.
AP1 may access the channel to obtain TXOP2. AP1 may send a 2nd invite frame to schedule a 2nd COBF transmission for remaining buffered data with AP2 to STA1 and STA2 (and STA3).
Problem: Signaling overhead occurs on invite/response frame exchange between two APs before each consecutive COBF procedure/transmission.

## Slide 5: Successive COBF Transmission
During TXOP1, AP1 sends to AP2 the 1st COBF trigger frame indicating a 2nd COBF transmissions being scheduled after the 1st COBF transmission completes.
  The 2nd COBF transmission is for use of transmitting remaining buffered data.
Without additional invite/response frame exchange, AP1 that obtains the 2nd TXOP sends a 2nd trigger frame indicating the parameters for the 2nd COBF transmission.
  Parameters indicated in the 2nd COBF trigger frame can be determined based on the previous COBF invite/response frames and the 1st COBF trigger frame.
  Example shows that AP1 obtains TXOP2.

## Slide 6: Summary
In this contribution, we shared some thoughts of Co-BF procedure.
  The COBF trigger frame may indicate a follow-up Co-BF transmissions being scheduled after the COBF transmission completes.
  The follow-up Co-BF transmission may use the information exchange during the last Co-BF transmission without additional invite/response frame exchange during the follow-up Co-BF transmission.

## Slide 7: Straw Poll 1
SP1. Do you support the Co-BF procedure that includes the following?
  A Co-BF coordinating AP of a Co-BF transmission may indicate another (or a follow-up) Co-BF transmission to be scheduled after the Co-BF transmission in a Co-BF trigger frame during the Co-BF transmission.
  Yes
  No
  Abstain

## Slide 8: Straw Poll 2
SP2. Do you support the Co-BF procedure that includes the following?
  A participating AP of a Co-BF transmission may initiate a follow-up Co-BF transmission without transmitting a Co-BF invite frame when the follow-up Co-BF transmission is scheduled after the Co-BF transmission.
  Note: The participating AP of the Co-BF transmission may be the Co-BF coordinating AP or the Co-BF coordinated AP of the Co-BF transmission.
  Yes
  No
  Abstain

## Slide 9: References
Draft P802.11bn D0.1
11-24/0209: Specification Framework for TGbn, Ross Jian Yu (Huawei)
11-25/0768r2, PDT MAC CR Coordinated beamforming protocol, Jason Yuchen Guo (Huawei)
11-25/0842r1, Information Exchange in the COBF Transmission Phase Follow-Up, Alice Chen (Qualcomm)
11-25/0389r2, Information Exchange in the COBF Transmission Phase, Alice Chen (Qualcomm)
11-25/0399r1, COBF/COSR Design Follow-up, You-wei Chen (Mediatek)
11-25/0401, CoBF PHY design consideration, Juan Fang (Intel)
11-24/1822r4, COBF Design for UHR, Sameer Vermani (Qualcomm)
11-24/2060, CSR/COBF Protocol Design, Kosuke Aio (Sony)