## Slide 1: Discussion on Co-BF Procedure
Date: 2025-07-23
Authors:

## Slide 2: Introduction
TGbn has defined Coordinated beamforming (Co-BF) as one of specific multi-AP coordination schemes [1-2].
Co-BF transmission sequence has been discussed for recipient STAs that support EMLSR or DPS mode [3-7].
In this contribution, we discuss termination of the COBF procedure.

## Slide 3: Recap: Co-BF Procedure with DPS/EMLSR STAs
  A Coordinating AP (AP1) and a coordinated AP (AP2) may perform a Co-BF invite/response frame exchange to begin the Co-BF procedure.
  Each participating AP may respectively perform an ICF/ICR frame exchange with its recipient STAs.
    STA1 and STA2 respectively transition from a listening state to an awake status of EMLSR or from a lower capability mode to a higher capability mode of DPS mode.
  AP1 may send a Co-BF trigger frame to AP2 to final sync and start their concurrent transmissions (PPDU1 and PPDU2) to STA1 and STA2 respectively.

## Slide 4: Co-BF Procedure with No-Response DPS/EMLSR STA
STA1 may be interfered by an OBSS STA and fail to receive an ICF1 from the coordinating AP (AP1). Consequently, STA1 may fail to send an ICR1.
Both AP1 and the coordinated AP (AP2) don’t receive/hear the ICR1 from STA1.
AP1 may back off and resend the ICF1 using EDCA. AP1 may resend ICF1 for multiple times, resulting an incremental delay to continue the remaining COBF procedure.
AP2 may send an ICF2 to STA2 based on receiving ICF1. AP2 and STA2 complete the ICF2/ICR2 frame exchange.
AP2 may not know when to receive the COBF trigger frame from AP1.
  AP2 needs to wait for receiving the COBF trigger frame to continue the COBF procedure.
  STA2 may return to listening state of EMLSR or lower capability mode of DPS after switching back delay.
Above operation may cause COBF procedure inefficient.

## Slide 5: Termination of COBF Procedure
When AP1 fails to receive an ICR1 from STA1, AP1 decides to terminate the COBF procedure. PIFS after sending ICF1, AP1 sends a frame indicating a termination of COBF.

## Slide 6: Summary
In this contribution, we shared some thoughts of termination of Co-BF procedure in the presence of DPS/EMLSR STAs.

## Slide 7: Straw Poll 1
SP1. Do you support defining a termination operation for Co-BF procedure or Co-BF transmission sequence?
  Yes
  No
  Abstain

## Slide 8: Straw Poll 2
SP2. Do you support defining a termination operation for Co-BF procedure (or Co-BF transmission sequence) that includes the following?
  A participating AP of a Co-BF procedure may terminate the Co-BF procedure, based on failing to receive an ICR frame from a recipient STA in response to an ICF during the Co-BF procedure.
  Yes
  No
  Abstain

## Slide 9: References
Draft P802.11bn D0.3
11-24/0209: Specification Framework for TGbn, Ross Jian Yu (Huawei)
11-25/0942r1, MAC PDT 37.8.2.1 COBF
11-25/1191r0, COBF Misc, You-Wei Chen (Mediatek)
11-25/0879r2, CoBF Frame Sequences and Signaling Details, Sherief Helwa (Qualcomm)
11-25/0412r3, CoBF Signaling Details, Sherief Helwa (Qualcomm)
11-25/0413r0, Supporting EMLSR STAs under CBF, Dibakar Das (Intel)