## Slide 1: Further Thoughts on Co-TDMA Procedure
Date: 2025-07-18
Authors:

## Slide 2: Introduction
According to the Co-TDMA procedure defined in D1.0, a Co-TDMA coordinating AP shall announce its intention of allocating a portion of an obtained TXOP to another AP in an ICF sent at the beginning of the TXOP.
  The ICF polls one or more APs to solicit response(s) from polled AP(s) regarding their intent to receive a time allocation within the TXOP.
Based on the responses to the ICF, the Co-TDMA coordinating AP may allocate portion(s) of the obtained TXOP to the polled AP(s).
In this contribution, we consider a scenario, where the allocated portion of the TXOP may not be adequate for a Co-TDMA coordinated AP to transmit its buffered traffic, and provide some solutions.

## Slide 3: Recap: Co-TDMA Procedure
After the ICF-ICR exchange, a Co-TDMA coordinating AP (e.g., AP1) may perform frame exchanges within BSS1 before allocating portion(s) of its TXOP to Co-TDMA coordinated AP(s) (e.g., AP2 and/or AP3).
AP1 may then allocate a portion of an obtained TXOP sequentially to one or more non-colocated APs.
  Initially, AP1 may allocate a portion of the obtained TXOP to AP2. If a TXOP return is solicited by AP1, AP2 returns the TXOP to AP1.
  AP1 may then allocate another portion of the obtained TXOP to AP3.
ICR
Frame exchanges within BSS1
MRTT
AP1
AP2
AP3
CTS
(Co-TDMA sharing AP)
Frame exchanges within BSS2
MRTT
CTS
Frame exchanges within BSS3
ICF
ICR
TXOP of AP1
TXOP allocated to AP2
TXOP allocated to AP3
TXOP Return
Ack

## Slide 4: Problem: Discarding Some Data by an AP
While allocating portion(s) of TXOP to Co-TDMA coordinated APs, AP1 may not allocate an adequate portion of its obtained TXOP to AP2 and/or AP3.
For example, AP1 may determine to allocate to AP2 a limited portion of TXOP, where AP2 may not be able to transmit its buffered data timely.
  As a result, AP2 may have to discard some of its buffered data (e.g., low latency data).
ICR
Frame exchanges within BSS1
MRTT
AP1
AP2
AP3
CTS
(Co-TDMA sharing AP)
Frame exchanges within BSS2
MRTT
CTS
Frame exchanges within BSS3
ICF
ICR
TXOP of AP1
TXOP allocated to AP2
TXOP allocated to AP3
TXOP Return
Ack
Some data may be discarded by AP2

## Slide 5: Approach: AP Requesting More Time Allocation
If AP2 determines that it needs more time allocation for transmission of its buffered data, AP2 may transmit a frame to AP1 requesting more time allocation after the allocated portion of the TXOP.
  The frame may be a TXOP return frame (e.g., public action frame).
  In the TXOP return frame, AP2 may optionally further indicate requested duration, AC and/or TID values.
Based on the indication, AP1 may allocate to AP2 via an MU-RTS TXS Trigger (MRTT) frame a further TXOP duration in the current TXOP or in a future TXOP.
Data may be delivered timely
Indication
ICR
Frame exchanges within BSS1
MRTT
AP1
AP2
AP3
CTS
(Co-TDMA sharing AP)
Frame exchanges within BSS2
MRTT
CTS
Frame exchanges within BSS2
ICF
ICR
TXOP of AP1
TXOP allocated to AP2
TXOP allocated to AP2
TXOP Return
Ack

## Slide 6: Conclusion
In this contribution, we considered a scenario in the Co-TDMA procedure, where the allocated portion of the TXOP was not adequate for a Co-TDMA coordinated AP to transmit its buffered traffic.
As one approach, the Co-TDMA coordinated AP may transmit a TXOP return frame to the Co-TDMA coordinating AP to request more time allocation after the allocated portion of the TXOP.
  The TXOP return frame may optionally indicate requested duration, AC and/or TID values.
  Depending on the availability of resources, the Co-TDMA coordinating AP may allocate a further portion of the TXOP to the Co-TDMA coordinated AP.

## Slide 7: Straw Poll – 1
Do you agree to add the following text to the TGbn SFD?
During the Co-TDMA procedure, the TXOP return frame may be used to indicate that the Co-TDMA coordinated AP requests more time allocation after the allocated portion of the TXOP.
  Yes
  No
  Abstain
  Y/N/A: