## Slide 1: Co-BF Sounding Invite and Response
Date: 2025-07-26
Authors:

## Slide 2: Abstract
The Invite and Response frames for Co-BF sounding are used to ensure that the an AP is ready to perform Co-BF sounding before the another AP initiates the procedure. Similar situation applies to
- Co-BF Invite/Response
- Co-SR Invite/Response
In this contribution, we discuss more details regarding Invite and Response frames to ensure smooth operation of Co-BF sounding, and Co-BF and Co-SR transmissions.

## Slide 3: Co-BF Sounding Invite and Response
AP 1
AP 2
STA 1
Other STAs
Co-BF Sounding Invite
Co-BF Sounding Response
UHR NDP Announce
ment
EHT Sounding NDP
BFRP
Trigger
EHT Compressed Beamforming/CQI
ICF
ICR
NAV
9.2.5.2 Setting for single and multiple protection under enhanced distributed channel
access (EDCA)
In a Co-BF sounding invite or a Co-BF Sounding Response frame generated by a UHR STA as part of a cross-BSS UHR Co-BF sounding or Co-BF joint NDP sounding sequence the Duration/ID field is set as follows:
— In a Co-BF Sounding Invite frame, the Duration/ID field is set to the estimated time, in microseconds, required to transmit at least the UHR NDP Announcement frame sent by the Co-BF sounding initiator, plus one Co-BF Sounding Response frame, plus one NDP, plus applicable IFSs and any necessary ICF/ICR for STA(s).

## Slide 4: NAV Reset for Unsuccessful Invite
AP 1
AP 2
STA 1
AP 3
Co-BF Sounding Invite
Co-BF Sounding Response
NAV
Reset
37.2.1 Setting and resetting the NAV with BSRP Trigger frame
A UHR STA shall follow the rules defined in 10.3.2.4 (Setting and resetting the NAV), and the additional following rules:
- A STA that used information from an BSRP Trigger frame or a BSRP NTB Trigger frame as the most recent basis to update its NAV setting is permitted to reset its NAV if no PHY-RXEARLYSIG.indication or PHYRXSTART.indication primitive is received from the PHY during a BSRPNAVTimeout period starting when the MAC receives a PHY-RXEND.indication primitive corresponding to the detection of the BSRP Trigger frame or BSRP NTB Trigger frame. The BSRPNAVTimeout period is equal to (2 × aSIFSTime) + ICR_Time + aRxPHYStartDelay + (2 × aSlotTime).
When a Co-BF Sounding Invite frame fails to elicit a response (e.g., CCA busy at AP 2), STAs that set their NAV based on the Co-BF Sounding Invite frame may reset their NAV.
Co-BF Sounding Invite
Co-BF Sounding Response
UHR NDP Announce
ment
EHT Sounding NDP

## Slide 5: Problem: Co-BF Sounding Invite Rejection
AP 1
AP 2
STA 1
AP 3
Co-BF Sounding Invite
37.2.1 Setting and resetting the NAV with BSRP Trigger frame
A UHR STA shall follow the rules defined in 10.3.2.4 (Setting and resetting the NAV), and the additional following rules:
- A STA that used information from an BSRP Trigger frame or a BSRP NTB Trigger frame as the most recent basis to update its NAV setting is permitted to reset its NAV if no PHY-RXEARLYSIG.indication or PHYRXSTART.indication primitive is received from the PHY during a BSRPNAVTimeout period starting when the MAC receives a PHY-RXEND.indication primitive corresponding to the detection of the BSRP Trigger frame or BSRP NTB Trigger frame. The BSRPNAVTimeout period is equal to (2 × aSIFSTime) + ICR_Time + aRxPHYStartDelay + (2 × aSlotTime).
When a Co-BF Sounding Invite frame elicits a rejection response, the current rule does not allow a STA to reset the NAV. Hence if an AP decides to perform sounding with another AP, the other AP may not respond.
Co-BF Sounding Invite
Co-BF Sounding Response
Co-BF Sounding Response (Reject)
NAV

## Slide 6: Solutions
Option 1: APs that set their NAV based on a Co-BF sounding invite frame (or other invite frames) are permitted to reset the NAV if the responder of the Co-BF sounding invite frame rejects the invite frame.
Option 2: APs may ignore the NAV set by a TXOP owner AP (e.g., Co-BF sounding invite frame) when transmitting a response frame (e.g., Co-BF sounding response frame) to the TXOP owner AP.

## Slide 7: Rejection Reason
When an AP rejects an invite frame, it would be useful for the initiating AP to know the reason. For example, a reason code in the Co-BF sounding response frame may help the initiating AP what to do next.
AP 1
AP 2
STA 1
Co-BF Sounding Invite
Co-SR Invite
Co-BF Sounding Response (Reject)
Co-SR Response (Accept)
Reason: No traffic to Co-BF STAs

## Slide 8: Conclusion
We discussed two open issues regarding the invite/response mechanism for MAPC transmissions.
We proposed enhancements to NAV reset rules for invite/response between APs.
We also propose to indicate a rejection reason when an AP rejects an invite frame