## Slide 1: Further Considerations on DSO
Date: 2025-07-18
Authors:

## Slide 2: Introduction
According to the DSO defined in TGbn D1.0, a DSO non-AP STA has to switch back to the primary subband if the STA does not receive a frame addressed to itself after the ICF-ICR exchange.
In this contribution, we consider a scenario, where a DSO AP may need to transmit data to a DSO non-AP STA later during the TXOP, without having the DSO non-AP STA switching back to the primary subband. We explain the necessity for this kind of behavior on the DSO subband, and provide some solutions.

## Slide 3: DSO (1/2)
According to the DSO defined in TGbn D1.0, a DSO AP may request multiple DSO non-AP STAs to switch to the DSO subband using different RUs in a single DSO band.
On receiving responses to the ICF, DSO AP may transmit data simultaneously to DSO non-AP STAs that have switched to the DSO subband.
ICR
Data to STA1
AP
STA3
P80
P80
S80
S80
STA1
STA2
STA3
ICF
ICR
STA2
P80
S80
BA
ICR
STA1
P80
S80
BA
BA
Data to STA2
Data to STA3

## Slide 4: DSO (2/2)
One advantage of the DSO AP requesting multiple DSO non-AP STAs switch to a DSO subband is to enable the DSO AP to transmit data to a DSO non-AP STA via the full bandwidth, if the other STA does not respond [1].
  For example, AP may request STA2 and STA3 to switch to S80 subband, and STA3 may fail to switch. In that case, AP may transmit data to STA2 via the full bandwidth available (e.g., via 80 MHz).
ICR
Data to STA1
AP
STA3
P80
P80
S80
S80
STA1
STA2
STA3
ICR
STA2
P80
S80
BA
ICR
STA1
P80
S80
BA
Data to STA2
ICF

## Slide 5: Problem: Switching Back
In a likely scenario, AP may have shorter duration low latency buffered traffic for STA2 (e.g., in the S80 subband) and longer duration buffered traffic for STA1 (e.g., in the P80 subband). AP may also want to transmit buffered traffic to STA3 after transmitting buffered traffic to STA2 in the S80 subband.
  AP may request STA2 and STA3 switch to the DSO subband and transmit data to STA2 initially.
  Based on the current draft, since STA3 receives a PPDU, but does not detect within the PPDU an individually addressed frame with the RA equal to the MAC address of STA3 during a timeout interval after the ICR transmitted by STA3, STA3 has to switch back to the P80.
  Hence, AP would need to perform a second ICF-ICR exchange (with STA1 and STA3) to have STA3 back on the S80 subband, yielding a higher overhead (an additional ICF with longer padding due to STA3’s switching delay and additional ICR).
Data to STA1
AP
STA3
P80
P80
S80
S80
TXOP of AP
STA1
STA2
ICF
STA2
P80
S80
ICR
STA1
P80
S80
BA
Data to STA2
Data to STA3
BA
BA
STA1
STA3
ICF
ICR
ICR
Data to STA1
BA
STA3 has to switch back to P80
timeout
STA3
ICR
ICR
timeout
STA2 remains on S80

## Slide 6: Proposed Approach
AP behavior: A DSO AP should be allowed not to serve a DSO non-AP STA on the DSO subband for every frame exchange in the same TXOP.
STA behavior: A DSO non-AP STA that has switched to the DSO subband does not switch back to the primary subband until it is served by the AP (i.e., it had UL/DL communications with the AP).
  Option-1: The DSO non-AP STA does not switch back to the primary subband after transmitting the ICR frame. Then the current switching back rules apply after the ICR frame.
  Option-2: The DSO AP disables the switching back rules for the DSO non-AP STAs. DSO non-AP STAs switch back before the end of the TXOP (similar to the rules for switching back to the BSS primary channel in the NPCA operation).
ICR
Data to STA1
AP
STA3
P80
P80
S80
S80
TXOP of AP
STA1
STA2
STA3
ICR
STA2
P80
S80
ICR
STA1
P80
S80
BA
BA
Data to STA2
Data to STA3
Data to STA1
ICF
BA
BA
switching back
switching back
(Option-1)
(Option-1)
timeout
timeout
(Only Option-1 is demonstrated)

## Slide 7: Conclusion
In this contribution, we considered a scenario, where a DSO AP may need to transmit data to a DSO non-AP STA later during the TXOP, without having the DSO non-AP STA switching back to the primary subband.
  According to TGbn D1.0, a DSO non-AP STA has to switch back to the primary subband if the STA does not receive a frame addressed to itself after the ICF-ICR exchange.
As the general approach to solve this problem, we explained how:
  the AP behavior and the STA behavior need to be modified, including the rules for switching back to the primary subband for DSO non-AP STAs.
With simple modifications to the current draft, the proposed approach can be achieved yielding the DSO operation more efficient.

## Slide 8: References
[1] 24/1587r2, Discussion on DSO Operation