## Slide 1: Initial Thought on AMP S1G Channelization
Date: 2025-07-28
Authors:
Name | Affiliation | Address | Email
Panpan Li | Huawei | Singapore | lipanpan25@huawei.com
Lei Huang |  |  | 
Lumin Liu |  |  | 
Bin Qian |  | Shenzhen, China | 

## Slide 2: Abstract
In this document we propose the transmission bandwidths and channelization for AMP S1G
  Transmission bandwidths (BW) refer to the channel widths (or BW modes) for which the AMP S1G PHY should provide support
    Reflected in draft PHY subclause
  Channelization refer to the process of breaking down the available spectrum in different regions into “channels”
    Reflected in draft Annex E

## Slide 3: Recap: Channelization of 11ah (1/2)
[1-5] summarized the discussion and decisions on channelization in 11ah
  Transmission bandwidth
    1,2 MHz (Mandatory)
    4, 8 and 16 MHz (Optional)
  Channelization
    S1G Operating classes are given in Table E-5 in P802.11-REVme/D7.0
However, 11ah channelization result in ~mW max allowable Tx Power according to corresponding regulations.
Notes: Channel number不分国别，operating channel , not operating class

## Slide 4: AMP-S1G Considerations
According to [6]:
  to achieve 5m coverage in sub-1GHz, AP Tx power need to achieve 20-36dBm
The BW and channelization in 11ah cannot satisfy the Tx power requirement for AMP-S1G.
AMP-S1G need to seek different BW and channelization from 11ah.
Note that RFID regulations allow relatively high max allowable Tx power, while narrower BW.
Thus, this contribution will discuss the transmission BW and channelization for AMP-S1G based on RFID regulations.

## Slide 5: US S1G Regulation: FCC 15.247 [7]
FH systems shall have,
  From 15.247 (a)(1)(i) The maximum allowed 20 dB bandwidth of the hopping channel is 500 kHz
  From 15.247 (b)(2) The max output power shall be 1 watt for systems with at least 50 hopping channels. Otherwise .25 watts
Digital modulation techniques shall have,
  From 15.247 (a)(2) The minimum 6 dB bandwidth shall be at least 500 kHz
  From 15.247 (b)(3) The max output power shall be 1 watt
Most RFID devices applicable in US adopt 500kHz BW, which is a universal safety choice under different modes and regulations.

## Slide 6: China S1G Regulation: RFID [8]
Channel bandwidth (99% energy): 250kHz
Channel centre frequency
  f_c=920.125+M*0.25, M=0, 1,…, 19
Adjacent channel rejection ratio:
  First adjacent channel: -40dBr
  Second adjacent channel: -60dBr
FHSS, maximum dwell time per hopping channel: 2 seconds
TX power:
Frequency (MHz) | TX power (e.r.p)
920.50-924.5 | 2W
920-925 | 100mW

## Slide 7: EU S1G Regulation: RFID [9]
Not sure whether EU can use RFID bands for AMP use.

## Slide 8: Proposal for AMP-S1G Transmission Bandwidths
Definitely need a 250kHz
  China can use
Better have 500kHz
  US allow
Better also consider other available RFID BWs
  EU: 200kHz, 400kHz
  Encourage group to consider more regions
We propose that the following BWs be supported in the standard
  At least 250kHz
  Better have 500, 200, 400kHz

## Slide 9: Proposal for AMP-S1G Channelization (1/6)
China
  11ah has no China operating class, so follow the regulation
  Operating bands: 920-925MHz
  Support 250kHz, totally 20 channels
  Center frequency
    920.125+M*0.25, M=0,…,19
250kHz
920MHz
925MHz
……

## Slide 10: Proposal for AMP-S1G Channelization (2/6)
US
  902-928MHz: support 500kHz, 52 channels
    Support of 250kHz is open for discussion
  Center frequency:
    902.25+N*0.5, N=0,…,51
Option 1
902MHz
928MHz
AMP-S1G 500kHz
11ah: 1MHz
11ah: 2MHz
S1G Preamble
AMP-S1G portion

## Slide 11: Proposal for AMP-S1G Channelization (3/6)
US
  Consider to align the centre frequency with 11ah 1MHz channel
    Advantage: easy for implementation at AP
    Disadvantage: spectrum waste
902MHz
928MHz
Option 2
AMP-S1G 500kHz
May cannot be used as AMP-S1G channel if S1G preamble is 1MHz
11ah: 1MHz
11ah: 2MHz
S1G Preamble
AMP-S1G portion

## Slide 12: Proposal for AMP-S1G Channelization (4/6)
EU
  865-868MHz: support 200kHz, 15 channels
    Center frequency: 865.1+N*0.2, N=0,…,15;
  915.3-920.9MHz: support 400kHz, 14 channels
    Center frequency: 915.5+N*0.4, N=0,…,13;
AMP-S1G: 200kHz
865MHz
11ah: 1MHz
868MHz
11ah: 2MHz
915.3MHz
920.9MHz
AMP-S1G: 400kHz

## Slide 13: Proposal for AMP-S1G Channelization (6/6)
Change to the base standard IEEE P802.11-REVme/D7.0
  Need to develop a new AMP-S1G operating classes
    Or revise based on current Table E-5—S1G operating classes
  Need to revise current Table E-4—Global operating classes

## Slide 14: Summary
In this contribution, we present some initial thoughts on the channelization for AMP in sub-1Ghz.
  Encourage group consider more regions

## Slide 15: Reference
[1] 11-11-1238-00-00ah-channelization-and-bandwidth-modes-for-11ah
[2] 11-11-1296-03-00ah-potential-channelization-for-11ah
[3] 11-11-1329-00-00ah-motions-and-sp-on-channelization-for-11ah
[4] 11-11-1320-00-00ah-11ah-channelization-of-china
[5] 11-11-1318-00-00ah-japanese-channelization-for-802-11ah
[6] 11-25-0816-00-00bp-feasibility-study-of-mono-static-backscatter-in-sub-1-ghz
[7] 关于发布800/900MHz 频段射频识别（RFID）技术应用试行规定的通知.
[8] https://www.law.cornell.edu/cfr/text/47/15.247.
[9]https://www.etsi.org/deliver/etsi_en/302200_302299/302208/03.04.01_60/en_302208v030401p.pdf.

## Slide 16: SP 1
Do you agree to add the following text to TG bp SFD?
  11bp shall allow transmission in sub-1 GHz with at least the following bandwidths restricted by regional regulations: 250 kHz.
  Yes
  No
  Abstain

## Slide 17: SP 2
Do you agree to add the following text to TG bp SFD?
  11bp shall adopt the channelization proposal contained in slide 9 of document 11/0xxxr0 for China
  Yes
  No
  Abstain