## Slide 1: Initial Thought on AMP-S1G PHY design
Date: 2025-07-28
Authors:
Name | Affiliation | Address | Email
Panpan Li | Huawei | Singapore | lipanpan25@huawei.com
Lei Huang |  |  | 
Lumin Liu |  |  | 
Bin Qian |  | Shenzhen, China | 

## Slide 2: Introduction
Motion #73:
  11bp defines at least one mode of MAC/PHY that supports mono-static backscattering communication in sub-1 GHz
Consider the standards progress, we recommend to consider only mono-static backscatter in sub-1Ghz for now, while ignoring bi-static backscatter and active transmitter.
[1] investigated the feasibility of mono-static backscattering communication in sub-1 GHz. According to the evaluations, it is feasible to achieve 5 meter coverage with high Tx power and both RF and baseband self-jammer cancellation.
This contribution intends to trigger the discussion on the AMP PHY in the sub-1 GHz band for mono-static backscattering communication.
  The general idea is: suggest AMP-S1G PHY to reuse 2.4G PHY as much as possible

## Slide 3: Recap: AMP S1G Tag reading [1]
AMP AP
Single antenna
Leakage removal modules
  RF carrier cancellation (including directional coupler/circulator)
  Baseband leakage removal
AMP tag
Similar simple tag as 2.4G
Carrier
OOK signal
RF Harvesting & Power Management
Digital Logic
RF carrier cancellation
ADC
Directional coupler/Circulator
Tx
Rx
Tx
Rx
Baseband leakage removal

## Slide 4: Recap: 2.4G AMP Backscatter
The device requirements and assumptions such as clock accuracies, receiver types of different AMP tags in 2.4G have been discussed and compared [2-4].
UHF RFID Tag Requirements [5]
  Clock accuracy (see table 6-9 in [5])
    Frequency tolerance: 4-22%
  Data rate: adjustable with “DR” and “TRcal”
    DL: 40-160kbps
    UL 40-640kbps
  Max operating clock 2MHz
Most existing UHF RFID tags’ clock drifting are within 100k ppm [6].
Non-AP AMP STA | Backscatter STA
UL transmitter | backscattering
RF ED Rx | Yes
IF Rx | No
Energy storage | No
Clock accuracy Tx | 100k ppm
Clock accuracy Rx | 100k ppm

## Slide 5: Recap: 2.4 GHz AMP Backscatter PPDUs
AMP DL PPDU
  802.11 preamble + Excitation + AMP-Sync + AMP-Data + Excitation
    could exist repetitions of “AMP-Sync + AMP-Data + Excitation”
AMP UL PPDU
  AMP-Sync + AMP-Data
  Within Excitation field of DL PPDU
802.11 preamble | Excitation | AMP-Sync | AMP-Data | Excitation | ….
AMP-Sync | AMP-Data
DL PPDU
UL PPDU
Notes: L-STF+L_LTF+L-SIG+RL-SIG+U-SIG= 8+8+4+4+8= 32us,

## Slide 6: Proposal: AMP-S1G Tag Requirements
We believe mono-static backscatter tag in S1G will be similar with close-range backscatter tag in 2.4G and UHF RFID tags.
It would be reasonable to restrict AMP-S1G mono-static backscatter tag to have same clock requirement as 2.4G.
Tag receiver
  Supports only ED Rx
Rx sampling rate
  2MHz
Clock accuracy
  +- 10%: 100k ppm

## Slide 7: Proposal: AMP-S1G Backscatter PPDUs
Excitation | AMP-Sync | AMP-Data | Excitation | ….
AMP-Sync | AMP-Data
DL PPDU
UL PPDU
AMP-S1G DL PPDU
  (S1G preamble) + Excitation + AMP-Sync + AMP-Data + Excitation
  For regions without 11ah, without S1G preamble
  for regions where 11ah is applicable and 11ah use overlapping bands with AMP-S1G, S1G preamble may be needed to provide coexistence with 11ah devices. Thus, this S1G preamble can be changed based on the S1G preamble of 11ah
  could exist repetitions of “AMP-Sync + AMP-Data + Excitation”
  In the two possible AMP-S1G DL PPDUs, the duration of Excitation may be different
AMP-S1G UL PPDU
  AMP-Sync + AMP-Data
  Within Excitation field of DL PPDU
S1G Preamble
Excitation | AMP-Sync | AMP-Data | Excitation | ….
Notes: STF+LTF+SIG=40*(4+4+6)=40*14=560us，

## Slide 8: S1G Preamble Considerations
Group need to first decide whether S1G preamble is needed for those regions where 11ah is applicable.
  Reasons for supporting S1G preamble
    for fair coexistence with 11ah
  Reasons for against S1G preamble
    Higher complexity at AP
    Low probability of 11ah and AMP-S1G devices in same space
11ah provide mandatory support for both 1MHz and 2MHz BW.
Thus, S1G Preamble of AMP-S1G DL PPDU can be either S1G_SHORT preamble (with 2MHz) or S1G_1M preamble
Consider that AMP-S1G BW is likely <=500kHz, S1G_1M preamble is preferred to avoid spectrum waste.
Choice of S1G Preamble may also affect the channelization scheme design.

## Slide 9: Proposal: Modulation, Coding, Base Waveform
Modulation, Coding
  Suggest to keep consistent with AMP 2.4G
  Modulation: OOK
  Coding: Manchester
Base waveform
  OFDM waveforms are more suitable for wideband system.
  Since AMP-S1G reuse RFID bands, an intuitive choice is to keep consistent with RFID and use CW. CW has advantages
    Easier to satisfy regulation masks
    Friendly to Rx filter
    Naturally has frequency shifting
    Both RF and baseband self-jammer cancellation are easier to implement on CW compared to wideband signal

## Slide 10: Data Rates for AMP-S1G PPDUs
Take China as example, RFID bands is the only option for AMP-S1G.
  Max channel BW: 250kHz
Data rates are limited by BW, instead of device capability.
  Take Manchester encoding as example, the theoretical maximum data rate will be 62.5 kbps for bandwidth being 250 kHz
  Choose another lower data rate (31.25 kbps) for ease of implementation
  Choose another higher data rate (125kbps) for other regions allowing 500kHz BW
Proposed data rates
  31.25 kbps
  62.5 kbps
  125 kbps (optional)
For specific aera, maybe only 1 or 2 data rates are applicable.
The indication of data rates is TBD.

## Slide 11: Summary
In this contribution, we presented preliminary thoughts on AMP PHY in the sub-1 GHz band for mono-static backscattering communication.
  Device requirements and assumptions of AMP-S1G mono-static backscattering AMP tags
    Tag receiver: supports only ED Rx
    Max operating clock: 2MHz
    Clock accuracy: +- 10%: 100k ppm
  AMP-S1G DL PPDU and AMP-S1G UL PPDU
  Modulation, coding: Manchester OOK
  Waveform: CW
  Data rates: 31.25kbps, 62.5kbps, 125kbps

## Slide 12: Reference
[1] 11-25-0816-00-00bp-feasibility-study-of-mono-static-backscatter-in-sub-1-ghz
[2] 11-24-1475-02-00bp-discussion-on-ultra-low-power-timing-clock
[3] 11-24-1237-00-00bp-amp-tag-sta-requirements-for-close-range-backscattering
[4] 11-25-0816-00-00bp-feasibility-study-of-mono-static-backscatter-in-sub-1-ghz
[5] https://ref.gs1.org/standards/gen2/3.0.0/Gen2v3_conformance_requirements_i3.0_r-2024-06-24
[6] https://tns.thss.tsinghua.edu.cn/sun/publications/2017.1.pdf

## Slide 13: SP 1
Do you agree to add the following text to TG bp SFD?
  For mono-static backscattering communication in sub-1 GHz, The maximum allowed clock inaccuracy for the backscattering tag using OOK modulation is 100,000 ppm for both receive mode and backscattering transmit mode?
  Yes
  No
  Abstain

## Slide 14: SP 2
Do you agree to add the following text to TG bp SFD?
  11bp shall specify an AMP-S1G Downlink PPDU supporting downlink transmission for backscattering AMP STA in sub-1 GHz.
  AMP-S1G Downlink PPDU contains at least an Excitation field, an AMP-Sync field and an AMP-Data field.
    Inclusion of an AMP-SIG field is TBD.
    Inclusion of an 802.11 preamble is TBD.
    Additionally, there will be one or more Excitation fields
    Additionally, there may be more than one AMP-Data field
      Additionally, AMP-Sync and AMP-SIG field may precede each AMP-Data field
  Yes
  No
  Abstain

## Slide 15: SP 3
Do you agree to add the following text to TG bp SFD?
  11bp shall specify an AMP-S1G Uplink PPDU supporting uplink transmission for backscattering AMP STA in sub-1 GHz.
  AMP-S1G Uplink PPDU contains an AMP-Sync field and AMP-Data field. Inclusion of an AMP-SIG field in the AMP uplink PPDU is TBD.
  Yes
  No
  Abstain

## Slide 16: SP 4
Do you agree to add the following text to TG bp SFD?
  The AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU AMP-Data field will use Manchester encoding for backscattering operation.
  Yes
  No
  Abstain

## Slide 17: SP 5
Do you agree to add the following text to TG bp SFD?
  The AMP-Sync field and the AMP-Data field of AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU for backscatter communication use OOK modulation.
  Yes
  No
  Abstain

## Slide 18: SP 6
Do you agree to add the following text to TG bp SFD?
  The AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU shall support the following data rates:
    31.25 kbps (Mandatory)
    62.5 kb/s
    125 kb/s
  Yes
  No
  Abstain

## Slide 19: SP 7
Do you agree to add the following text to TG bp SFD?
  The SYNC, Data field and Excitation field of 11bp AMP-S1G Downlink PPDU and AMP-S1G Uplink PPDU use continuous wave (CW) as base carrier waveform for OOK modulated AMP communication?
  Yes
  No
  Abstain